26.14.13 Editors - Properties Editor - Object Data Properties Tab - Light Object

Preview panel

Provides a preview window for the light.

Light panel

The light panel contains the settings for the different light types. Color, strength, and so on.
The content differs, depend and of the chosen renderer. Workbench has no settings here. So we just cover the panel content with Eevee and Cycles.
Some props can be animated by setting a keyframe with the Animate Property button behind.

## Point Light EEVEE
The light emits from a point, and has falloff.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Power of the light in Watts. Higher values increase the intensity of the light. Negative values can be set, but should be avoided for predictable and physically based result.
### Soft Falloff
Apply falloff to avoid sharp edges when the light geometry intersects with other objects.
### Radius
When larger than zero, light will be emitted from a spherical surfaces with the specified radius. Lights with larger size have softer shadows and specular highlights.
### Shadow
Allows the light source to cast shadows in the scene.
#### Jitter
Enables jittered soft shadows to increase the precision of shadows. This option is disabled in the viewport unless it is also enabled in the render settings.
Note: Enabling this can have a significant performance impact.
##### Overblur
Applies shadow tracing to each jittered sample to reduce under-sampling artifacts. The default setting is 10%, which helps mitigate shadow noise and improve shadow quality.
#### Filter
Blurs the aliasing in shadows, creating smoother transitions and reducing the harsh edges of shadows.
#### Resolution Limit
Sets the minimum size of a shadow map pixel. Higher values use less memory but at the cost of reduced shadow quality. This setting helps manage performance versus quality in shadow rendering.
### Influence
Slider properties that define how much the light affects certain elements, including diffuse, glossy, transmission and volume scattering. Useful for Non-Photo-Real (NPR) rendering.
#### Diffuse
Diffuse reflection multiplier.
#### Specular
Specular light intensity multiplier.
#### Transmission
Transmission or subsurface scattering light multiplier.
#### Volume Scatter
Volume Light multiplier within volumetric materials.
### Custom Distance
Eevee Renderer. If enabled uses Distance as the custom attenuation distance instead of global light threshold. In order to avoid long setup times, this distance is first computed automatically based on a light threshold. The distance is computed at the light origin and using the inverse square falloff.
#### Distance
The distance where light influence will be set to 0.

## Point Light Cycles
The light emits from a point, and has falloff.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Power of the light in Watts. Higher values increase the intensity of the light. Negative values can be set, but should be avoided for predictable and physically based result.
### Soft Falloff
Apply falloff to avoid sharp edges when the light geometry intersects with other objects.
### Radius
When larger than zero, light will be emitted from a spherical surfaces with the specified radius. Lights with larger size have softer shadows and specular highlights.
### Max Bounces
Cycles only. Maximum number of times light from the light is allowed to bounce. Limited by scene-wide bounce settings.
### Cast Shadow
Light casts shadow.
### Multiple Importance
Multiple importance sampling reduces noise for area lights and sharp glossy materials.
### Shadow Caustics
Enables the generation of approximate caustics in the shadows of refractive surfaces. Requires that lights, caster objects, and receiver objects have the shadow caustics option activated. This feature enhances the realism of light interaction with transparent materials by simulating caustic patterns in shadows.

## Sun Light Eeevee
The light has no falloff, and goes into one direction.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Strength
Strength of the light in Watts per square meter.
### Diffuse
Diffuse Reflection multiplier.
### Specular
Specular Light intensity multiplier.
### Volume
Volume Light multiplier.
### Angle
The size of the sun light according to its angular diameter as seen from earth.

## Sun Light Eeevee Next
The light has no falloff, and goes into one direction.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Strength
Strength of the light in Watts per square meter.
### Diffuse
Diffuse Reflection multiplier.
### Specular
Specular Light intensity multiplier.
### Volume
Volume Light multiplier.
### Angle
The size of the sun light according to its angular diameter as seen from earth.
### Cast Shadow
Light source casts shadow.
### Shadow Softness
Scale light shape for softer shadows.
### Filtering Radius
Blur shadow aliasing.
### Trace Distance
The maximum distance a shadow ray can travel.

## Sun Light Cycles
The light has no falloff, and goes into one direction.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Strength
Strength of the light in Watts per square meter.
### Angle
The size of the sun light according to its angular diameter as seen from earth.
### Max Bounces
Cycles renderer. Maximum number of times light from the light is allowed to bounce. Limited by scene-wide bounce settings.
### Cast Shadow
Light casts shadow.
### Multiple Importance
Multiple importance sampling reduces noise for area lights and sharp glossy materials.
### Shadow Caustics
Generate apporximate caustics in shadows of refractive surfaces. Lights, Caster and receiver objects must have shadow caustics option set to enabled to get this to work.

## Spot Light Eevee
The light has falloff. And gets distributed in a cone shape.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Strength of the light in Watts per square meter.
### Diffuse
Diffuse Reflection multiplier.
### Specular
Specular Light intensity multiplier.
### Volume
Volume Light multiplier.
### Soft Falloff
Apply falloff to avoid sharp edges when the light geometry intersects with other objects.
### Radius
When larger than zero, light will be emitted from a spherical surfaces with the specified radius. Lights with larger size have softer shadows and specular highlights.
### Custom Distance
Eevee Renderer. If enabled uses Distance as the custom attenuation distance instead of global light threshold. In order to avoid long setup times, this distance is first computed automatically based on a light threshold. The distance is computed at the light origin and using the inverse square falloff.
#### Distance
The distance where light influence will be set to 0.
### Spot shape
Eevee renderer.
#### Size
The size of the outer cone of a spot.
#### Blend
Blending to the inner cone of a spot. The inner cone boundary line indicates the point at which light from the Spot will start to blur/soften.
#### Show cone
Shows the cone opaque in the 3D view

## Spot Light Eevee Next
The light has falloff. And gets distributed in a cone shape.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Strength of the light in Watts per square meter.
### Diffuse
Diffuse Reflection multiplier.
### Specular
Specular Light intensity multiplier.
### Volume
Volume Light multiplier.
### Soft Falloff
Apply falloff to avoid sharp edges when the light geometry intersects with other objects.
### Radius
When larger than zero, light will be emitted from a spherical surfaces with the specified radius. Lights with larger size have softer shadows and specular highlights.
### Cast Shadow
Light source casts shadow.
### Shadow Softness
Scale light shape for softer shadows.
### Filtering Radius
Blur shadow aliasing.
### Custom Distance
Eevee Renderer. If enabled uses Distance as the custom attenuation distance instead of global light threshold. In order to avoid long setup times, this distance is first computed automatically based on a light threshold. The distance is computed at the light origin and using the inverse square falloff.
#### Distance
The distance where light influence will be set to 0.
### Spot shape
Eevee renderer.
#### Size
The size of the outer cone of a spot.
#### Blend
Blending to the inner cone of a spot. The inner cone boundary line indicates the point at which light from the Spot will start to blur/soften.
#### Show cone
Shows the cone opaque in the 3D view

## Spot Light Cycles
The light has falloff. And gets distributed in a cone shape.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Strength of the light in Watts per square meter.
### Soft Falloff
Apply falloff to avoid sharp edges when the light geometry intersects with other objects.
### Radius
When larger than zero, light will be emitted from a spherical surfaces with the specified radius. Lights with larger size have softer shadows and specular highlights.
### Max Bounces
Maximum number of times light from the light is allowed to bounce. Limited by scene-wide bounce settings.
### Cast Shadow
Light casts shadow.
### Multiple Importance
Multiple importance sampling reduces noise for area lights and sharp glossy materials.
### Beam shape
Eevee renderer.
#### Size
The size of the outer cone of a spot.
#### Blend
Blending to the inner cone of a spot. The inner cone boundary line indicates the point at which light from the Spot will start to blur/soften.
#### Show cone
Shows the cone opaque in the 3D view

### Shadow Caustics
Generate apporximate caustics in shadows of refractive surfaces. Lights, Caster and receiver objects must have shadow caustics option set to enabled to get this to work.

## Area Light Eevee
The light emits from a surface, and has falloff.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Power of the light in Watts. Higher values increase the intensity of the light. Negative values can be set, but should be avoided for predictable and physically based result.
### Diffuse
Diffuse Reflection multiplier.
### Specular
Specular Light intensity multiplier.
### Volume
Volume Light multiplier.
### Shape
The shape of the light emitting surface.
### Size
The size of the light emitting surface.
### Custom Distance
Eevee Renderer. If enabled uses Distance as the custom attenuation distance instead of global light threshold. In order to avoid long setup times, this distance is first computed automatically based on a light threshold. The distance is computed at the light origin and using the inverse square falloff.
#### Distance
The distance where light influence will be set to 0.

## Area Light Eevee Next
The light emits from a surface, and has falloff.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Power of the light in Watts. Higher values increase the intensity of the light. Negative values can be set, but should be avoided for predictable and physically based result.
### Diffuse
Diffuse Reflection multiplier.
### Specular
Specular Light intensity multiplier.
### Volume
Volume Light multiplier.
### Shape
The shape of the light emitting surface.
### Size
The size of the light emitting surface.
### Cast Shadow
Light source casts shadow.
### Shadow Softness
Scale light shape for softer shadows.
### Filtering Radius
Blur shadow aliasing.
### Custom Distance
Eevee Renderer. If enabled uses Distance as the custom attenuation distance instead of global light threshold. In order to avoid long setup times, this distance is first computed automatically based on a light threshold. The distance is computed at the light origin and using the inverse square falloff.
#### Distance
The distance where light influence will be set to 0.

## Area Light Cycles
The light emits from a surface, and has falloff.
### Color
The color of the light. Clicking at the color field will open a color picker.
### Power
Power of the light in Watts. Higher values increase the intensity of the light. Negative values can be set, but should be avoided for predictable and physically based result.
### Shape
The shape of the light emitting surface.
### Size
The size of the light emitting surface.
### Max Bounces
Cycles renderer. Maximum number of times light from the light is allowed to bounce. Limited by scene-wide bounce settings.
### Custom Distance
Eevee Renderer. If enabled uses Distance as the custom attenuation distance instead of global light threshold. In order to avoid long setup times, this distance is first computed automatically based on a light threshold. The distance is computed at the light origin and using the inverse square falloff.
#### Distance
The distance where light influence will be set to 0.
### Cast Shadow
Cycles renderer. The light source casts a shadow.
### Multiple Importance
Cycles renderer. By default lights use only direct light sampling. Which can be noisy with sharp glossy reflections. Multiple Importance activates Indirect light sampling to reduce noise.
### Shadow Caustics
Generate apporximate caustics in shadows of refractive surfaces. Lights, Caster and receiver objects must have shadow caustics option set to enabled to get this to work.

### Portal
With Cycles Area lights can also function as light portals to help sample the environment light. This can significantly reduce noise in interior scenes. Light portals are not helpful for outdoor scenes. Since outdoor the light bounces just fly off into the sky.
Using the light as portal hides it.
### Beam Shape Subpanel
#### Spread
How widely the emitted light fans out.

Spot Shape Panel

## Size
The size of the outer cone of a spot.

## Blend
Blending to the inner cone of a spot. The inner cone boundary line indicates the point at which light from the Spot will start to blur/soften.
## Show cone
Shows the cone opaque in the 3D view.

Nodes Panel

## Use Nodes
Use nodes for the light setup. Creates the standard nodes for an emission light. Which can be found in the Node editor then. Once activated the Nodes panel shows the content of the emission node.
To revert, and not to use nodes, untick the Use Nodes checkbox in the node editor.

Animation Panel

## Light
### New
Create a new action clip for the light, used in the Dopesheet Editor - Action Clip mode.
### Action Selector
This selector allows users to manage actions associated with a light source, ensuring that the correct animation data is applied.
Add: Make a copy of the current action, including all animation data.
Remove: Delete the selected action, removing it from the light source.
Fake User: Assigns a "fake user" to the action, preventing it from being automatically deleted when it is no longer in use.
### Slot Selector
Slots are used to organize distinct animation data within an action across multiple objects, lights or elements. The Slot Selector provides an interface to manage these slots, allowing for efficient duplication and removal as needed. Each object contains their own slot.
Duplicate: Make a copy of the current slot.
Remove: Delete the selected slot, removing it from the light source.

Custom Properties Panel

Here you can define custom properties that can be used for scripting.

Here you might also find custom properties from addons or scripts.

## Add
Adds a new property.

## Edit
Opens a panel where you can adjust the settings for the custom property.

## Remove
Removes the property.