12.1.46 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities - Math

Detailed table of content

Add menu - Utilities - Math

Utility nodes are mainly for mathematical operations.

## Bit Math
Performs a bit math operation between its inputs.
### Inputs
The inputs depends of the chosen method.
### Properties
#### Operation
##### And
Returns a value where the bits of A and B are both set.
##### Or
Returns a value where the bits of either A or B are set.
##### Exclusive Or
Returns a value where only one bit of A and B is set.
##### Not
Returns the opposite bit value of A, in decimal it is equivalent of A = -A -1
##### Shift
Shifts the bit values of A by the specified Shift amount. Positive values shift left, negative values shift right.
##### Rotate
Rotates the bit values of A by the specified Shift amount. Positive values rotates left, negative values rotates right.
### Output
#### Boolean
Standard Boolean output.

## Boolean Math
The Boolean Math node performs a basic logical operation between its inputs.
### Inputs
#### Boolean
Two standard Boolean inputs.
### Properties
#### Operation
##### And
True if both inputs are true.
##### Or
True if either or both inputs are true.
##### Not
True if both inputs are false.
##### Not And (NAND)
True when at least one input is false.
##### Nor (NOR)
True when both inputs are false.
##### Equal (XNOR)
True when both inputs are equal.
##### Not Equal (XOR)
True when both inputs are different.
##### Imply (IMPLY)
True unless the first input is true and the second is false.
##### Subtract (NIMPLY)
True when the first input is true and the second is false.
### Output
#### Boolean
Standard Boolean output.

## Integer Math
The Boolean Math node provides mathematical operations with integers.
### Inputs
#### Value
Two standard value inputs.
### Properties
#### Functions
The available mathematical functions to manipulate the input integers.

### Output
#### Value
The value output.

## Clamp
Clamps a value between a minimum and a maximum.
### Inputs
#### Value
The input value to be clamped.
#### Min
The minimum value.
#### Max
The maximum value.
### Properties
#### Clamp Type
##### Min Max
Clamp values using Min and Max values.
##### Range
Clamp values between Min and Max range.
### Outputs
#### Result
The input value after clamping.

## Compare
The Compare node takes two inputs and does a math comparison between them.
### Inputs
#### A, B
Standard float value input.
### Properties

#### Input Type
What kind of data to compare.

#### Operation
##### A is less than B
True if A is smaller than B.
##### A is lesser than or equal B
True if A is smaller or equal than B.
##### A is greater than B
True if A is bigger than B.
##### A is greater than or equal B
True if A is bigger or equal than B.
##### A is equal B
True if A and B are the same.
##### A is not equal B
True if A and B are different.
### Output
#### Result
Standard Boolean output.

## Float Curve
The Float Curve node maps an input float to a curve and outputs a float value. This curve can then be used for profiles for example.
### Inputs
#### Factor
How strong the input influences the output value.
#### Attribute
The input value.

### Properties
#### Curve Field
##### Channel buttons
Clicking on one of the channels displays the curve for each.
C (Combined RGB), R (Red), G (Green), B (Blue).

##### Navigation elements
They are described from left to right.
###### Zoom in and out
The two buttons with the magnifying glass at it zooms in and out in the curve window.

###### Use Clipping
Clipping options. Set up clipping for the stroke.

###### Tools
Tools is a menu where you can find some curve related tools.
###### Reset View
Resets the curve windows zoom.
###### Extend horizontal
Extends the curve before the first curve point and behind the last curve point horizontally.
###### Extend extrapolated
Extends the curve before the first curve point and behind the last curve point extrapolated.
###### Reset Curve
Resets the curve to the initial shape.

##### Curve edit field
Create and tweak a Bezier curve that varies the input levels (X axis) to produce an output level (Y axis).
###### Selecting Points
You can select curve points. This reveals two edit boxes for the x and y coordinate of this point.
Selected points can be moved around. Left click at them, hold the mouse button down and move them to a new location.
###### Adding Points
You can add new curve points by simply left clicking at the curve. Move the mouse to position them where you need it.

###### Curve point settings
When you have a point selected then you will reveal further settings at the bottom.
###### Vector Handle
Set handle type to Vector.
###### Auto Handle
Set handle type to Auto.
###### Auto Clamped Handle
Set handle type to Auto Clamped.

### Output
#### Value
The output value.

## Float to Integer
Converts a floating point value into an integer value.
### Inputs
#### Float
The input float value.
### Properties
#### Rounding Mode
How the float value should be converted.
### Outputs
#### Integer
The output integer value.

## Hash Value
The hash value converts a value input into a hashed value.
Note that Hashes cannot be relied upon to be used as unique identifiers because they are not guaranteed to be unique. It can be used to generate somewhat stable randomness especially in cases where White Noise does not offer enough flexibility.
### Input
#### Value
The input value.
#### Seed
A seed to randomize the value.
### Properties
#### Data Type
What data type to create.

### Output
#### Hash
The hash value output.

## Map Range
This node converts (maps) an input value range into a destination range. By default, values outside the specified input range will be proportionally mapped as well. This node is similar to Map Value node but provides a more intuitive way to specify the desired output range.
### Inputs
#### Value
Standard value input.
#### From Min
Start of the input value range.
#### From Max
End of the input value range.
#### To Min
Startof the destination range.
#### To Max
End of the destination range.
### Properties
#### Data Type
The data type to calculate.

#### Interpolation Type
how to interpolate the values between min and max.
#### Clamp
Clamps values to Min/Max of the destination range.
### Outputs
#### Value
Standard value output.

## Math
The Math Node performs math operations.
### Inputs
The inputs of the node are dynamic. Some inputs are only available with certain operations. For example, the Addend input is only available in the Multiply Add operator.
#### Value
Input Value. Trigonometric functions read this value as radians.
#### Addend
Input Addend.
#### Base
Input Base.
#### Exponent
Input Exponent.
#### Epsilon
Input Epsilon.
#### Distance
Input Distance.
#### Min
Input Minimum.
#### Max
Input Maximum.
#### Increment
Input Increment.
#### Scale
Input Scale.
#### Degrees
Input Degrees.
#### Radians
Input Radians.
### Properties
#### Operation
The mathematical operator to be applied to the input values:

##### Functions
###### Add
The sum of the two values.
###### Subtract
The difference between the two values.
###### Multiply
The product of the two values.
###### Divide
The division of the first value by the second value.
###### Multiply Add
The sum of the product of the two values with Addend.
##### Power
The Base raised to the power of Exponent.
###### Logarithm
The log of the value with a Base as its base.
###### Square Root
The square root of the value.
###### Inverse Square Root
One divided by the square root of the value.
###### Absolute
The input value is read with without regard to its sign. This turns negative values into positive values.
###### Exponent
Raises Euler’s number to the power of the value.
##### Comparison
###### Minimum
Outputs the smallest of the input values.
###### Maximum
Outputs the largest of two input values.
###### Less Than
Outputs 1.0 if the first value is smaller than the second value. Otherwise the output is 0.0.
###### Greater Than
Outputs 1.0 if the first value is larger than the second value. Otherwise the output is 0.0.
###### Sign
Extracts the sign of the input value. All positive numbers will output 1.0. All negative numbers will output -1.0. And 0.0 will output 0.0.
###### Compare
Outputs 1.0 if the difference between the two input values is less than or equal to Epsilon.
###### Smooth Minimum
Smooth Minimum.
###### Smooth Maximum
Smooth Maximum.
##### Rounding
###### Round
Round the input value to the nearest integer.
###### Floor
Rounds the input value down to the nearest integer.
###### Ceil
Rounds the input value up to the nearest integer.
###### Truncate
Outputs the integer part of the value.
###### Fraction
Fraction.
###### Modulo
Outputs the remainder once the first value is divided by the second value.
###### Wrap
Outputs a value between Min and Max based on the absolute difference between the input value and the nearest integer multiple of Max less than the value.
###### Snap
Round the input value to down to the nearest integer multiple of Increment.
###### Ping-pong
The output value is moved between 0.0 and the Scale based on the input value.
##### Trigonometric
###### Sine
The Sine of the input value.
###### Cosine
The Cosine of the input value.
###### Tangent
The Tangent of the input value.
###### Arcsine
The Arcsine of the input value.
###### Arccosine
The Arccosine of the input value.
###### Arctangent
The Arctangent of the input value.
###### Arctan2
Outputs the Inverse Tangent of the first value divided by the second value measured in radians.
###### Hyperbolic Sine
The Hyperbolic Sine of the input value.
###### Hyperbolic Cosine
The Hyperbolic Cosine of the input value.
###### Hyperbolic Tangent
The Hyperbolic Tangent of the input value.
##### Conversion
###### To Radians
Converts the input from degrees to radians.
###### To Degrees
Converts the input from radians to degrees.
###### Clamp
Limits the output to the range (0.0 to 1.0). See Clamp.
### Outputs
#### Value
Numerical value output.

###### Use Clipping
Clipping options. Set up clipping for the stroke.
###### Delete Points
Deletes selected curve point.

###### Curve window
Tweak and adjust the falloff curve by clicking at a curve point and dragging it around.
Double click adds a new point.
Holding down ctrl activates temporary snapping.
Holding down shift enables slower movement, which allows more accurate setting.
###### X / Y values
The x and y value of the currently selected point.

## Mix
Allows to mix values and vectors in various ways. The node has three different modes. Float, Vector and Color. This node covers the Float mode

### Input
#### Float
##### Factor
The mix factor.
##### A
Float value A input.
##### B
Float value B input.
### Properties
###### Clamp Factor
Clamp the factor to 0-1 range.
### Output
#### Result
The output value or vector.