Tool Shelf - Grease Pencil - Edit Mode

Here you can find tools to edit the curve geometry of the grease pencil strokes.

## Tweak, Select, Transform, 3D Cursor Measure and Annotate tools

The tweak, select, transform, 3d cursor, measure and annotate tools at the end of the list are explained in the chapter 7.1.1 Editors - 3D View - Tool Shelf - Object Mode. We won't cover this tools again here.

## Extrude
Extrude out selected curve points.
### Snapping
Holding down Ctrl activates temporary global snapping.
### Precision movement
When you hold down shift, then you will have a much slower but also much preciser movement.
### Header Values
When you move the mouse then you will see some values in the header, which defines the current position of the object.
The value m stands for the default metric system. Meters. You can change the units in the Properties editor in the Scene properties in the Units panel. When you choose kilometers here then you will see a km instead m.
The value D stands for the distance of the current selected axis. This can also be two axis. Then you have two d values. The value in the brackets is then the direct distance to the starting point.
These values are always relative to the starting point. You always start with zero, regardless of the real world position.
### Move without Widget
You don't have to use the widget to move the object. You can also click aside of it, and drag the object around. The mouse turns into a move cursor. The standard behaviour then is to move in screen space. When you want to move into a specific axis, then press X or Y or Z to limit the movement to this axis.

### Limit Axis
When you want to move along a specific axis, then press X or Y or Z to limit the movement to this axis. You usually start in global orientation. But you can change this in the Orientation settings.
By holding down the mouse button and pressing the X, Y or Z key twice you can toggle this to local. But also to other orientations. This depends in what orientation you start. With normal you can toggle that way between Normal and Global.

#### Tool Settings
##### Axis Type
You can choose between the regular axis type. That's the yellow widget with just one handler. It always points in the direction of the middled normals of the selection.
Or you can use the XYZ axis type. That's a handler with three axis. This widget can be aligned with the transform orientation methods.

#### Last Operator Extrude Stroke Points
##### Move X, Y Z
The position. Attention, the actual world orientation and rotation does not matter here. It always starts with a value of zero, and moves relative to this zero then. For the actual location values have a look in the sidebar in the transform panel.
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Radius
Increases the thickness of the stroke for the selected curve points.
### Snapping
Holding down Ctrl activates temporary global snapping.
### Precision movement
When you hold down shift, then you will have a much slower but also much preciser movement.
### Header Values
When you move the mouse then you will see some values in the header, which shows the current scale factor. This value is relative to the starting value, which always starts with 1.
#### Last Operator Transform
##### Transform X, Y Z
The scale factor. Actually just the Value X does really matter. The other values have no effect.
##### Axis
Here you can define an axis to scale. But this setting has no effect.
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Bend
Bends the selection.
### Snapping
Holding down Ctrl activates temporary global snapping.
### Precision movement
When you hold down shift, then you will have a much slower but also much preciser movement.
### Header Values
When you move the mouse then you will see some values in the header, which shows the current scale factor. This value is relative to the starting value, which always starts with 1.

## Shear / To Sphere Tools group
### Shear
#### Snapping
Holding down Ctrl activates temporary global snapping.
#### Precision movement
When you hold down shift, then you will have a much slower but also much preciser movement.
#### Header Values
When you move the mouse then you will see some values in the header, which shows the current scale factor. This value is relative to the starting value, which always starts with 1.
#### Hotkeys
As shown in the header, you can press X or Y to set the shear axis.
#### Last Operator Shear
##### Offset
The shear offset. This value always starts at zero.
##### Axis
Here you can define the first axis for the shear transformation.
##### Axis Ortho
Here you can define the second axis for the shear transformation
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

### To Sphere
Transforms the selection into a sphere shape.
#### Snapping
Holding down Ctrl activates temporary global snapping.
#### Precision movement
When you hold down shift, then you will have a much slower but also much preciser movement.
#### Header Values
When you move the mouse then you will see some values in the header, which shows the current to sphere factor. This value is relative to the starting value, which always starts with 0.
#### Last Operator To Sphere
##### Offset
The to sphere factor. This value is relative to the starting value, which always starts with 0.
##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.