12.1.16 Editors - Geometry Nodes Editor - Header - Add Menu - Vector

Detailed table of content

Add menu - Vector

Vector nodes are for calculating vector operations.

## Combine XYZ
The Combine XYZ Node combines a vector from its individual components.
### Input
#### X Y and Z
X, Y and Z values.
### Output
#### Color
Color output.

## Separate XYZ
The Separate XYZ Node splits a vector into its individual components.
### Input
#### Vector
The Input vector.
### Output
#### X, Y and Z
The output vectors for X, Y and Z.

## Vector Math
The Vector Math node performs the selected math operation on the input vectors.
### Inputs
The inputs of the node are dynamic. Some inputs are only available in certain operations. For instance, the Scale input is only available in the Scale operator.
#### Vector
Input vector A.
#### Vector
Input vector B.
#### Scale
Input Scale.
### Properties
#### Operation
The vector math operator to be applied on the input vectors.

### Outputs
The output of the node is dynamic. It is either a vector or a scalar depending on the operator. For instance, the Length operator have a scalar output while the Add operator have a vector output.
#### Vector
Output vector.
#### Value
Output value.

## Vector Rotate
The Vector Rotate node allows rotations by a vector.
### Inputs
The inputs of the node are dynamic. Some inputs are only available in certain operations. For instance, the Angle input is just available with the Axis Angle type.
#### Vector
Input vector.
#### Center
Input Center
#### Axis
Input Axis.
#### Angle
Input Angle
### Properties
#### Type
The rotation type.

### Outputs
#### Vector
The Output vector.