Graph Editor - Key Menu

This menu contains functionality to manage the keyframes.

## Transform
### Grab/Move
Moves the selected keyframe(s).
#### Last Operator Move
##### Move X, Y Z
The position. Attention, the actual world orientation and rotation does not matter here. It always starts with a value of zero, and moves relative to this zero then. For the actual location values have a look in the sidebar in the transform panel.
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

### Extend
Moves the last keyframes of the selection.
#### Last Operator Transform
##### Values X, Y Z, W
The new position.
##### Axis
Which axis to transform.
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

### Rotate
Rotates the selection.
#### Last Operator Rotate
##### Angle
The rotation. Attention, the actual world orientation and rotation does not matter here. It always starts with a value of zero, and rotates relative to this zero then. For the actual rotation values have a look in the sidebar in the transform panel.
##### Axis
Which axis to rotate.
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

### Scale
Scales the selected keyframes. You need to have more than one keyframe selected.
#### Last Operator Resize
##### Angle
The rotation. Attention, the actual world orientation and rotation does not matter here. It always starts with a value of zero, and rotates relative to this zero then. For the actual rotation values have a look in the sidebar in the transform panel.
##### Axis
Which axis to rotate.
##### Orientation
The widget can have different orientations. The menu items should be self explaining.

##### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
###### Proportional Falloff
Here you can adjust the falloff methods.
###### Proportional Size
Here you can see and adjust the falloff radius.

###### Connected
The proportional falloff gets calculated for connected parts only.
###### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Snap
Snaps the selected keyframes by the chosen method.

### Last Operator Snap Keys
#### Type
Snaps the selected keyframes by the chosen method.
## Mirror
Flips the selected keyframes over the current frame position.

### Last Operator Mirror Keys
#### Type
Flips the selected keyframes over the current frame position by the chosen method.
## Insert Keyframes
Choose a method how to insert a new keyframe at the current frame position.
### Last Operator Insert Keyframes
#### Type
Choose a method how to insert a new keyframe at the current frame position.
## Jump to Keyframes
Sets the frame marker at the average position of the currently selected keyframes.
## Copy Keyframes
Copy selected keyframes.
## Paste Keyframes
Pastes copied keyframes.
## Paste Flipped
Pastes copied keyframes, but flipped.
### Last Operator Paste Keyframes / Flipped

#### Offset
Define a offset for the paste position.

#### Type
Choose a method how to paste the copied keyframes.
#### Flipped
Pastes keyframes from mirrored bones if they exists.
## Duplicate
Duplicate selected keyframes.
### Last Operator Duplicate
#### Mode
#### Values X / Y
The x and y values for the pasted keyframes. Note that these values starts at the position of the original copied keyframe. These values are relative.
Values Z and W have no effect here.
#### Axis
These values have no effect.
#### Orientation
These values have no effect.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Delete Keyframes
Deletes selected keyframes.
## Decimate (Ratio)
Decimate F-Curves by removing keyframes that that has the least influence to the curve shape.
## Decimate (Allowed Change)
Decimate F-Curves by specifying how much it can derivate from the original curve.
### Last Operator Decimate Keyframes
#### Mode
The decimate mode. Error margin is Allowed change.
#### Remove or Max Error Margin
The percentage of keyframes to remove.
## Clean Keyframes
Simplify FCurces by deleting keyframes that are close to each other in all channels.
## Clean Channels
Simplify FCurces by deleting keyframes that are close to each other in selected channels.
### Last Operator Clean Keyframes
#### Threshold
The threshold amount for the simplify algorithm.
#### Channels
Clean keyframes or channels.
## Smooth Keys
Make selected curves less bumpy.
## Sample Keyframes
Adds keyframes at every unit between the selected keyframes.

## Bake Curve
Bake selected F-Curves to a set of sampled points. This makes the curve not longer editable.
## Discontinuity (Euler) Filter
Try to fix large jumps and flips in the selected F Curve. This jumps can appear when rotation values are clipping by baking physics.