12.1.39 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities - Field

Detailed table of content

Add menu - Utilities - Field

Field nodes.

## Accumulate Field
Creates a running total of a given Vector, Float, or Int field.
### Inputs
#### Value
The field to be accumulated.
#### Group Index
The values of this input are used to aggregate the input into separate 'bins', creating multiple accumulations.
### Properties
#### Data Type
What data type to work with.

Domain
From which domain to use the data.

### Outputs
#### Leading and Trailing
Returns the running totals starting at either the first value of each accumulations or 0 if there is no data
#### Total
Returns the total accumulation at all positions of the field.

## Evaluate at Index
This node allows accessing data of other elements in the context geometry.
It is similar to the Transfer Attribute node in Index mode. The main difference
is that this node does not require a geometry input, because the context
is used.
### Inputs
#### Index
Input Index.
#### Value
Input Value.
### Properties
#### Data Type
What data type to calculate.

#### Domain
What geometry to calculate.

### Output
#### Value
The output value.

## Evaluate on Domain
This node evaluates an existing field on a separate domain in a larger field context - an alternative to the Capture Attribute node. This nodes gets the field type of an existing field from the input socket and interpolates the field type as an array in the output socket.
### Inputs
#### Value
The input value to get the field.
### Properties
#### Data Type
Select the Data Type - which can be float, integer, vector, color and boolean.
#### Domain
The domain the Field evaluates. This gets and filters the field type. The domain can be point, edge, face, face corner, spline or instance.

### Outputs
#### Value
The output value.