12.1.11 Editors - Geometry Nodes Editor - Header - Add Menu - Geometry - Sample

Detailed table of content

Add menu - Geometry - Sample

Here you find nodes to modify the geometry.

## Geometry Proximity
This node finds the closest position on the target for each point in the input geometry.
### Inputs
#### Geometry
The target object.
#### Group ID
Is evaluated on the face domain, and splits the input mesh into multiple parts, each with its own id.
#### Sample Position
The position where the computed location is stored.
#### Sample Group ID
Determines in which group the closest nearest surface is detected.
### Properties
#### Target Geometry
The element of the target geometry to calculate the distance from.
### Outputs
#### Position
Closest location on the surface of the target mesh, or the closest point in the target point cloud in Points mode.
#### Distance
Distance from the source position to the closest location in the target.
#### Is Valid
Wether the sampling was successful. It is false when the sampled group is empty.

## Index of Nearest
Retreive values from specific geometry elements.
### Inputs
#### Position
The position of the nearest element.
#### Group ID
The group ID of the nearest element.
### Outputs
#### Index
The Index of the nearest element.
#### Has Neighbor
Has this element a neighbor.

## Raycast
This node sends a raycast and retreives data from the hit target.
### Inputs
#### Target Geometry
This is actually the source object that sends the ray.
#### Attribute
Attribute input.
#### Source Position
Source position input.
#### Ray Direction
A vector 3 for the ray direction.
#### Ray Length
The length of the ray.
### Properties
#### Data Type
What data to calculate on hit.

#### Mapping
Mapping from the target geometry to hit points. Interpolated or nearest.

### Output
#### Is Hit
Has the raycast hit something?
#### Hit Position
The hit position if any.
#### Hit Normal
The normal of the hit point.
#### Hit Distance
The distance of the hit point.
#### Attribute
The attribute of the hit object.

## Sample Index
Retreive values from specific geometry elements.
### Inputs
#### Geometry
The source object to take the data from.
#### Value
The value to retreive.
#### Index
The index position of the value.
### Properties
#### Data Type
The type for the source and result data.

#### Domain
What kind of data to process.

#### Clamp
Clamp the indices to the size of the attribute domain.
### Output
#### Value
The output value.

## Sample Nearest
Retreives the element of a geometry closest to a position.
### Inputs
#### Geometry
The source object to take the data from.
#### Sample Position
The position of the source object.
### Properties
#### Domain
What data to process.
### Output
#### Index
The index output.