26.9.10 Editors - Properties Editor - Modifiers Properties Tab - Grease Pencil - Color Modifiers

Detailed table of content

Color modifiers

Color modifiers just exists for the Grease Pencil object.

## Hue/Saturation
The Hue/Saturation Modifier applies a color transformation to the object output color.

### Mode
The color transformation will be applied on the stroke and/or the fill color.
Stroke and Fill, Stroke, Fill
### Hue
Specifies the hue rotation of the image. 360° are mapped to (0 to 1). The hue shifts of 0 (-180°) and 1 (+180°) have the same result.
### Saturation
A saturation of 0 removes hues from the image, resulting in a greyscale image. A shift greater than 1.0 increases saturation.
### Value
Value is the overall brightness of the image. De/Increasing values shift an image darker/lighter.
### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Layer Pass
The layer pass index.
##### Use Layer pass
Use the layer pass.
##### Layer pass value
The layer pass value.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Material Pass
The material pass index.
##### Use Material pass
Use the Material pass.
##### Material pass value
The Material pass value.
##### Invert
Inverts the influence.
#### Custom Curve
Use a custom curve to define the noise along the strokes.

##### Navigation elements
The navigation elements at the top are described from left to right.
###### Zoom in and out
The two buttons with the magnifying glass at it zooms in and out in the curve window.

###### Clipping
Clipping options. Set up clipping for the stroke.

###### Tools
Tools is a menu where you can find some curve related tools.
###### Reset View
Resets the curve windows zoom.
###### Extend Horizontal
Extend the curve points horizontal before the first curve point and after the last curve point.
###### Extend Vertical
Extend the curve points vertical before the first curve point and after the last curve point.
###### Reset Curve
Resets the curve to the initial shape.

#### Curve window
Tweak and adjust the falloff curve by clicking at a curve point and dragging it around.
Double click adds a new point.
Holding down ctrl activates temporary snapping.
Holding down shift enables slower movement, which allows more accurate setting.
###### Vector Handle
Set handle type to Vector.
###### Auto Handle
Set handle type to Auto.
###### Auto Clamped Handle
Set handle type to Auto Clamped.
##### X / Y
The position of the currently selected curve point.
###### Delete Points
Deletes selected curve points.

## Opacity Modifier
The Opacity Modifier change the opacity (alpha) value of the stroke points.
The alpha value in Grease Pencil is stored per-point. The modifier can alter these values to go from totally transparent points to totally opaque points.
### Mode
The color transformation will be applied to the stroke/fill color or stroke Hardness. When Hardness is selected, then the opacity affects the stroke’s transparency (alpha) from the center to the border.
Stroke and Fill, Stroke, Fill, or Hardness.

### Uniform Opacity
When enabled, makes the opacity equal for the entire strokes.
### Opacity Factor
Controls the opacity value of the stroke points. A value of 1.0 respect the original alpha value of the points, a shift less than 1.0 make the points more transparent than originally, and a shift greater than 1.0 make the points more opaque than originally.
Sets value to 2.0 makes the points alpha fully opaque.
#### Weighted
Use Weight to modulate effect.
### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Layer Pass
The layer pass index.
##### Use Layer pass
Use the layer pass.
##### Layer pass value
The layer pass value.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Material Pass
The material pass index.
##### Use Material pass
Use the Material pass.
##### Material pass value
The Material pass value.
##### Invert
Inverts the influence.
#### Custom Curve
Use a custom curve to define the noise along the strokes.

##### Navigation elements
The navigation elements at the top are described from left to right.
###### Zoom in and out
The two buttons with the magnifying glass at it zooms in and out in the curve window.

###### Clipping
Clipping options. Set up clipping for the stroke.

###### Tools
Tools is a menu where you can find some curve related tools.
###### Reset View
Resets the curve windows zoom.
###### Extend Horizontal
Extend the curve points horizontal before the first curve point and after the last curve point.
###### Extend Vertical
Extend the curve points vertical before the first curve point and after the last curve point.
###### Reset Curve
Resets the curve to the initial shape.

#### Curve window
Tweak and adjust the falloff curve by clicking at a curve point and dragging it around.
Double click adds a new point.
Holding down ctrl activates temporary snapping.
Holding down shift enables slower movement, which allows more accurate setting.
###### Vector Handle
Set handle type to Vector.
###### Auto Handle
Set handle type to Auto.
###### Auto Clamped Handle
Set handle type to Auto Clamped.
##### X / Y
The position of the currently selected curve point.
###### Delete Points
Deletes selected curve points.

## Tint Modifier
The Tint Modifier colorize the original stroke or fill with a selected color.

### Mode
The color transformation will be applied on the stroke and/or the fill color.
Stroke and Fill, Stroke, Fill
### Strength
Controls the amount for the color mixing.
A value of 0 respect the original strokes vertex color, a value of 1.0 totally replace the original color with the tint color.
A shift greater than 1.0 will make the points alpha less transparent than originally (2.0 is fully opaque).
#### Weighted
Use weight to modulate effect.
### Tint Type
#### Uniform
##### Color
Defines the tint color for mixing with the original color.

#### Gradient
##### Color Ramp
Defines the tint gradient color for mixing with the original vertex color.
##### Controls
###### +
Add a stop to your color ramp. The stop will be added after the selected one, in the middle to the next one.
###### -
Deletes the selected color stop from the list.
###### Tools menu
###### Flip Color Ramp
Flips the gradient, inverting the values of the color ramp.
###### Distribute Stops from Left
Rearrange the stops so that every step has the same space to the right.
###### Distribute Stops Evenly
Space between all neighboring stops becomes equal.
###### Eyedropper (pipette icon) E
An Eyedropper to sample a color or gradient from the interface to be used in the color ramp.
###### Reset Color Ramp
Resets the color ramp to its default state.
###### Color Mode
###### RGB
Blends color by mixing each color channel and combining.
###### HSV/HSL
Blends colors by first converting to HSV or HSL, mixing, then combining again. This has the advantage of maintaining saturation between different hues, where RGB would de-saturate, this allows for a richer gradient.
###### Interpolation
###### Ease
Uses an Ease Interpolation for the color stops.
###### Cardinal
Uses a Cardinal Interpolation for the color stops.
###### Linear
Uses a Linear Interpolation for the color stops.
###### B-Spline
Uses a B-Spline Interpolation for the color stops.
###### Constant
Uses a Constant Interpolation for the color stops.
###### Color Ramp
The color band. A click at one of the color stops makes it the active one. You can move the color stops by clicking at them and dragging them around.
###### Active Color Stop elements
Adjust the active color stop.
###### Choose active color stop
Choose the color stop by index.
###### Pos
The position of the active color stop. The range goes from 0.000 to 1.000.

##### Object
A Data ID to select an object (usually an empty), which position and rotation will be used to define the center of the effect.
##### Radius
Defines the maximum distance of the effect.
### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Layer Pass
The layer pass index.
##### Use Layer pass
Use the layer pass.
##### Layer pass value
The layer pass value.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Material Pass
The material pass index.
##### Use Material pass
Use the Material pass.
##### Material pass value
The Material pass value.
##### Invert
Inverts the influence.
#### Custom Curve
Use a custom curve to define the noise along the strokes.

##### Navigation elements
The navigation elements at the top are described from left to right.
###### Zoom in and out
The two buttons with the magnifying glass at it zooms in and out in the curve window.

###### Clipping
Clipping options. Set up clipping for the stroke.

###### Tools
Tools is a menu where you can find some curve related tools.
###### Reset View
Resets the curve windows zoom.
###### Extend Horizontal
Extend the curve points horizontal before the first curve point and after the last curve point.
###### Extend Vertical
Extend the curve points vertical before the first curve point and after the last curve point.
###### Reset Curve
Resets the curve to the initial shape.

#### Curve window
Tweak and adjust the falloff curve by clicking at a curve point and dragging it around.
Double click adds a new point.
Holding down ctrl activates temporary snapping.
Holding down shift enables slower movement, which allows more accurate setting.
###### Vector Handle
Set handle type to Vector.
###### Auto Handle
Set handle type to Auto.
###### Auto Clamped Handle
Set handle type to Auto Clamped.
##### X / Y
The position of the currently selected curve point.
###### Delete Points
Deletes selected curve points.