12.1.6 Editors - Geometry Node Editor - Header - Add Menu - Attribute

Detailed table of content

Add menu

The Attribute menu contains the attribute nodes. These nodes allows you to work with object attributes.

## Attribute Statistics
Retreive statistic values from the input mesh.
### Inputs
#### Geometry
Standard geometry input.
#### Selection
A selection of the geometry input.
#### Attribute
Attribute to get the statistics from.
### Properties
#### Domain Type
From which domain to retreive the data.

Data Type
What data type to use.
Float will output a single floating point value.
Vector will outupt a vector 3 with floating point values.
### Outputs
Outputs the statistics for the different types.
#### Mean
The average value of all data.
#### Median
The median value of all data.
#### Sum
The sum value of all data.
#### Min
The min value of all data.
#### Max
The max value of all data.
#### Range
The difference between the max and min value.
#### Standard Derivation
How much values differ from the mean. A low standard deviation indicates that the values are grouped tightly together at the mean. A high standard deviation indicates that the values are spread out over a large range.
#### Variance
The variance of all data, defined as the square of the standard deviation.

## Capture Attribute
The Capture Attribute node stores the result of a field on a geometry, and outputs the data as a node socket so it can be used by other nodes.
The result is stored on the geometry just like a regular attribute with a name. But instead of referencing it with a name, it is retrieved whenever the socket is connected to the input of a node. Later on when evaluating the node tree, the attribute will be removed automatically if it is no longer used.
### Inputs
#### Geometry
Standard geometry input.
#### Value
Name of the attribute that is used as input. It should be a float attribute with values between zero and one.
### Properties
#### Domain Type
In which domain to store the data.

Data Type
What data type to use.

### Outputs
#### Geometry
Standard geometry output.
#### Attribute
Attribute output.

## Domain Size
The Domain Size node has a single geometry input and a selection for the component type. And outputs containing single values for the related domains are shown, based on this chosen component.

### Input
#### Geometry
Geometry input.
### Properties
#### Component
What component to calculate.

### Output
#### With type mesh
##### Point Count
The point count of the mesh.
##### Edge Count
The edge count of the mesh.
##### Face Count
The face count of the mesh.
##### Face Corner Count
The face corner count of the mesh.
#### With type Point Cloud
##### Point Count
The point count of the point cloud.
#### With type Curve
##### Point Count
The point count of the curve.
##### Spline Count
The number of splines in the curve.
#### With type Instances
##### Instances count
How many instances the input geometry has.

## Remove Named Attribute
### Input
#### Geometry
Geometry input.
#### Name
The attribute name that you want to remove.
### Outputs
#### Geometry
The output geometry.

## Store Named Attribute
Puts the results of a field in a named attribute.
### Input
#### Geometry
Geometry input.
#### Name
The attribute name that you want to store.
### Value
The value that is connected with the stored attribute.
### Properties
#### Data Type
The type for the source and result data.

###### Domain
What element to use.

### Outputs
#### Geometry
The output geometry.

## Transfer Attribute
Captures and transfers values from a target object and provides them as an attribute.
### Inputs
#### Source
The source object to take the data from.
#### Attribute
Attribute input.
#### Source Position
Source position input.
### Properties
#### Data Type
The type for the source and result data.

#### Mapping
Which data to transfer.
##### Nearest Face Interpolated
Transfer the attribute from the nearest point from anywhere on the surface. Non-face attributes are interpolated across the surface (edge attributes are not supported yet). Loose points and edges are ignored.
##### Nearest
Transfer the attribute from the nearest element (with a domain chosen by the Domain input). No interpolation is done.
###### Domain
What element to use.

##### Index
Copy the attribute data from the value at the input index. In this mode, the target geometry can consist of a mesh, point cloud, or curve. The matching component type from the context will be chosen if possible, otherwise a component will be chosen in that order.
###### Domain
What element to use.

### Outputs
#### Attribute
Attribute output.