Detailed Table of content

Select menu

The Select menu provides you with all functionality around selecting. The content differs, dependant in which mode you are, and what object type you have selected. Some select functionality is very special for just one object type in one special mode. But not every mode has a select menu.

Object Mode - Select menu

The select menu in Object mode is for all object types equal. It provides you with several selection methods.
## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Grouped
Here you can select different types of objects within the group. It requires to have a group selected.
The menu items are pretty self explaining. So we won't go into detail here.

### Last Operator Select Grouped
###### Extend
Extends existing selection instead of deselecting everything first.
###### Type
Type is a drop-down list where you can choose the Linked type again.

## Linked
Linked is a menu where you can select different types.
Here you can select all objects that shares a common data-block with the active object. Select Linked uses the active object as a basis to select all others.

### Object Data
Selects every object that is linked to the same Object Data.
### Material
Selects every object that is linked to the same material data-block.
### Instanced Collection
Selects every object that is linked to the instanced collection.
### Particle System
Selects all objects that use the same Particle System.
### Library
Selects all objects that are in the same Library.
### Library (Object Data)
Selects all objects that are in the same Library and limited to object data.

## All by Type
Here you can select objects of a specific type.
The menu items are pretty self explaining. So we won't cover every single menu item here.

### Last Operator Select By Type
#### Extend
With this option activated the selection does not clear before performing the selection operation, but extends. This means when you have a mesh object selected, and want to select all objects by type curve, then the mesh object is still selected. Without Extend just the curve objects are selected. The mesh object gets deselected.
#### Type
Type is a drop-down box where you can choose the object type to select again.

## Random
Selects random objects.
### Last Operator Select Random
###### Percent
The Percentage of objects that should be selected randomly.
###### Random Seed
The Seed for the random number generator.
###### Action
Action is a drop-down box where you can choose if you want to select or to deselect random.

## Mirror Selection
Select the mirrored parts of an object. For example for L.Sword it selects R.Sword.
### Last Operator Select Mirror
###### Extend
Extends existing selection instead of deselecting everything first.

## By Pattern
Selects all objects whose name matches the entered string. For missing parts you need to add an asterix.
For example, you have four cubes in the scene. Cube, Cube.001, Cube.002 and mycube3. Then the term " Cube " will just select the first cube. While the term " Cube* " will select the first three. And " *cube* " will select all four.
Supported wild-cards:
* matches everything
? matches any single character
[abc] matches characters in “abc”
[!abc] match any character not in “abc”
The tool operates immediately at entering the string.
#### Pattern
Here you can type in your string.
#### Case Sensitive
When ticked then the string comparison happens by taking upper and lower letters into account.
#### Extend
Extends existing selection instead of deselecting everything first.
##### Last Operator Select Pattern
The Last Operator Select Pattern contains the same menu items than the pop-up. So see above. Also, it does not appear in the 3D view. But when you call it from the edit menu or with hotkey.

## Active Camera
Selects the active camera.

## More/ Less
### More
More requires to have a parent or child relationship. It expands the selection.
### Less
Less requires to have a parent or child relationship. It reduces the selection.
### Parent
Parent requires to have a parent or child relationship. It selects the parent object of the currently selected object(s).
### Child
Child requires to have a parent or child relationship. It selects the child object(s) of the currently selected object(s).
### Parent extended
Parent extended requires to have a parent or child relationship. It selects the parent object of the currently selected object(s). But keeps the active object in the selection, even when it's not currently selected.
### Child Extended
Child Extended requires to have a parent or child relationship. It selects the child object(s) of the currently selected object(s). But keeps the active object in the selection, even when it's not currently selected.

Edit Mode - Mesh Menu

The select menu for a mesh object in Edit mode.

A few tools here acts different, dependant in which mesh select mode you are. For example, when you are in mesh select method vertices, then the Random operator picks random vertices.

So you might want to check the mesh select mode when something does not work in an expected way.

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Linked
Select the geometry that is directly linked with the current geometry. You can for example have a mesh with several closed submeshes. Those submeshes are not linked together, but are part of the object.

### Last Operator Select Linked All
#### Delimit
Here you can add a limit to the selection. For example, just select up to the next seam.

## Linked Flat Faces
Select the geometry that is coplanar to the current selection. It works also in other selection modes, but you need to have face geometry selected.
### Last Operator Select Linked Flat Faces
Here you can adjust the angle up to which a face counts as coplanar.

## Linked Pick Select
Same as with Linked. But works with what is under the mouse cursor.
## Linked Pick Deselect
Same as with Linked. But works with what is under the mouse cursor. And deselects the selection.
### Last Operator Select Linked
#### Deselect
Select or deselect.
#### Delimit
Here you can add a limit to the selection. For example, just select up to the next seam.

## Similar
Here you can select geometry based on how similar certain properties are to it. The methods changes, dependant in which mesh selection mode you are. There is a pitfall with having more than one mesh selection method selected. Then you just get the face regions type presented. Vertices, Edges, Faces, more than one ...

### Last Operator Select Similar
#### Type
Here you can choose the select similar method again.
#### Compare
Compare with method less, greater or equal.
#### Threshold
Here you can adjust the threshold value after which the element counts as similar.

## Random
Selects a random group of vertices, edges, or faces, dependant of the mesh selection method.
### Last Operator Select Random
#### Percent
How much percent will be random selected.
#### Random Seed
The random seed value.
#### Action
Select or deselect.

## Checker Deselect
Deselect alternating faces, edges or vertices to create a checker like pattern. The result is dependant of the mesh selection method.
### Last Operator Checker Deselect
#### Nth Element
Here you can define how much elements gets unchecked. With 2 you have a checker board pattern. Every second element gets deselected.
#### Skip
Skip elements before the checker algorithm deselects again.
#### Offset
Here you can offset the deselected elements.

Mirror selection
Requires to have a symmetrical mesh. Selects the mirrored mesh parts from a selection.

### Last Operator Select Mirror
#### Axis
The world axis to mirror at.
#### Extend
Keep the current selection. Without extend the current selection gets deselected.

## Side of Active
Selects all mesh data in direction of a single axis, starting from the current selection.
### Last Operator Side of Active

#### Axis mode
The axis orientation to work with.

#### Axis Sign
In which direction to work form the current selection.
#### Axis
The axis to work with.
#### Threshold
Here you can define a threshold to extend the selection.

## Shortest Path
Select the shortest edge path between two selected mesh elements. This can be vertices, edges or faces. A start and a end point must be selected.

### Last Operator Select shortest path

#### Edge Tag
With Select shortest path you can not only select the shortest path, but also already modify it. Like mark it as seam.
The available methods should be pretty self explaining.

#### Face Stepping
Traverse connected faces.

#### Topology Distance
Find the minimum number of steps instead of the shortest distance.

#### Fill Region
Select the region faces too.

#### Nth Element
Don't select the whole path, but just every nth element of it.
#### Skip
This is connected to nth element. Number of elements to skip at once.
#### Offset
This is connected to nth element. Start with an offset.

## Sharp Edges
Select all edges that are marked as sharp.
### Last Operator Select Sharp Edges
#### Sharpness
The angle after which a sharp edge gets selected.

## Loose Geometry
Selects loose geometry.
### Last Operator Select Loose Geometry
#### Extend
Extend the current selection.

## Interior Faces
Select faces where all edges have more than 2 faces. In the picture here we have inlaying faces by joining two cubes together, then merge the vertices by distance. So the two faces from the former two cubes are now interior faces. That's usually unwanted geometry that you want to select and to remove.

## Faces by Sides
Selects faces that has the same number of edges, or better said vertices. Tris, quads, N-gons.
### Last Operator Select Faces by Side
#### Sharpness
Extend the current selection.
#### Number of vertices
How many numbers of vertices the face should have. 4 is a quad.
#### Type
Selection type.
#### Extend
Extend the current selection.

## Edge Loop
Selects a loop of edges from a selected edge. The method stops at poles. That's vertices where three or more than four edges comes together. At a UV sphere the north and south pole ...
### Last Operator Multi Select Loops
#### Ring
Select edge ring instead of edge loop.
## Edge Ring
Selects edges parallel to a selected edge in the same ring of faces. The method stops at poles. That's vertices where three or more than four edges comes together. At a UV sphere the north and south pole ...
### Last Operator Multi Select Loops
#### Ring
Select edge ring instead of edge loop.
## Loop Inner-Region
Select everything that is enclosed by an edge loop. When the loop is not closed, then it might select everything ...
By default the smaller enclosed part gets selected. The Inner-Region.
### Last Operator Select Loop Inner-Region
#### Select Bigger
Select the bigger enclosed part instead of the smaller enclosed part.
## Boundary Loop
Select the edges that encloses a selection of faces.

## Ungrouped Verts
Selects ungrouped Vertices. Just active in vertex selection mode. And requires to have at least one vertex group assigned.

### Last Operator Select Ungrouped
#### Extend
Extends the current selection.

## More / Less
### More
Extends the current selection.
### Less
Reduces the current selection.
### Next Active
Selects the next active element. For example, when you have two vertices selected, then the next vertice in the row with the same distance will be selected as the next active.
### Previous Active
Like next active, but deselects in the other direction down to the first selected vertice with every step.

Curve Object - Edit Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Linked
Select the geometry that is directly linked with the current geometry. You can for example have a mesh with several closed submeshes. Those submeshes are not linked together, but are part of the object.

### Last Operator Select Linked All
#### Delimit
Here you can add a limit to the selection. For example, just select up to the next seam.

## Linked Pick Select
Same as with Linked. But works with what is under the mouse cursor.
## Linked Pick Deselect
Same as with Linked. But works with what is under the mouse cursor. And deselects the selection.
### Last Operator Select Linked
#### Deselect
Select or deselect.
#### Delimit
Here you can add a limit to the selection. For example, just select up to the next seam.

## Similar
Here you can select curve geometry based on how similar certain properties are to it.

### Last Operator Select Similar
#### Type
Here you can choose the select similar method again.
#### Compare
Compare with method less, greater or equal.
#### Threshold
Here you can adjust the threshold value after which the element counts as similar.

## Random
Selects a random group of curve points.
### Last Operator Select Random
#### Percent
How much percent will be random selected.
#### Random Seed
The random seed value.
#### Action
Select or deselect.

## Checker Deselect
Deselect alternating curve points.
### Last Operator Checker Deselect
#### Nth Element
Here you can define how much elements gets unchecked. With 2 you have a checker board pattern. Every second element gets deselected.
#### Skip
Skip elements before the checker algorithm deselects again.
#### Offset
Here you can offset the deselected elements.

## De/Select First
Select or deselect first curve point.
## De/Select Last
Select or deselect last curve point.
## Next Active
Selects the next active element. For example, when you have two vertices selected, then the next vertice in the row with the same distance will be selected as the next active.
## Previous Active
Like next active, but deselects in the other direction down to the first selected vertice with every step.
## More
Extends the current selection.
## Less
Reduces the current selection.

Surface Object - Edit Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Linked
Select the geometry that is directly linked with the current geometry. You can for example have a mesh with several closed submeshes. Those submeshes are not linked together, but are part of the object.

### Last Operator Select Linked All
#### Delimit
Here you can add a limit to the selection. For example, just select up to the next seam.

## Similar
Here you can select curve geometry based on how similar certain properties are to it.

### Last Operator Select Similar
#### Type
Here you can choose the select similar method again.
#### Compare
Compare with method less, greater or equal.
#### Threshold
Here you can adjust the threshold value after which the element counts as similar.

## Random
Selects a random group of control points.
### Last Operator Select Random
#### Percent
How much percent will be random selected.
#### Random Seed
The random seed value.
#### Action
Select or deselect.

## Checker Deselect
Deselect alternating control points.
### Last Operator Checker Deselect
#### Nth Element
Here you can define how much elements gets unchecked. With 2 you have a checker board pattern. Every second element gets deselected.
#### Skip
Skip elements before the checker algorithm deselects again.
#### Offset
Here you can offset the deselected elements.

## Control Point Row
Selects a row of control points, including the active one.

## More
Extends the current selection.
## Less
Reduces the current selection.

Metaball Object - Edit Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Similar
Here you can select metaball geometry based on how similar certain properties are to it.

### Last Operator Select Similar
#### Type
Here you can choose the select similar method again.
#### Compare
Compare with method less, greater or equal.
#### Threshold
Here you can adjust the threshold value after which the element counts as similar.

## Random
Selects a random metaball element.
### Last Operator Select Random
#### Percent
How much percent will be random selected.
#### Random Seed
The random seed value.
#### Action
Select or deselect.

Grease Pencil Object - Edit Mode, Sculpt Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Linked
Select the geometry that is directly linked with the current geometry. You can for example have a mesh with several closed submeshes. Those submeshes are not linked together, but are part of the object.

### Last Operator Select Linked All
#### Delimit
Here you can add a limit to the selection. For example, just select up to the next seam.

## Alternated
Select every second element.
### Last Operator Alternated
#### Unselect Ends
The end points are always unselected.

## Grouped
Select grouped strokes by layer or color.
### Last Operator Select Grouped
#### Type
Here you can again adjust if you want to select by layer or color.

## First
Select the first element in the stroke.
### Last Operator Select First
#### Selected Strokes only
Only select the first point of strokes that has already some geometry selected.
#### Extend
Extend the current selection.
## Last
Select the last element in the stroke.

### Last Operator Select Last
#### Selected Strokes only
Only select the last point of strokes that has already some geometry selected.
#### Extend
Extend the current selection.

## More
Extends the current selection.
## Less
Reduces the current selection.

Armature Object - Edit Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Similar
Here you can select metaball geometry based on how similar certain properties are to it.

Most methods are self explaining. Immediate children selects just the direct children of the active object, while Children selects everything downwards the hierarchy.

### Last Operator Select Similar
#### Type
Here you can choose the select similar method again.
#### Compare
Compare with method less, greater or equal.
#### Threshold
Here you can adjust the threshold value after which the element counts as similar.

## Mirror Selection
Select the mirrored parts of an object. For example for L.bone it selects R.bone.
### Last Operator Select Mirror
###### Extend
Extends existing selection instead of deselecting everything first.

## By Pattern
Selects all objects whose name matches the entered string. For missing parts you need to add an asterix.
For example, you have four cubes in the scene. Cube, Cube.001, Cube.002 and mycube3. Then the term " Cube " will just select the first cube. While the term " Cube* " will select the first three. And " *cube* " will select all four.
Supported wild-cards:
* matches everything
? matches any single character
[abc] matches characters in “abc”
[!abc] match any character not in “abc”
The tool operates immediately at entering the string.
#### Pattern
Here you can type in your string.
#### Case Sensitive
When ticked then the string comparison happens by taking upper and lower letters into account.
#### Extend
Extends existing selection instead of deselecting everything first.
##### Last Operator Select Pattern
The Last Operator Select Pattern contains the same menu items than the pop-up. So see above. Also, it does not appear in the 3D view. But when you call it from the edit menu or with hotkey.

### Parent
Parent requires to have a parent or child relationship. It selects the parent object of the currently selected object(s).
### Child
Child requires to have a parent or child relationship. It selects the child object(s) of the currently selected object(s).
### Extend Parent
Extend Parent requires to have a parent or child relationship. It selects the parent object of the currently selected object(s). But keeps the active object in the selection, even when it's not currently selected.
### Extend Child
Extend Child requires to have a parent or child relationship. It selects the child object(s) of the currently selected object(s). But keeps the active object in the selection, even when it's not currently selected.
### More
More requires to have a parent or child relationship. It expands the selection.
### Less
Less requires to have a parent or child relationship. It reduces the selection.

Armature Object - Pose Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Grouped
Select grouped bones by type.

## Constraint Targets
Select the bones used as targets for the currently selected bone.

## By Pattern
Selects all objects whose name matches the entered string. For missing parts you need to add an asterix.
For example, you have four cubes in the scene. Cube, Cube.001, Cube.002 and mycube3. Then the term " Cube " will just select the first cube. While the term " Cube* " will select the first three. And " *cube* " will select all four.
Supported wild-cards:
* matches everything
? matches any single character
[abc] matches characters in “abc”
[!abc] match any character not in “abc”
The tool operates immediately at entering the string.
#### Pattern
Here you can type in your string.
#### Case Sensitive
When ticked then the string comparison happens by taking upper and lower letters into account.
#### Extend
Extends existing selection instead of deselecting everything first.
##### Last Operator Select Pattern
The Last Operator Select Pattern contains the same menu items than the pop-up. So see above. Also, it does not appear in the 3D view. But when you call it from the edit menu or with hotkey.

## Flip Active
Mirrors the bone selection. Works with a armature with mirrored parts.
### Last Operator Flip Active/Selected Bone
#### Active Only
Only select the mirror part of the active bone.
#### Extend
Extend the current selection.
### Parent
Parent requires to have a parent or child relationship. It selects the parent object of the currently selected object(s).
### Child
Child requires to have a parent or child relationship. It selects the child object(s) of the currently selected object(s).
### Extend Parent
Extend Parent requires to have a parent or child relationship. It selects the parent object of the currently selected object(s). But keeps the active object in the selection, even when it's not currently selected.
### Extend Child
Extend Child requires to have a parent or child relationship. It selects the child object(s) of the currently selected object(s). But keeps the active object in the selection, even when it's not currently selected.

Lattice Object - Edit Mode

## All
Select everything.
## None
Select nothing.
## Inverse
Invert the current selection.
## Lasso Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a form around what you want to select. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Box Select
Note that this select method works independant from the lasso select tool in the tool shelf.
In this select mode you can select elements by dragging a rectangle. And what's inside of the rectangle gets selected then. It adds to selection by default.
To subtract from selection hold down Shift key.
The selection gets applied when you release the mouse. You leave the mode automatically when you release the mouse.
## Circle Select

Circle select enters the Circle Select mode. This is a special select mode where you can select elements by moving with the mouse over it. It adds to selection by default.
To subtract from selection hold down Shift key. To exit the Circle select click with the right mouse button.
The pencil radius of the circle select tool can be adjusted with the scroll wheel.

## Mirror
Select the mirrored parts to the current selection.
### Last Operator Select Mirror
#### Axis
Here you can choose the world axis to mirror at.
###### Extend
Extends existing selection instead of deselecting everything first.

## Ungrouped Verts
Selects ungrouped Vertices. Requires to have at least one vertex group assigned.

### Last Operator Select Ungrouped
#### Extend
Extends the current selection instead of deselecting everything first.

## More
Extends the current selection.
## Less
Reduces the current selection.