Detailed table of content

Add menu - Point

Utility nodes are mainly for mathematical operations.

## Boolean Math
The Boolean Math node performs a basic logical operation between its inputs.
### Inputs
#### Boolean
Two standard Boolean inputs.
### Properties
#### Operation
##### And
True if both inputs are true.
##### Or
True if either or both inputs are true.
##### Not
True if both inputs are false.
### Output
Boolean
Standard Boolean output.

## Clamp Node
Clamps a value between a minimum and a maximum.
### Inputs
#### Value
The input value to be clamped.
#### Min
The minimum value.
#### Max
The maximum value.
### Properties
#### Clamp Type
##### Min Max
Clamp values using Min and Max values.
##### Range
Clamp values between Min and Max range.
### Outputs
#### Result
The input value after clamping.

## Float Compare
The Float Compare node takes two inputs and does a math comparison between them.
### Inputs
#### A, B
Standard float value input.
### Properties
#### Operation
##### A is less than B
True if A is smaller than B.
##### A is lesser than or equal B
True if A is smaller or equal than B.
##### A is greater than B
True if A is bigger than B.
##### A is greater than or equal B
True if A is bigger or equal than B.
##### A is equal B
True if A and B are the same.
##### A is not equal B
True if A and B are different.
### Output
#### Result
Standard Boolean output.

## Map Range
This node converts (maps) an input value range into a destination range. By default, values outside the specified input range will be proportionally mapped as well. This node is similar to Map Value node but provides a more intuitive way to specify the desired output range.
### Inputs
#### Value
Standard value input.
#### From Min
Start of the input value range.
#### From Max
End of the input value range.
#### To Min
Startof the destination range.
#### To Max
End of the destination range.
### Properties
#### Interpolation Type
how to interpolate the values between min and max.
#### Clamp
Clamps values to Min/Max of the destination range.
### Outputs
#### Value
Standard value output.

## Math Node
The Math Node performs math operations.
### Inputs
The inputs of the node are dynamic. Some inputs are only available with certain operations. For example, the Addend input is only available in the Multiply Add operator.
#### Value
Input Value. Trigonometric functions read this value as radians.
#### Addend
Input Addend.
#### Base
Input Base.
#### Exponent
Input Exponent.
#### Epsilon
Input Epsilon.
#### Distance
Input Distance.
#### Min
Input Minimum.
#### Max
Input Maximum.
#### Increment
Input Increment.
#### Scale
Input Scale.
#### Degrees
Input Degrees.
#### Radians
Input Radians.
### Properties
#### Operation
The mathematical operator to be applied to the input values:

##### Functions
###### Add
The sum of the two values.
###### Subtract
The difference between the two values.
###### Multiply
The product of the two values.
###### Divide
The division of the first value by the second value.
###### Multiply Add
The sum of the product of the two values with Addend.
##### Power
The Base raised to the power of Exponent.
###### Logarithm
The log of the value with a Base as its base.
###### Square Root
The square root of the value.
###### Inverse Square Root
One divided by the square root of the value.
###### Absolute
The input value is read with without regard to its sign. This turns negative values into positive values.
###### Exponent
Raises Euler’s number to the power of the value.
##### Comparison
###### Minimum
Outputs the smallest of the input values.
###### Maximum
Outputs the largest of two input values.
###### Less Than
Outputs 1.0 if the first value is smaller than the second value. Otherwise the output is 0.0.
###### Greater Than
Outputs 1.0 if the first value is larger than the second value. Otherwise the output is 0.0.
###### Sign
Extracts the sign of the input value. All positive numbers will output 1.0. All negative numbers will output -1.0. And 0.0 will output 0.0.
###### Compare
Outputs 1.0 if the difference between the two input values is less than or equal to Epsilon.
###### Smooth Minimum
Smooth Minimum.
###### Smooth Maximum
Smooth Maximum.
##### Rounding
###### Round
Round the input value to the nearest integer.
###### Floor
Rounds the input value down to the nearest integer.
###### Ceil
Rounds the input value up to the nearest integer.
###### Truncate
Outputs the integer part of the value.
###### Fraction
Fraction.
###### Modulo
Outputs the remainder once the first value is divided by the second value.
###### Wrap
Outputs a value between Min and Max based on the absolute difference between the input value and the nearest integer multiple of Max less than the value.
###### Snap
Round the input value to down to the nearest integer multiple of Increment.
###### Ping-pong
The output value is moved between 0.0 and the Scale based on the input value.
##### Trigonometric
###### Sine
The Sine of the input value.
###### Cosine
The Cosine of the input value.
###### Tangent
The Tangent of the input value.
###### Arcsine
The Arcsine of the input value.
###### Arccosine
The Arccosine of the input value.
###### Arctangent
The Arctangent of the input value.
###### Arctan2
Outputs the Inverse Tangent of the first value divided by the second value measured in radians.
###### Hyperbolic Sine
The Hyperbolic Sine of the input value.
###### Hyperbolic Cosine
The Hyperbolic Cosine of the input value.
###### Hyperbolic Tangent
The Hyperbolic Tangent of the input value.
##### Conversion
###### To Radians
Converts the input from degrees to radians.
###### To Degrees
Converts the input from radians to degrees.
###### Clamp
Limits the output to the range (0.0 to 1.0). See Clamp.
### Outputs
#### Value
Numerical value output.