12.1.1 Editors - Compositor - Header - Tools and Options

Options

At the right side of the header you will see the options.
## Use Nodes
The Use Nodes setting is mostly a legacy setting and should always be checked for materials.
## Pin (pin icon)
The pin button will keep the current material selection fixed. When a material is pinned, it will remain visible in the shader editor even when another object or material is selected elsewhere.
## Parent Node Tree
Grouping nodes can simplify a node tree by allowing instancing and hiding parts of the tree. Both material and composite nodes can be grouped. This button becomes active when you work with such grouped nodes, and you are in a child group. it allows you to switch to the parent group.
## Backdrop
By adding a viewer node you can display the compositing result as a background in the viewport. Here you can activate it, and adjust the look. It also contains controls to adjust the zoom and position of the backdrop image.
### Background Image Move
Move the background image. A click confirms. Watch the hotkey.
### Background Image Zoom in and out
Zoom in and out the Background image.
### Background Image Fit
Fits the background image into the view.
### Display channels
What channels to display in the backdrop.
## Snap
Activates snapping. When the tool is activated, then you will also reveal the snap settings where you can choose different snap methods.