12.1.18 Editors - Geometry Nodes Editor - Header - Add Menu - Curve - Write

Detailed table of content

Add - Curve - Write

Here you find curve related nodes.

## Set Curve Normal
Set the evaluation mode for curve normals.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Mode
The evaluation mode for the curve normals.
### Outputs
#### Curve
The curve output.

## Set Curve Radius
Set the curve radius.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Radius
The radius to set.
### Outputs
#### Geometry
Standard geometry output.

## Set Curve Tilt
Controls the tilt angle at each curve control point.
### Input
#### Geometry
The input curve.
#### Selection
Whether or not to change the value on each control point. True values mean the value will be changed, false values mean the value will remain the same.
#### Tilt
The tilt rotation.
### Outputs
#### Curve
Standard geometry output.

## Set Handle Positions
Set the handle positions of bezier curves
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Position
The position of the handle.
### Properties
#### Mode
Left or right handles.
### Outputs
#### Geometry
Standard geometry output.

## Set Handle Type
Sets a handle type for the curve points of a bezier curve. Handle types determines how the interpolation before and after the curve point happens.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Mode
Left or right handles.
#### Handle Type
The different available handle types.

##### Free
The handles can be adjusted individually.

##### Auto
The left and the right handle will always point to each other. The length of the handles will start in equal size.

##### Vector
The handles can be adjusted individually.

##### Aligned
The left and the right handle will always point to each other.
### Output
#### Curve
Standard geometry output.

## Set Spline cyclic
Sets the spline cyclic. Means looping.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Cyclic
Cyclic or not
### Outputs
#### Geometry
Standard geometry output.

## Set Spline Resolution
Sets the resolution of the spline. Means how many evaluated points should be generated on the curve for each control point.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Resolution
The resolution of the spline.
### Outputs
#### Geometry
Standard geometry output.

## Set Spline Type
Change the curve spline type.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Spline Type
The spline type to set the curve to.
Note that when converting from a NURBS spline to a Bézier spline, at least six points are needed. When the number of points is not a multiple of three a full conversion is not possible and the spline has to be truncated.
### Output
#### Curve
Standard geometry output.