12.1.19 Editors - Geometry Nodes Editor - Header - Add Menu - Curve - Operations

Detailed table of content

Add - Curve

Here you find curve related nodes.

## Cuve to Mesh
Converts a curve object to a mesh object. Optionally, a profile curve can be provided to give the curve a custom shape.
### Inputs
#### Curve
The input curve.
#### Profile Curve
If a profile curve is provided, it will be extruded along all splines. Otherwise the generated mesh will just be a chain of edges.
#### Fill Caps
For cyclic profile curve. Fill the ends of the generated mesh for each spline combination with an N-gon.
The resulting mesh is Manifold, the two new faces for each spline are simply connected to existing edges.
### Outputs
#### Mesh
Standard mesh output.

## Cuve to Points
Converts a curve object to a Point cloud.
### Inputs
#### Curve
The input curve.
### Properties
#### Mode
How to generate points from the input curve.

##### Evaluated
Create points from the evaluation points of the curve. This is based on the resolution attribute for nurbs and bezier splines.
##### Count
Sample each spline by evenly distributing the specified number of points along the spline.
###### Count Input
The number of points to distribute along the spline.
##### Length
Sample each spline by splitting the spline into segments by the specified length.
###### Length Input
The length of the single segments.
### Outputs
#### Point
Generated point cloud.
#### Tangent
The normalized curve tangent at the sampled position, or the direct evaluated normal in Evaluated mode.
#### Normal
The normal value from the evaluated curve at each result point. This is the same value from the Normal Node at those positions.
#### Rotation
The Euler rotation build from the Tangent and Normal outputs.

## Deform Curves on Surface
Curves that are attached to a surface can follow the surface at modification.
### Inputs
#### Curves
The input curve.
### Outputs
#### Curves
The output curve.

## Fill Curve
Fills the curve with mesh geometry. The mesh is only generated flat with a local Z of 0.
### Inputs
#### Curve
The input curve.
### Properties
#### Mode
#### Triangles or N-gons
Fill the curve with either triangles, or use N-Gon geometry.
### Outputs
#### Mesh
The output as mesh.

## Fillet Curve
The Fillet Curve rounds corners on curve control points, similar to the effect of the Bevel Modifier on a 2D mesh.
A key difference is that the rounded portions created by the Fillet Curve node are always portions of a circle.
### Input
#### Curve
The input curve.
#### Count
Polymode. Define the number of vertices that are created.
#### Radius
The radius of the arc
#### Limit Radius
Prevent overlapping when the defined radius exceeds the maximum possible radius for a given point.
### Properties
#### Mode
##### Bezier
Creates a circular arc at vertices by changing handle lengths (applicable only for Bezier splines).
##### Poly
Creates a circular arc by creating vertices (as many as defined by the Count fields input) along the arc (applicable for all spline types).
### Outputs
#### Curve
Standard geometry input with a curve component.

## Interpolate Curves
Todo

## Resample curve
Creates a poly spline for each input spline. In the Count and Length modes, the control points of the new poly splines will have uniform spacing.
### Input
#### Curve
The input geometry.
#### Selection
A selection of the input geometry
#### Count
The number of control points on the new splines.
#### Length
The approximate length between the control points of the new splines.
### Properties
#### Mode
The resample mode.
##### Evaluated
Use the resolution attribute for spline and bezier curves.
##### Count
Use the count of the curve points.
##### Length
Use the length of the curve.
### Output
#### Curve
Standard geometry output.

## Reverse Curve
Reverses the direction of the spline. The start point becomes the end point and vice versa. The shape of the spline is not modified.
### Inputs
#### Curve
The input curve.
#### Selection
An optional selection attribute to determine which part of the spline should be reversed.
### Outputs
#### Curve
Standard geometry output.

## Subdivide Curve
Subdivides the curve. The shape is not changed.
### Inputs
#### Geometry
The input curve.
#### Cuts
The number of cuts per segment.
### Outputs
#### Geometry
Standard geometry output.

## Trim Curve
The Curve Trim node shortens each spline in the curve by removing sections at the start and end of each spline.
Bézier splines will still output as Bézier splines. The first and last control point and its handles will be moved as necessary to preserve the shape. But NURBS splines will be transformed into poly splines in order to be trimmed.
Cyclic splines are currently not supported.
Note that if the Start input is larger than the End, then the resulting spline will have a single point, located at the sample location of the Start value.
### Inputs
#### Curve
The input curve.
#### Selection
A selection of the curve.
#### Start
The start point of the spline, as a factor.
#### End
The end point of the spline, as a factor.
### Properties
#### Mode
How to find endpoint positions for the trimmed spline.
##### Factor
The endpoint positions of each spline’s length is determined by a factor. The input values should be between 0 or 1.
##### Length
The endpoint positions of each spline is determined by a length from the start of each spline. The input values should be between 0 and the length of the splines.
### Outputs
#### Curve
Standard geometry output.