12.1.27 Editors - Geometry Nodes Editor - Header - Add Menu - Mesh Primitives

Detailed table of content

Add menu - Mesh - Primitives

Nodes to modify the mesh geometry.

## Cone
Cone creates a Cone mesh.
### Input
#### Vertices
Number of vertices.
#### Radius Top
The initial radius at the top.
#### Side Segments
Adjust the number of segments at the side.
#### Fill Segments
Adjust the number of segments at the fill faces.
#### Radius Bottom
The initial radius at the bottom.
#### Depth
The initial height.
### Properties
#### Fill Type
Defines how the Circle mesh is filled.
##### None
pure edge geometry.
##### N-Gon
The circle face is a N-Gon face.
##### Triangles
The circle face is triangulated.
### Outputs
#### Geometry
Standard geometry output.

## Cube
Cube creates a Cubeoid mesh.
### Input
#### Size
The initial size in X , Y and Z dimensions
#### Vertices
How much vertices the single edges has. This allows to subdivide the cube.
### Output
#### Geometry
Standard geometry output.

## Cylinder
Cylinder creates a Cylinder mesh.
### Input
#### Vertices
Number of vertices.
#### Side Segments
Adjust the number of segments at the side.
#### Fill Segments
Adjust the number of segments at the fill faces.
#### Radius
The initial radius.
#### Depth
The initial height.
### Properties
#### Fill Type
Defines how the Circle mesh is filled.
##### None
pure edge geometry.
##### N-Gon
The circle face is a N-Gon face.
##### Triangles
The circle face is triangulated.
### Outputs
#### Geometry
Standard geometry output.

## Grid
Grid creates a grid mesh.
### Input
#### Size
The initial size.
#### Vertices X
The initial number of vertices in X direction.
#### Vertices Y
The initial number of vertices in Y direction.
### Outputs
#### Geometry
Standard geometry output.

## Ico Sphere
Ico Sphere creates a ico Sphere mesh.
### Input
#### Radius
The initial radius.
#### Subdivisions
The initial subdivisions.
### Outputs
#### Geometry
Standard geometry output.

## Mesh Circle
Circle creates a Circle mesh.
### Input
#### Vertices
Number of vertices.
#### Radius
The initial radius.
### Properties
#### Fill Type
Defines how the Circle mesh is filled.
##### None
pure edge geometry.
##### N-Gon
The circle face is a N-Gon face.
##### Triangles
The circle face is triangulated.
### Outputs
#### Geometry
Standard geometry output.

## Mesh Line
Line creates a line mesh.
### Input
#### Count
The initial number of segments.
#### Start Location
The initial location.
#### Offset
The initial offset.
### Properties
#### Mode
##### Offset
Specify the offset from one vertice to the next.
##### End Points
Specify the line start and endpoints.
###### Count Mode
###### Count
Specify the number of total vertices.
###### End Points
Specify the distance between the vertices.
### Outputs
#### Geometry
Standard geometry output.

## UV Sphere
UV Sphere creates a uv sphere mesh.
### Input
#### Segments
The initial number of segments.
#### Rings
The initial number of edgerings.
#### Radius
The initial radius.
### Outputs
#### Geometry
Standard geometry output.