Draw Mode - Draw Menu

## Active Layer
Set and show the active grease pencil layer. The layer with the pencil is the active layer for drawing.
### New Layer
Add a new draw layer.
## Interpolate
Interpolates strokes between the previous and next keyframe by adding a single keyframe. When you are on a frame between two keyframes and click the Interpolate button a new breakdown keyframe will be added. This way you define the final interpolation for the new stroke.
## Sequence
Interpolate strokes between the previous and next keyframe by adding multiple keyframes. When you are on a frame between two keyframes and click the sequence button, then a breakdown keyframe will be added on every frame between the previous and next keyframe.

## Animation
### Insert Blank Keyframe ( Active Layer )
Inserts a keyframe into the active layer.
### Insert Blank Keyframe ( All Layers )
Inserts a keyframe into all layers.
#### Last Operator Insert Blank Frame
Some snap operations shows a last operation panel, some not.
##### All Layers
Insert into active layer or into all layers.

### Duplicate Active Keyframe ( Active Layer )
Duplicates the active keyframe in the active layer.
### Duplicate Active Keyframe ( All Layers )
Duplicates the active keyframe in all layers.
#### Last Operator Insert Blank Frame
Some snap operations shows a last operation panel, some not.
##### Mode
Duplicate the active keyframe in the active layer or in all layers.

### Delete Active Keyframe ( Active Layer )
Deletes the active keyframe in the active layer.
### Delete Active Keyframe ( All Layers )
Deletes the active keyframe in all layers

## Show/Hide
### Show all Layers
Makes all layers in the scene visible .
#### Last Operator Hide Layers
##### Select
Shows just selected layers.

### Hide Active Layer
Hides the active layer.
### Hide inactive Layers
Hides the not selected layers. The selected layers stays visible.
#### Last Operator Hide Layers
##### Unselected
Hides the not selected layers.

## Clean Up

### Boundary Strokes
Remove "no fill" boundary strokes from the active frame.
### Boundary Strokes all Frames
Remove "no fill" boundary strokes from all frames.
#### Last Operator Clean Fill Boundaries
##### Mode
Choose if you want to remove the "no fill" boundary strokes just from the active frame, or from all frames.

### Delete loose Points
Deletes loose stroke points.
#### Last Operator Clean loose points
##### Limit
Adjust with how much vertices a stroke gets count as loose geometry.
### Delete Duplicated Frames
Deletes all duplicated frames.
#### Last Operator Clean Duplicated Frames

##### Type
Delete just in the selected frames or in all frames.

### Recalculate Geometry
Update all internal geometry data

## Brush Radius
Adjust the brush radius by hotkey. Hotkey only tool! The menu entry just exists to tell you that the functionality is available.
## Brush Strength
Adjust the brush strength by hotkey. Hotkey only tool! The menu entry just exists to tell you that the functionality is available.
## Eraser Radius ( Old Toolsystem)
Adjust the eraser brush radius by hotkey. Hotkey only tool! The menu entry just exists to tell you that the functionality is available.