12.1.48 Editors - Geometry Nodes Editor - Header - Add Menu - Hair - Write

Detailed table of content

Add menu - Hair - Utility

Hair nodes are, different from the other nodes in the add menu, groups of nodes. And not single nodes. You can enter the node tree by clicking at the icon up right. Tab to leave the node tree. And you can of course also edit the node tree.

## Set Hair Curve Profile
Set the radius attribute of hair curces according to a profile shape.
### Input
#### Geometry
The input geometry.
#### Replace Radius
Replace the original radius.
#### Radius
Base radius to be set when replace radius is enabled.
#### Shape
Shape of the radius along the curve.
#### Factor Min
Factor of the radius at the minimum.
#### Factor Max
Factor of the radius at the maximum.
### Output
#### Geometry
The output geometry.