12.1.21 Editors - Geometry Nodes Editor - Header - Add Menu - Volume

Detailed table of content

Add menu - Volume

Here you find nodes to modify the volume.

## Volume to Mesh
The Volume to Mesh node generates a mesh on the “surface” of a volume. The surface is defined by a threshold value. All voxels with a larger value than the threshold are considered to be outside.
Note that currently this node only works on volumes generated using geometry nodes.
### Inputs
#### Geometry
Standard geometry input.
#### Density
The density input of the volume object. Either a tag or the information from another node.
#### Threshold
The voxel amount to use.
#### Adaptivity
The input radius.
### Properties
#### Resolution
Base the voxel resolution at the gridsize, the amount or the size of the point cloud.

### Output
#### Geometry
Standard geometry output.

Legacy - Volume

These nodes existed in a former Bforartists version, but are now deprecated. They do not show in the regular menu or UI anymore. And you cannot insert them in a newer Bforartists version. But old projects that uses this nodes still loads with these nodes showing and enabled.

## Points to Volume
Creates a fog volume sphere around every point in the input geometry. The new volume grid is then called density.
### Inputs
#### Geometry
Standard geometry input.
#### Density
The density of the point cloud.
#### Voxel Amount
The voxel amount to use.
#### Radius
The radius of the generated volume around each point.
### Properties
#### Resolution
Base the voxel resolution at the amount or the size of the point cloud.

#### Radius
The type of the radius input.
### Output
#### Geometry
Standard geometry output.