UV Editor

The UV Image Editor is the place where you can display and edit the UV mapping, which doesn't necessarily require to have an image to be loaded.

The functionality of the UV Editor is connected to the 3D view. You need to have a mesh object selected, and you need to be in Edit mode to show the UV wire.

The UV editor is divided into several areas has several tool areas.

Green - Tool Settings Area
Grey - Viewport
Orange - Header
Blue - Tool Shelf
Pink - Sidebar

The Tool Settings area contains the same functionality than the Tools tab in the Sidebar. So we won't cover it.

Navigating in the UV Image Editor viewport

## Hotkeys
Pan the view - MMB
Zoom - Mouse Wheel, LMB+CTRL, Numpad + / -
## Navigation Elements
There are also two navigation elements for panning and zoom in the upper right corner. Click at them, hold the mouse button down, and move.
## 2D Cursor
The 2D Cursor is the center point for tool operations. It can be set to mouse position with Alt + Right Mouse click. Or with the Cursor tool in the

UV context menu

When you double right click into the viewport, then you will open a menu. The UV Context menu. Its content is to 100% double content to already existing menus. And it is despite the name not contextual.

## Unwrap
Unwraps the selected geometry with the method Angle based. ABF stands for Angle Based Flattening.
### Last Operator Unwrap
The last operator appears in the 3D view. Unwrap ABF and Unwrap LSCM shares the same Last Operator.
#### Method
Method is a drop down box where you can choose between Unwrap method Angle Based and Conformal.
#### Fill Holes
Fill holes in the mesh before unwrapping.
#### Correct Aspect
Take the Image Aspect Ratio into account.
#### Use Subsurf Modifier
Unwraps an existing Subsurf Modifier. You need to add a Subsurf Modifier first.
#### Margin
The distance between the single UV patches.

## Follow Active Quads
Follow Active quads maps UV coordinates starting from an active face, and maps all adjacent faces in quad shape then. This way you can for example unwrap a pipe or a road. You first need to have a face selected. Then select everything. And then click at Follow Active Quads.
### Last Operator Follow Active Quads
The Last Operator contains the same settings than the Settings dialogue.
#### Edge Length Mode
Edge Length Mode is a drop-down box where you can choose the Length method.

## Pin
Pins the selected vertices . This vertices are now nailed for the unwrap algorithms Angle based and Conformal. Their positions will not change when you repeat the unwrapping. And the algorithms will try to fit the rest of the geometry to this pinned vertices.
Pinned vertices are marked red.
A use case is for example when you have a distorted result for symmetric geometry like a face with the Conformal method. Then you can try to align two center vertices, pin them, and repeat the conformal method. It may be more symmetrical afterwards.
## Unpin
Unpins pinned geometry.

## Snap
Snap is a sub menu with some snapping tools. The menu items should be pretty self explaining. Selected to Pixels snaps the selected geometry to the pixels of the image, and so on.

### Last Operator Snap Selection and Snap Cursor
#### Target
Set the snap target method again.

#### Last operator Pin
This last operator appears in the 3D view. Pin and unpin shares the same last operator.
##### Clear
Unpins pinned geometry.

## Mirror X
Mirrors the selection along the X axis. The mirror point is the pivot of the selection.
## Mirror Y
Mirrors the selection along the Y axis. The mirror point is the pivot of the selection.
### Last Operator Mirror
The Last Operator Mirror panel gives you tools to adjust the mirror action.
#### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the mirroring action.

#### Constraint Axis
Constraint Axis gives you the possibility to define the mirror axis. You can choose more than one axis here.
#### Proportional Editing
Activates proportional editing
#### Proportional Editing Falloff
Proportional Editing Falloff is a drop-down box where you can choose a method for the falloff for the proportional editing.

#### Connected
The proportional falloff gets calculated for connected parts only.
#### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Straighten
Straightens the selected geometry in both directions, X and Y axis.
## Straighten X
Straightens the selected geometry along the X axis.
## Straighten Y
Straightens the selected geometry along the Y axis.
## Align Auto
Aligns the selection. The align axis gets chosen from the selection itself. When it's higher than tall, then it aligns along the Y axis. When it's taller than high, then it aligns along the X axis.
The align point is the pivot of the selection.
## Align X
Aligns the selection along the X axis. The align point is the pivot of the selection.
## Align Y
Aligns the selection along the Y axis. The align point is the pivot of the selection.
### Last operator Align
The Last operator Align unions all the single straighten and align actions in one operator.
#### Axis
Lists the straighten and align methods again.

## Merge
### At Center
Merges the selected vertices at the center.
### At Cursor
Merges the selected vertices at the 2d cursor
#### Last operator Snap Selection

##### Target
To which element to snap to.

### By Distance
Merge vertices that are below a specified distance to each other.
#### Last operator Merge UVs by Distance
##### Merge Distance
Maximum distance for welding vertices.
##### Unselected
Merge selected vertices to other unselected vertices.

## Stitch
Stitch tries to union UV patches along the selected edges or vertices.

### Last Operator Stitch
This last operator appears in the 3D view.
#### Use Limit
Just snap when the elements are below a given distance.
##### Snap Island
Snap the whole UV patch, or just the selected edge(s)/vertices
#### Limit
The limit distance for Use Limit.
#### Static Island
Adjust which island stays in place when stitching.
#### Active Object
Index of the active object.
#### Snap at Midpoint
Snap at the center point of the two elements instead the first to the last.
#### Clear Seams
Unmarks seams when stitching.
#### Operation Mode
The operation mode. Calculate with Edges or Vertices.

## Split
### Selection
Split the selected geometry from the not selected geometry.

Quick Favorites menu

When you right click at a menu or a button, then a right click menu will open. Tools have usually an Add to Quick Favorites menu entry.

The Quick Favorites Menu is empty by default. With Add to Quick favorites you can add this menu to the Quick menu.

In the 3D view we have a menu called Quick in the header, which shows this content then. In the Image Editor you can just call it with its hotkey. Q. It has no regular menu entry here.

Slider snapping

Snapping also works at sliders. Hover with the mouse over the slider, start to slide, and holding down Ctrl will snap the sliders in incremental steps.
When it's a default value between 0 and 1 then it usually snaps in 0.1 steps. When it's a default value over 1 then it usually snaps in steps of 10.

Hotkey only functionality

Important! These hotkeys works with the default Bforartists key map And they do not list the Ndof hotkeys. Ndof is a 3d connexion mouse device that is also used for tablets.
Most of the tools can be found in the graphical UI. But there are still some tools that are hotkey only. Some have a UI brother with equal functionality. For example, Pick shortest path is the hotkey sister of Select shortest path. Some are hotkey only since they cannot be integrated in the graphical UI. Like calling the File menu under the mouse. Or mouse position dependent functionality like selecting an edge loop.
The navigation hotkeys and the context menus are excluded here since they are already covered.
## Loop Select - Alt Left Mouse
Select an edge loop.
## Loop Select - Shift Alt Left Mouse
Select an edge loop. Adds to selection.
## Edge Ring Select - Ctrl Alt Left Mouse
Select an edge ring.
## Edge Ring Select - Shift Ctrl Alt Left Mouse
Select an edge ring. Adds to selection.

## Unwrap - U
Unwraps the selected geometry. This operator starts with the method Angle based.
### Last Operator Unwrap
The last operator appears in the 3D view. Unwrap ABF and Unwrap LSCM shares the same Last Operator.
#### Method
Method is a drop down box to choose between Unwrap method Angle Based and Conformal.
#### Fill Holes
Fill holes in the mesh before unwrapping.
#### Correct Aspect
Take the Image Aspect Ratio into account.
#### Use Subsurf Modifier
Unwraps an existing Subsurf Modifier. You need to add a Subsurf Modifier first.
#### Margin
The distance between the single UV patches.

## Pick shortest path
Click at the first edge or vertice, hold down ctrl, click at the last edge or vertice.
### Last operator Pick shortest path
#### Face stepping
Traverse connected faces. Including diagonals and edge rings.
#### Topology Distance
Find the minimum number of steps. And ignore the spatial distance.
#### Deselected
Don't select the whole path, but just every nth element of it.
#### Selected
This is connected to nth element. Number of elements to skip at once.
#### Offset
This is connected to nth element. Start with an offset.