12.1.43 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities

Detailed table of content

Add menu - Utilities

Utility nodes are mainly for mathematical operations.

## Index Switch
The Index Switch node is meant as a simpler version of the Menu Switch node. It doesn't allow naming items or displaying them in a dropdown, but still allows choosing between an arbitrary number of items, unlike the regular Switch node where you can just switch between two states.
### Inputs
#### Index
Wich input to choose.
#### 0 , 1 ...
The available input index types that you want to switch between. You can define more input sockets in the sidebar.

### Properties
#### Data Type
What input type to evaluate.

### Outputs
#### Output
The output index.

## Menu Switch
The Menu Switch node selects and computes one input based on a user-defined menu. Only the selected input is computed.
Menu entries can be added, removed, renamed, and reordered. Renaming keeps existing input links.
The menu can be used in node groups and the nodes modifier UI. Connecting the menu to a Group Input node exposes it as a group input. A menu needs to be connected to a Menu Switch node to work. An unconnected menu is empty.
Connecting multiple Menu Switch nodes to the same output creates a conflict. To avoid this, a menu switch can be grouped. Multiple groups of the same type can connect to the same menu.
Note: You cannot plug in the same value socket into the Menu selector. If you’d like to use the same value for various Menu Switches, group the Menu Switch into a Node Group and use the top-level switch override.
Top Level Grouped Menu Switches with same inputs:	Conflict caused by Same Level menu Switch inputs:

### Inputs
#### Data Type
Determines the data type the menu switch will operate in.

#### Menu
Determines which of the input options will be selected and passed through as the default.
#### A , B ...
The available input index types that you want to switch between. You can define more input sockets in the sidebar Menu Switch panel.
Note: You can add more menu switch options to the empty socket.

### Properties
#### Data Type
Determines the type of the data that is handled by the node.

### Outputs
#### Output
The output index.

## Random Value
Generates a random value.
### Input
##### Min
The minimum value of the range. This input is only available for Float, Integer, and Vector types.
##### Max
The maximum value of the range. This input is only available for Float, Integer, and Vector types.
##### ID
An ID to drive the random number generator seed. By default, this input uses the same value as if the ID Node, which is the id attribute of the context geometry if it exists, and otherwise the index.
##### Seed
The random seed for the random number generation.
### Properties
#### Data Type
What kind of random value to create. The items should be self explaining.
### Output
#### Value
The output value.

## Repeat Zone

When adding a repeat zone, two nodes are added with a “zone” set between them. The inputs connected to the Repeat Input node reads and gets data at the beginning of the loop before starting the looping - then the data is processed within the zone, here you can set any changes to the data to then repeat the execution again at the beginning of the chain for the next iteration of the loop. This chain of operations is repeated the specified number of times in the Repeat Input node.
In the example in the image above, we duplicate the cube, transform it with a rotation, then join it together again. We do this 8 times in a loop, creating a circular array.
Note: It is not possible to set data outside the Repeat Zone, you can only get data from outside the Repeat Zone. Any data connected from the outside of the zone are constant throughout every iteration based on their value at the current frame. The result of the looping can only be accessed via the Repeat Output node.
#### Repeat Zone Input
The beginning of the iteration or loop.
##### Input
###### Iterations
Number of repetitions or loops.
###### Geometry
Standard geometry input.
##### Output
###### Geometry
Standard geometry output.

#### Repeat Zone Output
The result and output of the iteration or loop. You can define custom attributes outputs here from the
##### Input
###### Geometry
Standard geometry output.
##### Output
###### Geometry
Standard geometry output.

## Switch
Switch between two inputs values based on a boolean.
### Inputs
#### Switch
The boolean switch.
#### A
The input value A. Used when the switch is off.
#### B
The input value B. Used when the switch is on.

### Properties
#### Input Type
What input type the values are, which defines what type to output then.

### Outputs
#### Output
Numerical value output.