12.1.8 Editors - Geometry Nodes Editor - Header - Add Menu - Curve

Detailed table of content

Add - Curve

Here you find curve related nodes.

## Cuve Length
Retreives the length of all splines added together.
### Inputs
#### Curve
The input curve.
### Outputs
#### Length
The length of the curve.

## Cuve to Mesh
Converts a curve object to a mesh object. Optionally, a profile curve can be provided to give the curve a custom shape.
### Inputs
#### Curve
The input curve.
#### Profile Curve
If a profile curve is provided, it will be extruded along all splines. Otherwise the generated mesh will just be a chain of edges.
#### Fill Caps
For cyclic profile curve. Fill the ends of the generated mesh for each spline combination with an N-gon.
The resulting mesh is Manifold, the two new faces for each spline are simply connected to existing edges.
### Outputs
#### Mesh
Standard mesh output.

## Cuve to Points
Converts a curve object to a Point cloud.
### Inputs
#### Curve
The input curve.
### Properties
#### Mode
How to generate points from the input curve.

##### Evaluated
Create points from the evaluation points of the curve. This is based on the resolution attribute for nurbs and bezier splines.
##### Count
Sample each spline by evenly distributing the specified number of points along the spline.
###### Count Input
The number of points to distribute along the spline.
##### Length
Sample each spline by splitting the spline into segments by the specified length.
###### Length Input
The length of the single segments.
### Outputs
#### Point
Generated point cloud.
#### Tangent
The normalized curve tangent at the sampled position, or the direct evaluated normal in Evaluated mode.
#### Normal
The normal value from the evaluated curve at each result point. This is the same value from the Normal Node at those positions.
#### Rotation
The Euler rotation build from the Tangent and Normal outputs.

## Deform Curves on Surface
Curves that are attached to a surface can follow the surface at modification.
### Inputs
#### Curves
The input curve.
### Outputs
#### Curves
The output curve.

## Fill Curve
Fills the curve with mesh geometry. The mesh is only generated flat with a local Z of 0.
### Inputs
#### Curve
The input curve.
### Properties
#### Mode
#### Triangles or N-gons
Fill the curve with either triangles, or use N-Gon geometry.
### Outputs
#### Mesh
The output as mesh.

## Fillet Curve
The Fillet Curve rounds corners on curve control points, similar to the effect of the Bevel Modifier on a 2D mesh.
A key difference is that the rounded portions created by the Fillet Curve node are always portions of a circle.
### Input
#### Curve
The input curve.
#### Count
Polymode. Define the number of vertices that are created.
#### Radius
The radius of the arc
#### Limit Radius
Prevent overlapping when the defined radius exceeds the maximum possible radius for a given point.
### Properties
#### Mode
##### Bezier
Creates a circular arc at vertices by changing handle lengths (applicable only for Bezier splines).
##### Poly
Creates a circular arc by creating vertices (as many as defined by the Count fields input) along the arc (applicable for all spline types).
### Outputs
#### Curve
Standard geometry input with a curve component.

## Resample curve
Creates a poly spline for each input spline. In the Count and Length modes, the control points of the new poly splines will have uniform spacing.
### Input
#### Curve
The input geometry.
#### Selection
A selection of the input geometry
#### Count
The number of control points on the new splines.
#### Length
The approximate length between the control points of the new splines.
### Properties
#### Mode
The resample mode.
##### Evaluated
Use the resolution attribute for spline and bezier curves.
##### Count
Use the count of the curve points.
##### Length
Use the length of the curve.
### Output
#### Curve
Standard geometry output.

## Reverse Curve
Reverses the direction of the spline. The start point becomes the end point and vice versa. The shape of the spline is not modified.
### Inputs
#### Curve
The input curve.
#### Selection
An optional selection attribute to determine which part of the spline should be reversed.
### Outputs
#### Curve
Standard geometry output.

## Sample Curve
Calculates a point on a curve at a certain distance from the start of the curve, specified by the length or factor inputs. It also outputs data retrieved from that position on the curve.
The sampled values are linearly interpolated from the values at the evaluated curve points at each side of the sampled point.
In case that the curve contains multiple splines, the sample position is found based on the total accumulated length, including the lengths of all previous splines. The order of the splines is the same order as displayed in the Spreadsheet Editor.
### Input
#### Curve
The input geometry.
#### Value
Input Value.
#### Mode Factor
##### Factor
The resample amount with method Factor.
##### Curve Index
The curve index.
#### Mode Factor
##### Factor
The resample amount with method Factor.
#### Length
The resample amount with method Length.
### Properties
#### Data Type
What data to calculate.

#### Sample Curve Mode
How to calculate the curve. By a factor, or by its length.
#### All Curves
Sample lengths based on the length of all curves.
### Output
#### Value
Output Value.
#### Position
The position at the sample along the spline.
#### Tangent
The normalized curve tangent at the sample.
#### Normal
The normalized curve normal at the sample.

## Subdivide Curve
Subdivides the curve. The shape is not changed.
### Inputs
#### Geometry
The input curve.
#### Cuts
The number of cuts per segment.
### Outputs
#### Geometry
Standard geometry output.

## Trim Curve
The Curve Trim node shortens each spline in the curve by removing sections at the start and end of each spline.
Bézier splines will still output as Bézier splines. The first and last control point and its handles will be moved as necessary to preserve the shape. But NURBS splines will be transformed into poly splines in order to be trimmed.
Cyclic splines are currently not supported.
Note that if the Start input is larger than the End, then the resulting spline will have a single point, located at the sample location of the Start value.
### Inputs
#### Curve
Standard geometry input with a curve component.
#### Start
The factor or length used to determine where to start each output spline.
#### End
The factor or length used to determine where to end each output spline.
### Properties
#### Mode
How to find endpoint positions for the trimmed spline.
##### Factor
The endpoint positions of each spline’s length is determined by a factor. The input values should be between 0 or 1.
##### Length
The endpoint positions of each spline is determined by a length from the start of each spline. The input values should be between 0 and the length of the splines.
### Outputs
#### Curve
Standard geometry output.

## Curve Handle Positions
Get the position of the left or right handle of a curve point.

### Outputs
#### Left
The left handle of the curve point.
#### Right
The right handle of the curve point.

## Curve Tangent
Retreive the tangent direction of a curve. The output values are normalized vectors.
Note that for NURBS and Bézier spline curves the value retrieved from this node is the value at every control point, which may not correspond to the visible evaluated points. For NURBS splines the difference may be even more pronounced and the result may not be as expected. A Resample Curve Node node can be used to create a poly spline, where there is a control point for every evaluated point.
### Outputs
#### Factor
The vector of the tangent.

## Curve Tilt
Outputs the angle used to turn the curve normal around the direction of the curve tangent in its evaluated points.
The output is per control point. For NURBS and Bézier splines, the values will be interpolated to the final evaluated points.
### Outputs
#### Tilt
The tilt angle for the normal in radians.

## Endpoint Selection
The Endpoint Selection node allows for the Selection of an aribitrary
number of endpoints from each spline in a curve. The start and end
inputs are evaluated on the spline domain. The result is outputted
as a boolean field on the point domain.
### Input
#### Start Size
The start point of the spline.
#### End Size
The end point of the spline.
### Outputs
#### Selection
Selection output.

## Handle Type Selection
Creates a selection based on the handle types of the control points.
### Properties
#### Left / Right
Wether to check for the type of handles.
#### Handle Type
What handle type to compare.
### Output
#### Selection
The selection.

## Is Spline Cyclic
Retreive if the curve is set to cyclic.

### Outputs
#### Cyclic
If the spline is cyclic or not.

## Spline Length
Retreive the total length of each spline in a curve.
### Outputs
#### Length
The length of each spline in the curve.
#### Point Count
Integer Field input of the number of control points on each spline in the spline domain. Or in the point domain, it is the number of points on the spline that contains the given control point.

## Spline Parameter
The Curve Parameter node outputs how far along each spline a control point is, with a value between zero and one. The output is different from dividing the index by the total number of control points, because the control points might not be equally spaced along the curve.
The first value is zero, so the output corresponds to the length at the control point rather than including the length of the following segment.

When used on the spline domain, the node outputs the portion of the total length of the curve (including all splines) has been traversed at the start of each spline. The order of the curve’s splines is visible in the Spreadsheet Editor.
Note that for NURBS and Bézier spline curves the value retrieved from this node is the value at every control point, which may not correspond to the visible evaluated points. For NURBS splines the difference may be even more pronounced and the result may not be as expected. A Resample Curve Node node can be used to create a poly spline, where there is a control point for every evaluated point.
### Outputs
#### Factor
The factor of the curve.
#### Length
The length of the curve.
#### Index
The index of the curve.

## Spline Resolution
Retreive the curve resolution. Means the number of spline points.

### Outputs
#### Resolution
The spline resolution.

## Set Curve Normal
Set the evaluation mode for curve normals.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Mode
The evaluation mode for the curve normals.
### Outputs
#### Curve
The curve output.

## Set Curve Radius
Set the curve radius.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Radius
The radius to set.
### Outputs
#### Geometry
Standard geometry output.

## Set Curve Tilt
Controls the tilt angle at each curve control point.
### Input
#### Geometry
The input curve.
#### Selection
Whether or not to change the value on each control point. True values mean the value will be changed, false values mean the value will remain the same.
#### Tilt
The tilt rotation.
### Outputs
#### Curve
Standard geometry output.

## Set Handle Positions
Set the handle positions of bezier curves
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Position
The position of the handle.
### Properties
#### Mode
Left or right handles.
### Outputs
#### Geometry
Standard geometry output.

## Set Handle Type
Sets a handle type for the curve points of a bezier curve. Handle types determines how the interpolation before and after the curve point happens.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Mode
Left or right handles.
#### Handle Type
The different available handle types.

##### Free
The handles can be adjusted individually.

##### Auto
The left and the right handle will always point to each other. The length of the handles will start in equal size.

##### Vector
The handles can be adjusted individually.

##### Aligned
The left and the right handle will always point to each other.
### Output
#### Curve
Standard geometry output.

## Set Spline cyclic
Sets the spline cyclic. Means looping.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Cyclic
Cyclic or not
### Outputs
#### Geometry
Standard geometry output.

## Set Spline Resolution
Sets the resolution of the spline. Means how many evaluated points should be generated on the curve for each control point.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
#### Resolution
The resolution of the spline.
### Outputs
#### Geometry
Standard geometry output.

## Set Spline Type
Change the curve spline type.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Spline Type
The spline type to set the curve to.
Note that when converting from a NURBS spline to a Bézier spline, at least six points are needed. When the number of points is not a multiple of three a full conversion is not possible and the spline has to be truncated.
### Output
#### Curve
Standard geometry output.