7.1.20 Editors - 3D Viewport - Header - Mesh - Weight Paint mode - Weights menu

Weight Paint Mode - Weights Menu

## Legacy submenu
The legacy sub menu contains legacy menu items. These tools exists in the toolbar.
### Sample Weight
Pick the weight under the mouse by a click.
### Sample Group
Pick the group under the mouse by a click.
### Gradient (Linear)
Allows you to draw a gradient at the mesh. Click, drag the mouse, release. The gradient will be applied linear in drag direction.
### Gradient( Radial)
Allows you to draw a gradient at the mesh. Click, drag the mouse, release. The gradient will be applied radial from the mouse position.

## Assign from Bone Envelopes
Weights the vertices from the connected bone envelopes. And takes the distance to the bone envelope into account.
## Assign Automatic from Bones
Weights the vertices connected with the bone. And takes the distance to the bone into account.
### Last Operator Weight from Bones
This last operator is the same for both tools. Assign Automatic from Bones, and Assign from Bone Envelopes.
#### Type
Choose if you want to Assign from Bone Envelopes, or from Bones.

## Normalize All
Normalize all normalizes the weight of all Vertex groups so that the values for the single vertices in the sum is 1.
### Last Operator Normalize all
#### Subset
Subset is a drop-down menu choose the Subset method.
#### Lock Active
Normalize just the other groups. Not the active group.

## Normalize
Normalize normalizes the weight of the current selected Vertex group so that the values for the single vertices in the sum is 1. Means when there is influence from other groups, then those values are kept, but the one for the current group gets lowered so that the sum is 1.

## Mirror
Mirror Vertex Group mirrors Vertex Groups and flips weights and/or names. It only edits selected Vertices. It flips when both sides are selected. Otherwise it copies from Unselected.
### Last Operator Mirror Vertex Group
#### Mirror Weights
With Mirror Weights ticked it mirrors the weights.
#### Flip Group Names
With Flip Group Names ticked it flips the Group names
#### All Groups
Mirrors all Vertex Groups.
#### Topology Mirror
Uses topology based mirroring. This requires matching mirrored topology.

## Invert
Invert inverts the weight painting for the selected vertex group.
### Last Operator Invert Vertex Group
#### Subset
Subset is a drop-down menu choose the Subset method.
#### Add Weights
Add Vertices from Groups that have zero Weighting before inverting.
#### Remove Weights
Remove Vertices from Groups that have zero weight after inverting.

## Clean
Removes Vertex group assignments that are not required from the active vertex group.
### Last Operator Clean Vertex Group
#### Subset
Subset is a drop-down menu choose the Subset method.
#### Limit
Remove weights that are below or equal to the limit value.
#### Keep Single
Keep Vertices assigned to at least one vertex group when cleaning.

## Quantize
Quantize quantizes the weight paint values. It starts with 4 steps. With a step of 1 you have a single vertex color, no matter how you have painted it before.
### Last Operator Quantize Vertex Weights
#### Subset
Subset is a drop-down menu choose the Subset method.
#### Steps
Here you adjust in how many steps the weight paint colors should be divided.

## Levels
Adds some offset to the Weight paint, and multiplys it with some gain.
### Last Operator Levels
#### Subset
Subset is a drop-down menu choose the Subset method.
#### Offset
Here you adjust the offset.
#### Gain
Here you adjust the gain.

## Smooth
Smooths the weight for selected vertices.
### Last Operator Smooth Vertex Weights
#### Subset
Subset is a drop-down menu choose the Subset method.
#### Factor
Here you adjust the factor.
#### Iterations
Here you adjust how many iterations you use.
#### Expand/Contract
Expand or contract the weights.

## Transfer Weights
Transfer weights allows you to transfer weights from one object to another object in the same space. For example to copy the weight of a body shape to a covering cloth.
### Usage
Make sure the target part is at its location.
In Object mode Select the source object(s). Then shift click to select the target object too. This makes the target object the active object
Switch to Weight Paint mode.
Click the Transfer Weight Button, and the weighting should be transferred to the target object.
You can adjust the result in the Last Operator Transfer Mesh Data panel.

### Last Operator Transfer Mesh Data
#### Freeze Operator
Prevent the operator to rerun when you tweak the settings. So that you can tweak many settings at once, then untick to run the operator again.
#### Data Type
A drop down box choose the data type to work with.

#### Create Data
Add Data layers on target object if needed.
#### Vertex Mapping
A drop down box choose the vertex mapping method.
#### Auto Transform
Automatically compute transformation to get the best possible match between source and target object.
#### Object Transform
Calculate the objects in Global space. Unticked means the transfer happens from and to the origin of the objects.
#### Only Neighbor Geometry
Source Objects must be closer than given distance to the target objects.
#### Ray Radius
The ray distance for Only Neighbor Geometry.
#### Source Layers Selection
A drop down box choose the Source Layer selection method.
##### Destination Layers Matching
A drop down box choose the Destination Layers matching.

#### Mix Mode
A drop down box choose the mix mode. That's how the mapping gets transferred into the target object.
#### Mix Factor
The strength of the chosen mix mode.

## Limit Total
Limit the number of deform weights for a vertex by removing the lowest weights. For example when five vertex groups are assigned to one vertice, and you set the limit to 4, then the vertice will just be assigned to the four vertex groups with the highest weight. This is useful for game content where the game engine has a limit for how much bones can be connected to one vertice.
## Last Operator Limit Number of Weights
#### Subset
A drop down box choose to work with the Active Group or All Groups.
#### Limit
Set the limit.

## Set Weight
This tool is just active when you have either Face Selection Masking or Vertex Selection Masking activated.

The tool fills the selection with the current active weight color that you have adjusted in the Brush panel in the Tools tab in the Tool shelf.

## Locks
Locks is a sub menu with which you can modify the vertex group locks in the properties editor.
The names should be self explaining.

### Last Operator Change Lock

#### Action
Choose the locking method again.

#### Mask
Choose what vertex groups should be affected.