12.1.11 Editors - Geometry Nodes Editor - Header - Add Menu - Input - Scene

Detailed table of content

Add menu - Input - Scene

Here you find input nodes.

## Active Camera
The node outputs the the scene's current active camera.
Typical usage would be to connect this node to an Object Info node to
obtain its transform.
### Outputs
#### Active Camera
The active camera.

## Camera Info
The node outputs settings from the chosen camera.
Typical usage would be to connect this node to an Object Info node to
obtain its transform.
### Inputs
#### Camera
The camera object.
### Outputs
### Projection Matrix
The projection matrix.
### Focal length
The focal length.
### Sensor
The sensor size.
### Shift
The camera shift.
### Clip Start
The camera near clipping distance.
### Clip End
The camera far clipping distance.
### Focus Distance
Distance to the focus point for depth of field.
### Is Orthographic
If the camera is using orthographic view.
### Orthographic Scale
The orthographic camera scale in case it is using Orthographic view.

## Collection Info
The Collection Info node retreives information from collections. This can be useful to use an external collection to control parameters in the geometry node tree.
### Inputs
#### Collection
Collection to get the properties from.
#### Separate Children
Output each child of the collection as a separate instance. The output is sorted alphabetically.
##### Reset Children
Reset the transform of every child instance in the output. This setting is just active when Separate Children is active.
### Properties
#### Transform Space
The transformation of the geometry outputs.
#### Original
Output the geometry relative to the collection offset.
#### Relative
Bring the input collection geometry into the modified object, maintaining the relative position between the objects in the scene.
### Outputs
#### Geometry
Geometry of the collection in world space with all its modifiers applied.

## Image Info
Retreive infos from an image.
### Input
#### Image
Load or connect a image.
##### New
Create a new image.
Opens a new image dialog where you can adjust the color, size and further settings.
##### Open
Open a existing image.

##### Image prop
###### Image browser
A list of available images
###### Image name
The name of the image
###### Fake user
Add a fake user to this asset.

###### New
Create a new image.
Opens a new image dialog where you can adjust the color, size and further settings.
###### Open Image
Open a existing image.
###### Remove
Removes the image as the active image.
#### Frame
For videos. Which frame to use.
### Outputs
#### Width
The width of the image.
#### Height
The height of the image
#### Has Alpha
Returns true if the image has an alpha channel
#### Frame Count
For movies. How many frames.
#### FPS
For movies, what FPS rate.

## Is Viewport
The Is Viewport node outputs true when geometry nodes is evaluated for the viewport. For the final render the node outputs false.
### Outputs
#### Is Viewport
A booleran that indicates if the geometry nodes is evaluated for preview.

## Object Info
The Object Info node retreives information from objects. And outputs it then.
### Inputs
#### Object
Object to get the properties from.
### Outputs
#### Transform
Transform matrix output.
#### Location
Location of the object in world space.
#### Rotation
Rotation of the object in world space.
#### Scale
Scale of the object in world space.
#### Geometry
Geometry of the object in world space with all its modifiers applied.

## Scene time
Outputs the current scene time in seconds or in frames.
The Frame output is a float value to make subframe rendering for motion
blur possible.
### Outputs
#### Seconds
Output in seconds.
#### Frame
Output in Frames.

## Self Object
Retreives the parent object of the geometry nodegroup.