12.1.8 Editors - Geometry Nodes Editor - Header - Add Menu - Curve

Detailed table of content

Add menu - Curve

Here you find mainly nodes to convert color values.

## Cuve Length
Retreives the length of a curve.
### Inputs
#### Curve
The input curve.
### Outputs
#### Length
The length of the curve.

## Cuve Reverse
Reverses the direction of the spline. The start point becomes the end point and vice versa. The shape of the spline is not modified.
### Inputs
#### Curve
The input curve.
#### Selection
An optional selection attribute to determine which part of the spline should be reversed.
### Outputs
#### Curve
Standard geometry output.

## Cuve Subdivide
Subdivides the curve. The shape is not changed.
### Inputs
#### Geometry
The input curve.
#### Cuts
The number of cuts per segment.
### Properties
#### Cuts
The cut method.
Integer cuts all sements with the same number of cuts.

Attribute cuts just the segments that are defined by the chosen attribute.

### Outputs
#### Geometry
Standard geometry output.

## Cuve to Mesh
Converts a curve object to a mesh object.
### Inputs
#### Curve
The input curve.
#### Profile Curve
Input profile curve.
### Outputs
#### Mesh
Standard mesh output.

## Cuve to Points
Creates a point geometry along the curve. The generated points have a tangent, normal and rotation attribute that can be used for instancing.
Note that the radius of the generated points is 1/10 of the radius of the curve.
### Inputs
#### Geometry
The input curve.
#### Properties
#### Mode
The sample method.

##### Evaluated
Creates a point geometry at every curve node. It takes the built-in resolution attribute into account. But the result may not have equal distances between the points.
##### Count
Samples the points along the curve. The distance between the points will be equal.
###### Count
The number of points to use.
##### Length
The calculation happens by splitting the spline into segments with the defined length. The length will be rounded down. That way a whole numer of samples will fit in each input spline.
###### Length
The length of each segment.
### Outputs
#### Geometry
Standard mesh output.

## Mesh to Curve
Converts a curve object to a mesh object.
### Inputs
#### Mesh
The input mesh.
#### Selection
A selection of the mesh.
### Outputs
#### Curve
Standard curve output.

## Resample curve
Resmaples a curve object.
### Input
#### Geometry
The input geometry.
#### Count
The resample amount with method Count.
#### Length
The resample amount with method Count.
### Properties
#### Mode
Either use the count of the curve points, or the length of the curve for resampling.
### Output
#### Geometry
Standard geometry output.