Brushes context menus

Call this menu with double right click in the 3D viewport. You need to be in Sculpt mode with a mesh object.

In Sculpt mode you will call a context menu with the sliders from the Brush settings. The content depends of the chosen brush. Every brush has different settings.

## Radius
The Radius edit box allows you to adjust the radius of the brush.
### Size Pressure
The first button behind the edit box enables tablet pressure sensitivity for radius.
### Use Unified Radius
The second button behind the edit box enables global radius size. Any modification at the radius will also modify the radius value for other paint tools.

## Strength
The Strength edit box allows you to adjust the strength of the brush.
### Size Pressure
The first button behind the edit box enables tablet pressure sensitivity for radius.
### Use Unified Radius
The second button behind the edit box enables global radius size. Any modification at the radius will also modify the radius value for other paint tools.

## Autosmooth
The autosmooth edit box allows you to adjust the amout of smoothing that gets automatically applied to each stroke.
### Tablet Pressure
The button behind the edit box enables tablet pressure sensitivity for autosmooth.

## Plane Offset
Clay brush setting. Adjust the plane on which the brush acts towards or away from the objects surface. Sculpting with the Clay brush happens in a plane defined by the view you are in and the first vertices hit by the brush.

## Distance
Adjust the plane trim distance.

## Height
Layer brush setting. The height that can be affected by the layer brush.

## Magnify
Blob Brush setting. The Crease Brush Pinch Factor.

## Pinch
Crease Brush setting. The Crease Brush Pinch Factor.

## Normal Weight
Various brushes like Grab or Elastic Deform. How much grab will pull vertexes out of surface during grab.

## Magnify
Blob Brush setting. The Crease Brush Pinch Factor.

## Rake
Snake Hook brush setting. How much grab will follow cursor rotation.