12.1.14 Editors - Geometry Nodes Editor - Header - Add Menu - Mesh

Detailed table of content

Add menu - Mesh

Nodes to modify the mesh geometry.

## Dual Mesh
The Dual Mesh node calculates the dual of the input mesh. This means that faces get replaced with vertices and vertices with faces.
### Inputs
#### Mesh
The input mesh.
#### Keep Boundaries
Keep the (non-manifold) boundaries of the mesh intact.
### Outputs
#### Dual Mesh
The output mesh.

## Extrude Mesh
Extrudes out geometry at the selection by a given amount.
### Inputs
#### Mesh
The input mesh.
#### Selection
A selection of the mesh.
#### Offset
The offset amount.
#### Offset Scale
The offset scale. Without an offset this is equal the amount.
#### Individual
Just Faces mode. Extrude out individual faces.
### Properties
#### Mode
What kind of elements to extrude out. Vertices, Edges or Faces.
### Outputs
#### Mesh
The output mesh.
#### Top
The top elements of the extrusion.
#### Side
The side elements of the extrusion.

## Flip Faces
Flips the winding order of the selected faces.
Blender developers decided not to call it Flip Normals. Since "normals are
derived data, changing them is only a side effect." However, what the node does is in fact to flip the normals.
### Inputs
#### Mesh
The input mesh.
#### Selection
A selection of the input mesh.
### Outputs
#### Dual Mesh
The output mesh.

## Mesh Boolean
The Boolean Node allows you to cut, subtract, and join the geometry of two inputs. This node offers the same operations as the Boolean modifier.
### Inputs
#### Geometry 1, 2
Standard geometry input.
#### Self Intersect
Allow self intersection.
#### Hole Tolerant
Allow holes.
### Properties
#### Operation
The boolean operation.
##### Intersect
Produce a new geometry containing only the volume inside of both geometry 1 and geometry 2.
##### Union
The two input pieces of geometry are joined, then any interior elements are removed.
##### Difference
Geometry 2 is subtracted from geometry 1 (everything outside of geometry 2 is kept).
### Output
#### Geometry
Standard geometry output.

## Mesh to Curve
Converts a mesh geometry to a curve geometry.
### Inputs
#### Mesh
Input mesh.
#### Selection
A selection of the input mesh.
### Outputs
#### Curve
Standard curve output.

## Mesh to Points
Converts a mesh geometry to a point geometry.
### Inputs
#### Mesh
Input mesh.
#### Selection
A selection of the input mesh.
#### Position
The position of the points.
#### Radius
The radius of the points
### Properties
#### Mode
What geometry to convert to points.

### Outputs
#### Curve
Standard curve output.

## Split Edges
Splits the edges of the geometry.
Note that splitting edges breaks the mesh topology.
### Inputs
#### Mesh
Input mesh.
#### Selection
A selection of the input mesh.
### Outputs
#### Mesh
Standard Mesh output.

## Subdivide Mesh
Subdivides the geometry by a simple division.
### Inputs
#### Geometry
Standard geometry input.
#### Level
To which degree the geometry will be deformed.
### Outputs
#### Geometry
Standard geometry output.

## Subdivision Surface
The Subdivision Surface node subdivides the geometry using Catmull-Clark deformation.
### Inputs
#### Geometry
Standard geometry input.
#### Level
To which degree the geometry will be deformed.
#### Creases
Control how smooth edges should be with Weighted Edge Creases.

### Properties
#### UV Smooth
The methbod to deal with smoothing the UV.

#### Boundary Smooth
Controls if open boundaries and corners are smooth.
### Outputs
#### Geometry
Standard geometry output.

## Triangulate
The Triangulate node triangulates all faces in a mesh.
### Inputs
#### Geometry
Standard geometry input.
#### Minimum Vertices
Minimum number of vertices a face must have to be triangulated. For example, setting this value to 5, will prevent triangulation of Quads and only triangulate N-gons.
### Properties
#### Quad Method
A quad is a polygon with four edges.
##### Beauty
Split the quads in nice triangles, slower method.
##### Fixed
Split the quads on their 1st and 3rd vertices.
##### Fixed Alternate
Split the quads on their 2nd and 4th vertices.
##### Shortest Diagonal
Split the quads based on the diagonal distance between their vertices.
#### Polygon Method
Meant are N-Gons. Faces with more than four edges. Tris, Quads and N-Gons are all Polygons.
##### Beauty
Arrange the new triangles nicely, slower method.
##### Clip
Split the polygons using an ear-clipping algorithm (gives similar results to the tessellation used for the viewport rendering).
### Outputs
#### Geometry
Standard geometry output.

## Scale Elements
Allows to scale the selected elements.
### Inputs
#### Geometry
Standard geometry input.
#### Selection
A selection of the geometry.
#### Scale
The scale factor
#### Center
The center of the scaling.
#### Axis
Scale Mode Single axis only. Scale the selection separately along its single axis.
### Properties
#### Domain
What kind of elements to scale.
#### Scale Mode
Uniform scales uniformly in all three world coordinates.
Single Axis scales separately in the single axis.
### Outputs
#### Geometry
The output geometry.

## Edge Angle
Calculates the angle in radians between two faces that meet at an edge. Without two faces on the edge, the angle will be 0.
### Outputs
#### Unsigned Angle
The unsigned output angle. The shortest angle will be picked.
#### Signed Angle
The signed angle between the two faces, where Convex angles are positive and Concave angles are negative. This calculation is slower than the unsigned angle.

## Edge Neighbours
Outputs the number of faces connected to each edge.
### Outputs
#### Face Count
The number of faces.

## Edge Vertices
Outputs the index and position of the two vertices that defines an edge. Index outputs an integer. Position a vector.
### Outputs
#### Vertex Index 1
The index of the first vertice.
#### Vertex Index 2
The index of the second vertice.
#### Position 1
The position of the first vertice.
#### Position 2
The position of the second vertice.

## Face Area
Gives each face area a unique id. Which can be used in a capture attribute for example, to create instances of other geometry to this now unique face areas.
### Outputs
#### Area
The face area output.

## Face Neighbours
Outputs the number of vertices or faces connected to each face.
### Outputs
#### Vertex Count
The vertex count for the face neighbors.
#### Face Count
The face count for the face neighbors.

## Mesh Island
Outputs a separate index for each mesh island. The indices are based on the order of the lowest-numbered vertex in each island.
### Outputs
#### Index
The index output.

## Is Shade Smooth
Retreives if the geometry is shaded smooth.
### Outputs
#### Smooth
Smooth output.

## Vertex Neighbors
Outputs the number of vertices or faces connected to each vertex.
### Outputs
#### Vertex Count
The vertex count for the vertex neighbors.
#### Face Count
The face count for the vertex neighbors.

## Set Shade Smooth
Retreives if the geometry is shaded smooth.
### Input
#### Geometry
Input mesh.
#### Selection
A selection of the input mesh.
#### Shade Smooth
Set the shading to smooth.
### Outputs
#### Geometry
Geometry output.

Legacy - Mesh

These nodes existed in a former Bforartists version, but are now deprecated. They do not show in the regular menu or UI anymore. And you cannot insert them in a newer Bforartists version. But old projects that uses this nodes still loads with these nodes showing and enabled.

## Edge Split
The Edge Split node splits as split edge marked edges into two edges.
Note that splitting edges breaks the mesh topology.

### Inputs
#### Geometry
Standard geometry input.
#### Edge Angle
When enabled, edges will be split if the angle between its two adjacent faces is greater than the Split Angle.
#### Angle
On 0: all edges are split. On 180: no edges are split.
#### Sharp Edges
When enabled, edges will be split if they were marked as sharp.
### Outputs
#### Geometry
Standard geometry output.

## Subdivision Surface
The Subdivision Surface node subdivides the geometry using Catmull-Clark deformation.
### Inputs
#### Geometry
Standard geometry input.
#### Level
To which degree the geometry will be deformed.
#### Creases
Control how smooth edges should be with Weighted Edge Creases.
### Properties
#### UV Smooth
The methbod to deal with smoothing the UV.

#### Boundary Smooth
Controls if open boundaries and corners are smooth.
### Outputs
#### Geometry
Standard geometry output.