12.1.37 Editors - Geometry Nodes Editor - Header - Add Menu - Volume

Detailed table of content

´

Add menu - Volume

Here you find nodes to modify the volume.

## Volume Cube
The Volume Cube node generates a voxel based volume cube primitive that can be used for volume conversion to mesh in conjunction with the Volume to Mesh node.
### Inputs
#### Geometry
Standard geometry input.
#### Density
Volume density per voxel. Higher values makes it more dense.
#### Background
Value per voxel outside the cube domain.
#### Min:
Minimum boundary of the volume cube.
Max:
Maximum boundary of the volume cube.
Resolution X
Number of volume voxules in the X axis.
Resolution Y
Number of volume voxules in the Y axis.
Resolution Z
Number of volume voxules in the Z axis.

## Volume to Mesh
The Volume to Mesh node generates a mesh on the “surface” of a volume. The surface is defined by a threshold value. All voxels with a larger value than the threshold are considered to be outside.
Note that currently this node only works on volumes generated using geometry nodes.
### Inputs
#### Geometry
Standard geometry input.
#### Density
The density input of the volume object. Either a tag or the information from another node.
#### Threshold
The voxel amount to use.
#### Adaptivity
The input radius.
### Properties
#### Resolution
Base the voxel resolution at the gridsize, the amount or the size of the point cloud.

### Output
#### Geometry
Standard geometry output.