12.1.44 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities - Bundle

Detailed table of content

Add menu - Bundle

Bundles are like packed containers—they let you group multiple values (like vectors, floats, booleans) into a single wire. Think of them as a way to package data together and pass it around cleanly.

## Combine Bundle
This node takes multiple inputs and wraps them into a single bundle.
### Inputs
#### Sockets
This is a dynamic socket that will populate with whatever you want to plug into it for later use. Accepts one or more bundle-compatible data streams.
These could represent attributes, geometry sets, vales, vectors, or grouped attributes depending on context.
### Outputs
#### Bundle Socket
Standard bundle socket with a unified bundle containing all input elements. Use this to pass the packeged sockets to a Seperate Bundle node for later user down the node tree lines.

## Separate Bundle
This node unpacks a bundle back into its individual components.
### Inputs
The inputs of the node are dynamic. Some inputs are only available in certain operations. For instance, the Scale input is only available in the Scale operator.
#### Bundle
Standard bundle socket with a unified bundle containing all input elements from a Combine Bundle node.
### Outputs
#### Sockets
This is a dynamic series of socket that will populate with whatever is available from the incoming bundle line. Ouptuts one or more bundle-compatible data streams.
These could represent attributes, geometry sets, vales, vectors, or grouped attributes depending on context.