12.1.58 Editors - Geometry Nodes Editor - Header - Add Menu - Hair - Utility

Detailed table of content

Add menu - Hair - Utility

Hair nodes are Node Groups found in the Essentials Library included with Bforartists. They differ from the other nodes in the add menu due to being mid level node groups instead of individual low level nodes.

You can enter the node tree by clicking at the icon up right. Tab to leave the node tree. And you can of course also edit the node tree.

## Attach Hair Curves to Surface
Attaches hair curves to a surface mesh.
### Input
#### Geometry
The input geometry.
#### Surface Object
A surface object to attach to. It needs to have matching transforms.
#### Surface
Surface geometry to attach hair curves to.
#### Surface UV Map
Surface UV Map used to attach hairs to.
#### Surface Rest Position
Set the surface into rest position before attachment.
#### Sample Attachment UV
Sample the surface UV mapp at the attachment point.
#### Snap to Surface
Snap the root of the curve to the closest surface point.
#### Align to Surface Normal
Align the curves to surface normals. Needs a guide as reference.
#### Blend along Curve
Blend deformation along eacah curve from the root.
### Output
#### Geometry
The output geometry.
#### Surface UV Coordinate
Surface UV Coordinate at the attachment point.
#### Surface Normal
Surface Normal at the attachment point.
## Redistribute Curve Points
Redistributes existing control points evenly along each curve.
### Input
#### Curves
The input curve.
#### Factor
Factor to blend overall effect.
#### Feature Awareness
Use simple feature awareness to keep feature definition.
### Output
#### Curves
The output curves.
## Restore Curve Segment Length
### Input
#### Curves
The input curve.
#### Selection
A selection of the input curve.
#### Factor
Factor to blend overall effect.
#### Reference Position
Reference position before deformation.
#### Pin at Parameter
Pin each curve at a certain point for the operation.
### Output
#### Curves
The output curves.