12.1.8 Editors - Geometry Nodes Editor - Header - Add Menu - Curve

Detailed table of content

Add menu - Curve

Here you find mainly nodes to convert color values.

## Cuve Endpoints
Extracts the start and endpoints of a curve.
### Inputs
#### Geometry
The input curve.
### Outputs
#### Start Points
The start points.
#### End Points
The end points.

## Cuve Fill
Fills the curve with mesh geometry.
### Inputs
#### Curve
The input curve.
### Properties
#### Mode
#### Triangles or N-gons
Fill the curve with either triangles, or use N-Gon geometry
### Outputs
#### Mesh
The output as mesh.

## Cuve Length
Retreives the length of a curve.
### Inputs
#### Curve
The input curve.
### Outputs
#### Length
The length of the curve.

## Cuve Reverse
Reverses the direction of the spline. The start point becomes the end point and vice versa. The shape of the spline is not modified.
### Inputs
#### Curve
The input curve.
#### Selection
An optional selection attribute to determine which part of the spline should be reversed.
### Outputs
#### Curve
Standard geometry output.

## Cuve Subdivide
Subdivides the curve. The shape is not changed.
### Inputs
#### Geometry
The input curve.
#### Cuts
The number of cuts per segment.
### Properties
#### Cuts
The cut method.
Integer cuts all sements with the same number of cuts.

Attribute cuts just the segments that are defined by the chosen attribute.

### Outputs
#### Geometry
Standard geometry output.

## Cuve to Mesh
Converts a curve object to a mesh object.
### Inputs
#### Curve
The input curve.
#### Profile Curve
Input profile curve.
### Outputs
#### Mesh
Standard mesh output.

## Cuve to Points
Creates a point geometry along the curve. The generated points have a tangent, normal and rotation attribute that can be used for instancing.
Note that the radius of the generated points is 1/10 of the radius of the curve.
### Inputs
#### Geometry
The input curve.
#### Properties
#### Mode
The sample method.

##### Evaluated
Creates a point geometry at every curve node. It takes the built-in resolution attribute into account. But the result may not have equal distances between the points.
##### Count
Samples the points along the curve. The distance between the points will be equal.
###### Count
The number of points to use.
##### Length
The calculation happens by splitting the spline into segments with the defined length. The length will be rounded down. That way a whole numer of samples will fit in each input spline.
###### Length
The length of each segment.
### Outputs
#### Geometry
Standard mesh output.

## Curve Trim
The Curve Trim node shortens each spline in the curve by removing sections at the start and end of each spline.
Bézier splines will still output as Bézier splines. The first and last control point and its handles will be moved as necessary to preserve the shape. But NURBS splines will be transformed into poly splines in order to be trimmed.
### Inputs
#### Curve
Standard geometry input with a curve component.
#### Start
The factor or length used to determine where to start each output spline.
#### End
The factor or length used to determine where to end each output spline.
### Properties
#### Mode
How to find endpoint positions for the trimmed spline.
##### Factor
The endpoint positions of each spline’s length is determined by a factor. The input values should be between 0 or 1.
##### Length
The endpoint positions of each spline is determined by a length from the start of each spline. The input values should be between 0 and the length of the splines.
### Outputs
#### Curve
Standard geometry output.

## Mesh to Curve
Converts a curve object to a mesh object.
### Inputs
#### Mesh
The input mesh.
#### Selection
A selection of the mesh.
### Outputs
#### Curve
Standard curve output.

## Resample curve
Resmaples a curve object.
### Input
#### Geometry
The input geometry.
#### Count
The resample amount with method Count.
#### Length
The resample amount with method Length.
### Properties
#### Mode
The resample mode.
##### Evaluated
Use the resolution attribute for spline and bezier curves.
##### Count
Use the count of the curve points.
##### Length
Use the length of the curve.
### Output
#### Geometry
Standard geometry output.

## Select by Handle Type
Select curbe points by their handle type.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Left / Right
Wether to check for the type of handles.
#### Handle Type
What handle type to compare.

### Output
#### Curve
Standard geometry output.

## Set Handle Type
Sets a handle type for the curve points. Handle types determines how the interpolation before and after the curve point happens.
### Input
#### Curve
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Update Handles
If the handles are updated at the left side of the input curve, the right side of the input curve, or at both sides.
#### Handle Type
The different available handle types.

##### Free
The handles can be adjusted individually.

##### Auto
The left and the right handle will always point to each other. The length of the handles will start in equal size.

##### Vector
The handles can be adjusted individually.

##### Aligned
The left and the right handle will always point to each other.
### Output
#### Curve
Standard geometry output.

## Set Spline Type
Change the curve spline type.
### Input
#### Geometry
The input curve.
#### Selection
A selection of the input curve.
### Properties
#### Spline Type
The spline type to set the curve to.
### Output
#### Curve
Standard geometry output.