26.9.2 Editors - Properties Editor - Modifiers Properties Tab - Grease Pencil - Generate Modifiers

Detailed table of content

Grease Pencil - Generate modifiers

Some of the modifiers are just available for specific object types.
Left grease pencil object, right a mesh object.

## Array
The Array modifier creates an array of copies of the base object. Each copy can offset from the previous one in any of a number of possible ways. Vertices in adjacent copies can be merged if they are nearby, allowing smooth Subdivision Surface frameworks to be generated.
This modifier can be useful when combined with tillable meshes for quickly developing large scenes. It is also useful for creating complex repetitive shapes.
Multiple Array modifiers may be active for an object at the same time. This allows to create complex three-dimensional constructs.
Hint for Offset Calculation. The transformation applied from one copy to the next is calculated as the sum of the three different components (Relative, Constant and Object), each of which can be enabled/disabled independently of the others. This allows, for example, a relative offset of (1.0, 0.0, 0.0) and a constant offset of (0.1, 0.0, 0.0), giving an array of objects neatly spaced along the X axis with a constant 0.1 unit between them, whatever the original object’s size.

### Count
Number of Items

### Material Override
Index of the material used for generated strokes. A value of 0 uses the original material.

### Relative Offset subpanel
#### Factor X/Y/Z
Adds a translation equal to the object’s bounding box size along each axis to the offset, multiplied by a scaling factor. X, Y and Z scaling factors can be specified.

### Constant Offset subpanel
#### Distance X/Y/Z
Adds a constant translation component to the duplicate object’s offset. X, Y and Z constant components can be specified.
### Object Offset subpanel
Adds a transformation taken from a chosen object relative to the current object to the offset.
#### Object
Choose an object.
### Randomize
Randomize the transform values.
#### Offset
Randomize the offset values.
#### Rotation
Randomize the rotation values.
#### Scale
Randomize the scale values.
##### Uniform Scale
Use uniform scaling.
#### Seed
The random seed value.
### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Inverse Layers
Inverts the influence.
#### Pass
The layer pass index.
##### Inverse Pass
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert Materials
Inverts the influence.
#### Pass
The material pass index.
##### Inverse Pass
Inverts the influence.

## Build
The Build modifier lets the strokes of the grease pencil object appear or disappear over time when you play the animation.

### Mode
How many strokes are animated at the same time.
#### Sequential
Strokes appear or disappear one after the other.
#### Concurrent
All strokes appear or disappear at once.
##### Time Alignment
When strokes should start to appear or disappear.
###### Align Start
All strokes appears at the same time.
###### Disappear
All strokes disappears at the same time.
### Transition
How the strokes are animated. The items should be self explaining.
### Start delay
Number of frames after each GP keyframe before the modifier has any effect.
### Frames
Maximum number of frames that the build effect can run.
### Use Factor
Use a factor instead fixed frames. Turning on Use Factor will turn off Start Delay and Frames.
### Custom Range
Only modify strokes that lies in the specified time frame.
#### Start
The first frame of the range.
#### End
The last frame of the range.
### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Inverse Layers
Inverts the influence.
#### Pass
The layer pass index.
##### Inverse Pass
Inverts the influence.

## Dot Dash
Turns a grease pencil stroke into a dotted line.
### Offset
The offset into each stroke before the dot creation starts.
### Segment list
Manage the single segments of the dotted dash. Segments gets repeated as they appear in the list. Means when you just have one segment in the list, then this shape will be repeated. When you have two, then the first will be displayed, then the second, then the first, and so on. Every segment can have its own settings. Which are managed below.
#### Add Segment
Add a new dash segment.
#### Remove Segment
Remove the dash segment.
#### Move Dash Segment up or down
Moves the selected dash segment up or down in the list.
#### Search element
By clicking at the triangle button you reveal a search field with which you can search through the list.
##### Edit Box
Type in the search term and hit enter.
##### Invert
Inverts the search term.
##### Sort by name
Sorts the list alphabetically.
##### Reverse
Inverts the list.
### Dash
The number of points (vertices) from the orignal stroke to include in this segment.
### Gap
The number of points (vertices) skipped after this segment.
### Radius
The radius of the segment. Maximum is 1 of the original stroke.
### Opacity
The visibility of this segment.
### Material Index
What material to use.
### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Inverse Layers
Inverts the influence.
#### Pass
The layer pass index.
##### Inverse Pass
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert Materials
Inverts the influence.
#### Pass
The material pass index.
##### Inverse Pass
Inverts the influence.

## Length
The Length Modifier extends or shortens the original strokes length.

### Mode
Defines the mode to use for the length calculation. Relative to the length of the grease pencil stroke, or absolute in geometry space.
### Factor Start/End
Length difference for each stroke.
### Used Length
What position of the stroke is used for the calculation of the extension.
### Curvature subpanel
Follow the curvature of the stroke.
#### Point Density
Multiplied by Start/End for the total added point count.
#### Segment Influence
How much the length of the individual segments should influence the final computed curvature.
#### Filter Angle
Ignore points of the stroke that derivate from their neighbours by more than this angle.
#### Invert
Invert the curvature of the stroke's extension.
### Random Offset subpanel
Randomization for the start / end lengths.
#### Random offset Start
Size of random length added to the start of each stroke.
#### Random offset End
Size of random length added to the end of each stroke.
#### Random Noise Offset
Smoothly offset the random value of each stroke.
#### Seed
The random seed value.
#### Randomize subpanel
Use random values over time.
##### Step
Number of frames before recalculate random values again.

### Influence subpanel
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Inverse Layers
Inverts the influence.
#### Pass
The layer pass index.
##### Inverse Pass
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert Materials
Inverts the influence.
#### Pass
The material pass index.
##### Inverse Pass
Inverts the influence.

## Line Art
The Line Art modifier generates stylized line art from the scene or selected source collection or objects.
Note that due to lack of global cache at the moment, each Line Art modifier will run the entire occlusion calculation for itself. So if you have multiple line art modifiers to select different parts of the scene (to apply different styles, etc.), the evaluation will take much longer. There are plans to remedy this in the future, but this is a known limitation for now.

### Source Type
What type of geometry source should line art be generated from.

#### Collection
##### Collection
The collection where you want to apply the line art to.
###### Invert
Inverts the selection of collections.
##### Layer
Grease Pencil layer that is assigned to the generated strokes.
##### Material
Grease pencil material assigned to the generated strokes.
#### Object
##### Object
The object where you want to apply the line art to.
##### Layer
Grease Pencil layer that is assigned to the generated strokes.
##### Material
Grease pencil material assigned to the generated strokes.
#### Scene
Applies the line art grease pencil strokes to the whole scene.
##### Layer
Grease Pencil layer that is assigned to the generated strokes.
##### Material
Grease pencil material assigned to the generated strokes.

### Edge types subpanel
Which kind of edges to influence. The names from contour to intersections should be pretty self explaining.
#### Crease
Influence crease edges. The angle what edges are treaten as creases can be adjusted in the edit box.
#### Allow Overlap
Allow an edge to have multiple overlapping types.

### Geometry Processing subpanel

#### Custom Camera
Allows to pick a different camera than the active scene camera for line art rendering.
#### Remove Doubles
Perform an “merge by distance” operation when loading geometry into Line Art. The threshold of this operation is internally set to a value that is optimal for Line Art algorithm precision.
#### Overlapping Edges as Contour
This option allows overlapping edges (e.g. from an edge split modifier or imported geometry where two edges occupy the exact same space) to be drawn as contour. Enabling this option will slow down the calculation slightly but it will handle edge overlapping cases without erroneous occlusion results.
#### Instanced Objects
This option enables particles and other instanced objects to be loaded for line art calculation. There will be performance impact when there are a large amount of instanced objects in the scene.
#### Clipping Boundaries
When enabled, line art will generate clipping lines as contour type at the place where near or far clipping planes cut the model. Otherwise there will be no lines.
#### Crease on Smooth
Allow crease edges to show inside smooth surfaces.
#### Crease on Sharp
Allow crease to show on sharp edges.
#### Back Face Culling
Remove all backfaces to speed up calculation.

### Style Subpanel
#### Thickness
The strokes generated by line art are given this thickness.
#### Opacity
The strokes generated by line art are given this Opacity.

### Occlusion Subpanel
#### Range
If enabled, the modifier will select lines that have an occlusion level between start and end values.
If not enabled just a single Level value slider shows.
#### Material Mask
Use material masks to filter out occluded strokes. You need to have a range level higher than 0.
##### Masks
Choose up to eight mask bits for the masking.
##### Exact match
Require matching all material masks instead of just one.

### Intersection subpanel
#### Collection Masks
Choose up to eight mask bits for masking.
##### Exact match
Require matching all intersections instead of just one.

### Face Mask Filtering subpanel
Filter Feature Lines using Freestlye Face Masks.
#### Invert
Invert face mask filtering.
#### Boundaries
Filter feature lines based on face mask boundaries.
#### Keep Contour
Preserve contour lines while filtering.

### Chain
#### Intersection with Contour
Allows intersection lines to be chained together with contour lines.
#### All Lines
Enabling this option will cause all lines to have the type of contour and to be chained together.
#### Loose Edges
Allow loose edges to be chained together.
#### Loose As Contour
Loose edges will have contour type.
#### Preserve Details
Keep the zig-zag noise in initial chanining.
##### Geometry Space
Use Geometry distance for chaining instead of image space.
#### Image Threshold
Segments with an image distance smaller than this value will be chained together.
#### Smooth tolerance
Strength of smoothing applied on jagged chains.
#### Angle Splitting
The angle in screen space below which a stroke is split into two.

### Vertex Weight Transfer subpanel
#### Filter Source
If source mesh has vertex groups whose name starts with this string, then the vertex weight info will be transferred into weight groups in Grease Pencil strokes.
##### Invert Vertex Group
Inverts the selection.
#### Match Output
Transfer the filtered object vertex weights into Grease Pencil weight groups with the same names as the filtered ones.
#### Target
If Match Output is off, then a target vertex group has to be specified. If there are multiple weight groups copied into target, then the highest weight value is copied into it.

### Composition
#### Overscan
A margin to prevent an abrupt end of the stroke at the edge of the image.
##### Image boundary trimming
Trim all edges right at the boundary of image (including overscan region)
#### Depth Offset
Move strokes slightly towards the camera to avoid clipping.
##### Towards custom camera
Offset strokes towards selected camera instead of the active camera.

### Bake subpanel
#### Bake Line Art / Bake Line Art (All)
Bakes Line Art strokes for active Grease Pencil object within the start, end frame range in scene.
Bake Line Art (All) bakes all Grease Pencil objects that contains at least one Line Art modifier. After baking, baked Line Art modifier will be deactivated automatically.
#### Clear Baked Line Art / Clear Baked Line Art ( All)
Clears baked line art frames within the scene frame range for active Grease Pencil object.
Clear Baked Line Art (All) applies the same operation for all Grease Pencil objects that contains at least one Line Art modifier.

## Mirror
The Mirror modifier for the Grease Pencil Object works in Object mode. It mirrors the object along its local X, Y and/or Z axes, across the Object Origin. It can also use another object as the mirror center, then use that object’s local axes instead of its own.
### Object
Define an object to mirror at its origin instead of mirroring along the grease pencil origin.
You can animate it to move the mirror axis.
### Influence
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Pass
The layer pass index.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Pass
The material pass index.
##### Invert
Inverts the influence.

## Multiple Strokes
Adds multiple parallel copies of the stroke around the original stroke.
### Duplicates
The number of additional strokes.
### Distance
Distance between the original and the duplicate strokes.
### Offset
Control the offset position (inner or outer) for duplicate strokes.
### Fade
Fade out duplicate strokes, using their opacity or thickness.
#### Center
Control the initial position for the fading.
#### Thickness
Fade influence on strokes thickness.
#### Opacity
Fade influence on strokes opacity.
### Influence
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Pass
The layer pass index.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Pass
The material pass index.
##### Invert
Inverts the influence.

## Simplify
The Simplify modifier allows you to reduce the amount of points in the strokes. It tries to reduce points while maintaining the lines shape.
### Mode
How to reduce points in the strokes.
#### Fixed
Deletes alternated points in the strokes, except the start and end points.
#### Adaptive
Uses the RDP algorithm (Ramer-Douglas-Peucker algorithm) for points deletion. The algorithm try to obtain a similar line shape with fewer points.
#### Sample
Recreates the stroke geometry with a predefined length between points.
#### Merge
Simplifies the strokes by merging points that are closer than a specified distance to each other.
#### Iterations
Number of times to repeat the procedure.
### Influence
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Pass
The layer pass index.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Pass
The material pass index.
##### Invert
Inverts the influence.

## Subdivide
The Subdivide modifier subdivide the strokes by inserting points between other points to the lines.

### Subdivision Type
#### Catmull-Clark
Subdivides and smooths the surfaces.
#### Simple
Only subdivides the surfaces, without any smoothing.
### Subdivisions
Number of subdivisions.
### Influence
#### Layer
Restricts the effect only to one layer or to any layers that share the same pass index. Click to pick the layer that you want to use.
##### Invert
Inverts the influence.
#### Pass
The layer pass index.
##### Invert
Inverts the influence.
#### Material
Restricts the effect only to material that share the same material or pass index. Click to pick the material that you want to use.
##### Invert
Inverts the influence.
#### Pass
The material pass index.
##### Invert
Inverts the influence.