12.1.11 Editors - Geometry Nodes Editor - Header - Add Menu - Input

Detailed table of content

Add menu - Input

Here you find input nodes.

## Collection Info
The Collection Info node retreives information from collections. This can be useful to use an external collection to control parameters in the geometry node tree.
### Inputs
#### Collection
Collection to get the properties from.
### Properties
#### Transform Space
The transformation of the geometry outputs.
#### Original
Output the geometry relative to the collection offset.
#### Relative
Bring the input collection geometry into the modified object, maintaining the relative position between the objects in the scene.
### Outputs
#### Geometry
Geometry of the collection in world space with all its modifiers applied.

## Is Viewport
The Is Viewport node outputs true when geometry nodes is evaluated for the viewport. For the final render the node outputs false.
### Outputs
#### Is Viewport
A booleran that indicates if the geometry nodes is evaluated for preview.

## Material
Retreive a material.
### Outputs
#### Material
The material output.

## Object Info
The Object Info node retreives information from objects. And outputs it then.
### Inputs
#### Object
Object to get the properties from.
### Outputs
#### Location
Location of the object in world space.
#### Rotation
Rotation of the object in world space.
#### Scale
Scale of the object in world space.
#### Geometry
Geometry of the object in world space with all its modifiers applied.

## Random Float
The Random Float generates a random (floating point) value from a given range.
### Inputs
#### Min
Minimum random value.
#### Max
Maximum random value.
#### Seed
The random seed.
### Outputs
#### Value
The random generated value.

## String
Input a string.
### Properties
#### String
The string that you want to input.
### Outputs
#### Value
The value set in the node properties.

## Value
Input numerical values to other nodes in the tree.
### Properties
#### Value
Single numerical value (floating point).
### Outputs
#### Value
The value set in the node properties.

## Vector
Creates a single vector of three values that can be used as an input.
Properties
### X Y Z
The values of the vector.
### Output
#### Vector
Standard vector output.