12.1.13 Editors - Geometry Nodes Editor - Header - Add Menu - Mesh

Detailed table of content

Add menu - Mesh

Nodes to modify the mesh geometry.

## Boolean
The Boolean Node allows you to cut, subtract, and join the geometry of two inputs. This node offers the same operations as the Boolean modifier.
### Inputs
Geometry 1, 2
Standard geometry input.
### Properties
#### Operation
The boolean operation.
##### Intersect
Produce a new geometry containing only the volume inside of both geometry 1 and geometry 2.
##### Union
The two input pieces of geometry are joined, then any interior elements are removed.
##### Difference
Geometry 2 is subtracted from geometry 1 (everything outside of geometry 2 is kept).
### Output
#### Geometry
Standard geometry output.

## Edge Split
The Edge Split node splits as split edge marked edges into two edges.
Note that splitting edges breaks the mesh topology.

### Inputs
#### Geometry
Standard geometry input.
#### Edge Angle
When enabled, edges will be split if the angle between its two adjacent faces is greater than the Split Angle.
#### Angle
On 0: all edges are split. On 180: no edges are split.
#### Sharp Edges
When enabled, edges will be split if they were marked as sharp.
### Outputs
#### Geometry
Standard geometry output.

## Mesh Subdivide
Subdivides the geometry by a simple division
### Inputs
#### Geometry
Standard geometry input.
#### Level
To which degree the geometry will be deformed.
### Outputs
#### Geometry
Standard geometry output.

## Subdivision Surface
The Subdivision Surface node subdivides the geometry using Catmull-Clark deformation.
### Inputs
#### Geometry
Standard geometry input.
#### Level
To which degree the geometry will be deformed.
#### Creases
Control how smooth edges should be with Weighted Edge Creases.
#### Boundary Smooth
Controls if open boundaries and corners are smooth.
#### Smooth UVs
Controls if subdivision smooth is applied to UVs.
### Outputs
#### Geometry
Standard geometry output.

## Triangulate
The Triangulate node triangulates all faces in a mesh.
### Inputs
#### Geometry
Standard geometry input.
#### Minimum Vertices
Minimum number of vertices a face must have to be triangulated. For example, setting this value to 5, will prevent triangulation of Quads and only triangulate N-gons.
### Properties
#### Quad Method
A quad is a polygon with four edges.
##### Beauty
Split the quads in nice triangles, slower method.
##### Fixed
Split the quads on their 1st and 3rd vertices.
##### Fixed Alternate
Split the quads on their 2nd and 4th vertices.
##### Shortest Diagonal
Split the quads based on the diagonal distance between their vertices.
#### Polygon Method
Meant are N-Gons. Faces with more than four edges. Tris, Quads and N-Gons are all Polygons.
##### Beauty
Arrange the new triangles nicely, slower method.
##### Clip
Split the polygons using an ear-clipping algorithm (gives similar results to the tessellation used for the viewport rendering).
### Outputs
#### Geometry
Standard geometry output.