12.1.40 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities - Rotation

Detailed table of content

Add menu - Utilities - Rotation

Utility nodes are mainly for mathematical operations.

## Align Rotation to Vector
Aligns a rotation to a vector.
### Inputs
#### Rotation
The input euler rotation vector.
#### Factor
The factor to align the euler value to the vector.
#### Vector
The vector to align to.
### Properties
#### Align Axis
To which axis to align the vector.
#### Pivot
The pivot axis.

### Output
#### Rotation
The output rotation euler angle.

## Axes to rotation
Creates a rotation from a primary and a secondary axis. The axis should be ideally orthogonal.
### Inputs
#### Primary Axis
The axis to rotate around.
#### Secondary Axis
The secondary axis that gives the alignment.
### Properties
#### Primary axis
Which axis to rotate around.
#### Secondary Axis
Which axis to align to.
### Output
#### Rotation
The output rotation euler angle.

## Align Euler to Vector (Deprecated)
Aligns a euler value to a vector.
### Inputs
#### Rotation
The input euler rotation vector.
#### Factor
The factor to align the euler value to the vector.
#### Vector
The vector to align to.
### Properties
#### Align Axis
To which axis to align the vector.
#### Pivot
The pivot axis.

### Output
#### Rotation
The output rotation euler angle.

## Axis Angle to Rotation
Converts an axis angle to a rotation.
### Inputs
#### Axis
The input axis.
#### Angle
The input angle.
### Output
#### Rotation
The output rotation value.

## Euler to Rotation
Converts an euler angle to a rotation.
### Inputs
#### Euler
The input euler angle vector.
### Output
#### Rotation
The output rotation value.

## Invert Rotation
Inverts a rotation
### Inputs
#### Rotation
The input rotation vector.
### Output
#### Rotation
The output rotation value.

## Rotate Rotation
Rotates an euler rotation by another euler rotation.
### Inputs
#### Rotation
Use the rotation of an existing geometry.
#### Rotate By
The input rotation.
### Properties
#### Rotate Space
##### Global
Rotate by the global orientation
##### Local
Rotate by the local orientation
### Outputs
#### Rotation
The euler angle output.

## Rotate Euler (Deprecated)
Rotates an euler rotation. This node will be removed in the near future. Alternatively use the Rotate Rotation node.
### Inputs
#### Rotation
Use the rotation of an existing geometry.
#### Rotate By
The input rotation.
### Properties
#### Rotate Type
##### Axis Angle
Rotate around an axis by an angle.
##### Euler
Rotate around the x, y and z axis.
#### Rotate Space
##### Object
Rotate points in the local space of the object.
##### Point
Rotate every point in its local space.
### Outputs
#### Rotation
The euler angle output.

## Rotate Vector
Rotates a vector
### Inputs
#### Vector
The input vector.
#### Rotation
The input rotation.
### Output
#### Rotation
The output rotation value.

## Rotate Vector
Rotates a vector.
### Inputs
#### Vector
The input vector.
#### Rotation
The input rotation.
### Output
#### Rotation
The output rotation value.

## Rotation to Euler
Converts a rotation vector to euler angle.
### Inputs
#### Rotation
The input rotation.
### Output
#### Euler
The output euler angle.

## Rotation to Quaternion
Converts a rotation vector to a quaternion.
### Inputs
#### Rotation
The input rotation.
### Output
#### W, X, Y, Z
The single output values of the quaternion.

## Quaternion
Converts a rotation vector to a quaternion.
### Inputs
#### W, X, Y, Z
The single input values of the quaternion.
### Output
#### Rotation
The output rotation.