Mask Menu

## Transform
### Move
Move the selected curve spline or points.
#### Last Operator Move
##### Values
Adjust the move amount.
X, Y and Z defines the position.
##### Axis Ortho
Along which axis to move
##### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the transform action.

##### Proportional Editing
Proportional Editing is a drop-down box where you can choose to use proportional editing. When you choose one of the active methods then the neighbour geometry gets influenced too in a proportional way.

###### Proportional Editing Falloff
Proportional Editing Falloff is a drop-down box where you can choose a method for the falloff for the proportional editing.
###### Proportional size
Proportional size is a edit box where you can adjust the strength of the Proportional falloff.
###### Connected
Just edit geometry that is directly connected with the current selection. 4 Bforartists 2 Reference Manual - 7.1.4 Editors - 3D View - Header - Navigation Menu
###### Projected ( 2D)
Edit geometry that is in 2d space aligned with the current selection. This one goes from the current view in depth direction.
### Rotate
Rotate the selected curve spline or points.
#### Last Operator Rotate
##### Angle
Adjust the angle.
##### Axis
Along which axis to rotate
##### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the transform action.

##### Proportional Editing
Proportional Editing is a drop-down box where you can choose to use proportional editing. When you choose one of the active methods then the neighbour geometry gets influenced too in a proportional way.
###### Proportional Editing Falloff
Proportional Editing Falloff is a drop-down box where you can choose a method for the falloff for the proportional editing.
###### Proportional size
Proportional size is a edit box where you can adjust the strength of the Proportional falloff.
###### Connected
Just edit geometry that is directly connected with the current selection. 4 Bforartists 2 Reference Manual - 7.1.4 Editors - 3D View - Header - Navigation Menu
###### Projected ( 2D)
Edit geometry that is in 2d space aligned with the current selection. This one goes from the current view in depth direction.
### Scale
Scale the selected curve spline or points.
#### Last Operator Resize
##### Scale X Y Z
Adjust the scaling.
##### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the transform action.

##### Proportional Editing
Proportional Editing is a drop-down box where you can choose to use proportional editing. When you choose one of the active methods then the neighbour geometry gets influenced too in a proportional way.
###### Proportional Editing Falloff
Proportional Editing Falloff is a drop-down box where you can choose a method for the falloff for the proportional editing.
###### Proportional size
Proportional size is a edit box where you can adjust the strength of the Proportional falloff.
###### Connected
Just edit geometry that is directly connected with the current selection. 4 Bforartists 2 Reference Manual - 7.1.4 Editors - 3D View - Header - Navigation Menu
###### Projected ( 2D)
Edit geometry that is in 2d space aligned with the current selection. This one goes from the current view in depth direction.
### Scale Feather
Scale feather weight for the selected points.
The curve type that is used to create mask splines is almost a Bézier curve. But it has some differences. Smooth edges of the mask are defined by feathering. The curve needed to support feathering in a way that stuck to the curve as you edited it, for ease of editing an animation. These are called S-Curves.
Besides the handles, every control point also has points that define the feather between the current point and the next point on the spline. Each feather point is stored in UV space, where U means position across spline segment, and V means distance between main spline and feather points.
#### Last Operator Transform
##### Values
Here you can adjust the scale amount.
X, Y and Z defines the position. W defines the rotation.
##### Axis
Around which axis to rotate. X, Y or Z.
##### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the transform action.

##### Proportional Editing
Proportional Editing is a drop-down box where you can choose to use proportional editing. When you choose one of the active methods then the neighbour geometry gets influenced too in a proportional way.
###### Proportional Editing Falloff
Proportional Editing Falloff is a drop-down box where you can choose a method for the falloff for the proportional editing.
###### Proportional size
Proportional size is a edit box where you can adjust the strength of the Proportional falloff.
###### Connected
Just edit geometry that is directly connected with the current selection. 4 Bforartists 2 Reference Manual - 7.1.4 Editors - 3D View - Header - Navigation Menu
###### Projected ( 2D)
Edit geometry that is in 2d space aligned with the current selection. This one goes from the current view in depth direction.
### Clear Feather Weight
Reset the feather weight to zero.

## Duplicate
Duplicates the selected curve and moves it.
## Delete
Deletes the selected mask curve point.
## Copy Splines
Copies the currently selected spline.
## Paste Splines
Pastes a copied spline.
## Make Parent
Set the mask's parenting.
## Clear Parent
Clears the mask's parenting.
## Toggle Cyclic
Make the spline closed or open.
## Switch Direction
A spline has a direction. A starting point and an endpoint. Here you can switch the direction in which the spline points. The starting point becomes the end point, the end point becomes the starting point.
## Recalc Normals
Recalculate the direction of the selected spline handlers.
## Set Handle Type
In this sub menu you can set the handle type for the currently selected spline points.

## Animation
### Insert Shape Key
Inserts a shape key keyframe.
The inserted keyframes can then be found in the dopesheet editor in mask mode.
### Clear Shape Key
Clears an existing shape key keyframe.
### Reset Feather Animation
Resets the feather offset across all animated frames.
### Re-key Shape points
Recalculate animation data on selected points for frames selected in the dopesheet.

## Show / Hide
### Show Hidden
Reveals all hidden curves
### Hide Selected
Hides the selected curve.
### Hide Unselected
Hides the unselected curves.
#### Last operator Hide Layer
##### Unselected
Hide selected or unselected curves.