12.1.43 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities - Vector

Detailed table of content

Add menu - Vector

Vector nodes are for calculating vector operations.

## Vector Curves
The Vector Curves node maps an input vector components to a curve.
### Inputs
#### Factor
Standard vector input.
#### Vector
Standard vector input.
### Properties
#### Channel
#### Channel buttons
X, Y, Z. Clicking on one of the channels displays the curve for each.

#### Curve edit field
Create and tweak a Bezier curve that varies the input levels (X axis) to produce an output level (Y axis).
##### Selecting Points
You can select curve points. This reveals two edit boxes for the x and y coordinate of this point.
Selected points can be moved around. Left click at them, hold the mouse button down and move them to a new location.

##### Adding Points
You can add new curve points by simply left clicking at the curve. Move the mouse to position them where you need it.

##### Navigation elements
The navigation elements at the top are described from left to right.
###### Zoom in and out
The two buttons with the magnifying glass at it zooms in and out in the curve window.

##### Tools
Tools is a menu where you can find some curve related tools.
###### Reset View
Resets the curve windows zoom.
###### Vector Handle
Set handle type to Vector.
###### Auto Handle
Set handle type to Auto.
###### Auto Clamped Handle
Set handle type to Auto Clamped.
###### Extend horizontal
Extends the curve before the first curve point and behind the last curve point horizontally.
###### Extend extrapolated
Extends the curve before the first curve point and behind the last curve point extrapolated.
###### Reset Curve
Resets the curve to the initial shape.

##### Use Clipping
Clipping options. Set up clipping for the stroke.
##### Delete Points
Deletes selected curve points.

### Outputs
#### Vector
Standard vector output.

## Vector Math
The Vector Math node performs the selected math operation on the input vectors.
### Inputs
The inputs of the node are dynamic. Some inputs are only available in certain operations. For instance, the Scale input is only available in the Scale operator.
#### Vector
Input vector A.
#### Vector
Input vector B.
#### Scale
Input Scale.
### Properties
#### Operation
The vector math operator to be applied on the input vectors.

### Outputs
The output of the node is dynamic. It is either a vector or a scalar depending on the operator. For instance, the Length operator have a scalar output while the Add operator have a vector output.
#### Vector
Output vector.
#### Value
Output value.

## Vector Rotate
The Vector Rotate node allows rotations by a vector.
### Inputs
The inputs of the node are dynamic. Some inputs are only available in certain operations. For instance, the Angle input is just available with the Axis Angle type.
#### Vector
Input vector.
#### Center
Input Center
#### Axis
Input Axis.
#### Angle
Input Angle
### Properties
#### Type
The rotation type.

### Outputs
#### Vector
The Output vector.

## Combine XYZ
The Combine XYZ Node combines a vector from its individual components.
### Input
#### X Y and Z
X, Y and Z values.
### Output
#### Color
Color output.

## Mix Vector
Allows to mix values and vectors in various ways. The node has three different modes. Float, Vector and Color. This here is the node in Vector mode.

### Input
#### Factor
The mix factor. With mode Uniform it is a single value. With mode Non Uniform it is a vector.

#### A
Vector A input.
#### B
Vector B input.
### Properties
#### Data Type
Which mode to use. We cover here the Vector mode.

#### Factor Mode
Use a single value or a vector for the factor.
### Output
#### Result
The output value or vector.

## Separate XYZ
The Separate XYZ Node splits a vector into its individual components.
### Input
#### Vector
The Input vector.
### Output
#### X, Y and Z
The output vectors for X, Y and Z.