20.3.2 Editors - NLA Editor - Sidebar - Strip tab

Strip Tab

The settings for the currently selected action strip. You need to have a action strip selected to show this tab.

## Name
The name of the currently selected action strip.
To rename the strip click into the edit field, change the name and press enter.
## Mute
Disable the action strip.

Active Strip panel

## Frame Start + End
The start and end position of the strip.
## Extrapolation
Action to take for gaps past the strip extents.
### Hold
Affects both sides of the strip. This should only be set on the very first strip.
### Hold Forward
Affects the region after the clip, only. This can be set on any strip.
### Nothing
Affects only the region of the strip itself. This can be set on any strip.

## Blending
Affects how the property values directly produced by the strip are combined with the result of evaluating the stack below. The bottom-most strip is blended on top of the default values of the properties.
### Replace
The top strip is linearly blended in with the accumulated result according to influence, completely overwriting it if influence is set to 100%.
### Combine
Depending on the type of each property, one of the following methods is automatically chosen:
Axis/Angle Rotation
result=previous+value*influence
This results in averaging the axis and adding the amount of rotation.
Quaternion Rotation
Quaternion math is applied to all four channels of the property at once:
result=previous×valueinfluence
Proportional (Scale)
result=previous*(value/default)influence
Others
result=previous+(value-default)*influence
This allows layering actions that can also be used as a standalone. Properties keyframed at their default values remain at default.
### Add, Subtract, Multiply
The result of the strip is multiplied, subtracted, or added to the accumulated results, and then blended in according to influence.
result=mix(previous,previous(+-*)value,influence)
## Blend In + Out
Number of frames to fade in or out the action strip.
## Auto Blend In/Out
Number of frames for blending in and out is automatically calculated from overlapping strips.
## Playback
### Reversed
The action strip is played in reversed order. This just works when timing is determined automatic.
### Cyclic Strip Time
Cycle the action strip.
## Animated Influence subpanel
Control the influence settings by an F-Curve instead of automatically determined. The F-Curve can be edited in the Graph Editor.
### Influence
The influence value.
### Animate Property
Set or remove a keyframe at current position.
## Animated Strip Time subpanel
Control the Strip time settings by an F-Curve instead of automatically determined. The F-Curve can be edited in the Graph Editor.
### Influence
The influence value.
### Animate Property
Set or remove a keyframe at current position.

Action Clip panel

This represents the ‘object data’ of the strip. Much like the transform values of an object.

## Action
The action that is referenced in the strip. This can be changed to replace the current strip’s value with another Action in the scene.
## Slot
Define which subset is meant for this strip.
## Frame Start / End
The start and end frame values of the strip.
Note. To loop the animation you might need to reduce the End Frame by one frame to have a loopable animation.
Note. If you select values that are above or below the actual keyframe count of the Action, then the F-curve Extrapolation will be applied.

## Sync Length
Set the Start and End Frames to the first and last keyframed frames of the Action.
## Now
Causes the Start and End Frames, above, to be reset to the first and last keyframed frames of the Action.
## Playback Scale
Stretches the strip.
## Repeat
Repeats the strip by the chosen value. With a value of 1 the strip plays once.

Action panel

## Manual Frame Range
Set the playback frame range manually.
### Start
The start frame.
### End
The end frame.
## Cyclic Animation
Make the animation loop.