7.0.1 Editors - 3D Viewport - Object mode - Object Context Menu

Detailed table of content

Object Context Menu

Call this menu with double right click in the 3D viewport. You need to be in Object mode.
The Object Context Menu appears in object mode with all object types. Even without any object in the scene.
The content of this menu differs. With a mesh object you have for example smoothing available too. And with a curve object the convert options.

Object Context Menu - All objects

This content shows with all object types.
## Copy Objects
Copies the selected object(s).
## Paste Objects
Pastes copied object(s).
### Last Operator Paste Selection from Buffer
#### Select
Select pasted object(s).
#### Active Collection
Put the pasted objects into the active collection.
## Duplicate Objects
Duplicates selected objects. The copy is completely independent. All containing data gets duplicated too. And you can edit the object instances completely independent. then.
You are automatically in grab mode, and so you can easily move the object out of position. Which is sometimes wanted, since you can position the duplicate then. But sometimes this is unwanted. A right click after releasing the mouse lets the object snap back into its creation position.
When you drag the duplicate around you will see the position values in the header.
### Last Operator Duplicate
#### Duplicate Objects
##### Linked
With this option ticked the duplication happens with linked data.
#### Move X , Y , Z
The Position of the duplicated object.
#### Orientation
Orientation is a drop-down box choose the type of orientation for the duplicate action.

#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Adjust the falloff methods.
##### Proportional Size
See and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.
## Duplicate Linked
Duplicates selected objects. The instance has its own transforms. But the duplicate shares some data with the first instance. This means when you for example edit the mesh of one of the instances, then the other instance gets modified too. As you can see this in the screenshot. Here you can also see that the mesh name is the same. The object name is different though.

If you want to make changes to an object in the new linked duplicate independently of the original object, then you will have to manually make the object a “single-user” . This can be done for example in the Outliner, in the right click menu of the object. (Currently broken). Or in the Object menu. Choose what attached data you want to make single user.

When you duplicate an object, then you are automatically in grab mode. And so you can easily move the object out of position. which is sometimes wanted, since you can position the duplicate then. But sometimes this is unwanted. A right click after releasing the mouse lets the object snap back into its creation position.
Duplicate linked instances the object data.
Explanation: Each Bforartists object type (mesh, lamp, curve, camera etc.) is composed from two parts: an Object and Object Data (sometimes abbreviated to ObData):
Object - Holds information about the position, rotation and size of a particular element.
Object Data - Holds everything else. For example. Meshes stores geometry, material lists, vertex groups, etc. . Cameras stores focal length, depth of field, sensor size, etc. .
Each object has a link to its associated object-data, and a single object-data, like a material, may be shared by many objects.
### Last Operator Duplicate Linked
#### Duplicate Objects
##### Linked
With this option ticked the duplication happens with linked data.
#### Move X, Y, Z
The Position of the duplicated object.
#### Orientation
Orientation is a drop-down box choose the type of orientation for the duplicate action.

#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Adjust the falloff methods.
##### Proportional Size
See and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.
## Rename active Item / Object
Allows you to rename the currently active item or object. A rename dialog will pop up where you can type in a new name for the current item. You can have more than one item selected. Just the active item gets renamed.

## Mirror
Mirrors the selection.

### Interactive Mirror
Mirrors the selection.
#### Usage:
Activate the tool. In the header you will now see further instructions. Which is: type in the axis at which you want to mirror. Interactive mirroring starts in Global space. You can change the orientation in the last operator.
### X Y Z Global
Mirrors along the global axis.
### X Y Z Local
Mirrors along the object axis.
### Last Operator Mirror
#### Orientation
Choose the orientation in which the transform should happen.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Adjust the falloff methods.
##### Proportional Size
See and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.
## Snap
### Selection to Cursor
Snaps the currently selected object(s) to the cursor location.
### Selection to Cursor(Keep Offset)
Snaps the currently selected object(s) to the cursor location, but keeps the offset of the selected objects to each other. Means the center of the current selection goes to cursor position. Not every individual object.

#### Last operator Snap Selection to Cursor
##### Offset
Keep the offset of the selected objects to each other.
### Selection to Active
Snaps the currently selected object(s) to the active object.
### Selection to Grid
Snaps the currently selected object(s) to the nearest grid point.

### Cursor to Selected
Moves the cursor to the center of the selected object(s).
### Cursor to World Origin
Moves the cursor to the world origin.
### Cursor to Active
Moves the cursor to the center of the active object.
### Cursor to Grid
Moves the cursor to the nearest grid point.

## Parent
The parent menu provides you with all parenting methods at object level.
To use parenting you first have to select the source object, hold down shift, then select the target object so that both are selected. This also works in the outliner (here you can also simply hold down shift and drag the source object at the target object to make it a child). The source object becomes the child object then.

The methods are object type dependent. The armature methods requires to have a mesh and an armature. The path methods a curve. The available methods for the current selection can also be found out by pressing the hotkey ctrl P. This calls the parenting menu with just the available methods.

### Object
Sets the parent to selected object.
### Object ( Keep Transform)
Sets the parent to selected object, but applies all transform before the operation.

Armature parenting creates an armature modifier at the mesh.
### Armature Deform
Sets the parent to selected Armature.
### With empty Groups
Sets the parent to selected Armature, using empty groups.
### With Envelope Weights
Sets the parent to selected Armature, using envelope weights
### With automatic Weights
Sets the parent to selected Armature, with automatic weights.
### Bone
Sets the parent absolute to selected Bone.
### Bone Relative
Sets the parent relative to selected Bone.

### Curve Deform
allows you to deform a mesh by a curve shape. It adds a curve modifier at the mesh.
Usage:
Create a curve. Bend it in edit mode to your needs. Create a mesh. I have for demonstration purposes created a cylinder with several subdivisions.

To demonstrate the only pitfall, by parenting the center of the object goes to the start point of the curve. So you better put the origin at the bottom of the cylinder before parenting.

### Follow Path

Attaches an object to a curve. The curve then gets used to animate the object position. Every vertice of the curve is one key frame.
Create a curve, create an object, hold down shift and select the curve, make parent ...
Take care of the position and rotation of the object before parenting it to the curve. It influences how the object behaves.
There is a constraint with the same name and functionality. But parenting with follow path will not create such a constraint.

### Path Constraint

Path constraint adds a AutoPath constraint at the mesh object, which is most probably a wrong labeled path constraint. It is not documented by the Blender developers.

Create a curve, create an object, hold down shift and select the curve, make parent ...
Take care of the position and rotation of the object before parenting it to the curve. It influences how the object behaves.

### Lattice Deform

Parents a lattice object to the object.
You need a lattice object and a mesh object. Lattice deformations just works with mesh objects.
Create a lattice, create an object, hold down shift and select the lattice, make parent ...
Parent the mesh object to the lattice object with method Lattice Deform. A Lattice Deform constraint will be added at the mesh object.
Take care of the position and size of the lattice object. It influences how the deformation works.
Enter Edit Mode with the lattice object. Deform it. The mesh object will follow the deformation.

### Vertex
Vertex parents the current object to a vertex of the target object. The vertex will be chosen automatically, it's the

closest vertice of the parent object. When you want to assign the object to a specific vertice, then you have to do
The vertex parenting in Edit mode. You need to have an object type that has vertices. Mesh or curve.
Create a mesh or curve object, create an object, hold down shift and select the mesh object, make parent ...

### Vertex (Triangle)
Vertex (Triangle) parents the current object to a face of the target object. The face will be chosen automatically.

It's the closest face of the parent object. When you want to assign the object to a specific face, then you have to
Do the vertex parenting in Edit mode. You need to have an object type that has vertices. Mesh or curve.
Create a mesh or curve object, create an object, hold down shift and select the mesh object, make parent ...

### Make Parent without Inverse
With normal parenting the child object keeps its world transformation.
Without inverse parenting the child object uses the coordinate system of the parent object. As one of the effects you will see that the child objects will jump to the origin of the parent object when parenting.
### Make Parent without Inverse (Keep Transform )
Set the object’s parenting without setting the inverse parent connections and applies all transform before the operation. Without inverse parenting the child object uses the coordinate system of the parent object. By keeping the transform, the origin of the parent and child object stay in position.
### Object (Attach Curves to Surface)
Parent a Hair Curve to the surface of a new object.

### Last Operator Make Parent
#### Type
Choose the make parent method again. This last operator counts for most of the parent actions.
#### Keep Transform
Apply transform before parenting.

### Clear Parent
Clear Parent clears the parent relation completely, including involved modifiers.

#### Clear and Keep Transformation
Clear Parent clears the parent relation completely, including involved modifiers.
But keeps the current visual transformation.
#### Clear Parent Inverse
Clear Parent Inverse resets the transform corrections applied to the parenting relationship. It does not remove
the parenting itself.
#### Last Operator Clear Parent

Change the type of clearing.

## Move to Collection
Moves the selected object to a collection. The object is removed from the collection it was in.
By clicking at this menu item a popup will appear choose the new collection. Allows also to create a new collection. Once done, the object will be moved to this new created collection.
This operator can also be found in the Header Object menu.
### Last Operator Move to Collection
#### Name
Set a name for your new collection. When you haven't created a new collection, then this name stays blank.
## Toggle Local View
Toggles local view isolating the selection in the viewport. You can find this operator in the Header View menu.
## Remove from Local
Removes the selection from the Local View keeping the unselected items in the viewport.
You can find this operator in the Header View menu.
Note: This is a conditional operator that only shows when the context of the 3D View editor is in the Local View mode.
## Insert Key frame
Calls the Insert Key frame menu
The keying set defines what kind of key frames gets recorded. When you start with an
animation, and your object does not have a keying set yet, then you will be prompted with a menu choose the proper keying set. The Insert Key frame menu.
Note that this just adds a keying set to the current key frame. And not to the whole object. That's why the keying set menu down right stays empty when you add a key frame. this way.

## Delete
Deletes the selected object(s).
## Show/Hide
Sub-menu with shows or hide selection, unselected or hidden operators.
### Show Hidden
Makes all geometry in the scene visible again.
### Hide Selected
Hides the selected geometry.
#### Last Operator Hide Selected
##### Unselected
Hides the not selected geometry.
### Hide Unselected
Hides the not selected geometry. The selected geometry stays visible.

Mesh object

## Shade Smooth
Sets the shading for the object to smooth. Smooth means that the sharp edges are no longer seen.

## Shade Auto Smooth
Sets the shading for the object to smooth with Autosmooth activated. Autosmooth means that sharp edges above an angle threshold will have sharp faceted faces, meanwhile angles under the threshold will be smooth.
## Shade Flat
Sets the shading for the object to flat. Flat means that every face of the object shows faceted, with a sharp edge.

## Convert to
### Curve
Converts a selected Mesh or Text Object to a Curve Object.
### Mesh
Converts a selected object to a Mesh Object.
### Grease Pencil
Converts a selected curve to a grease pencil stroke.
### Point Cloud
Converts a selected object to a point cloud object.
### Last Operator Convert to
#### Target
Target is a drop-down box that allows you to choose the convert method again.
#### Keep Original
With this option ticked the original object gets kept. And a new object gets created.

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.

### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Curve object

## Shade Smooth
Sets the shading for the object to smooth. Smooth means that the sharp edges are no longer seen.

## Shade Auto Smooth
Sets the shading for the object to smooth with Autosmooth activated. Autosmooth means that sharp edges above an angle threshold will have sharp faceted faces, meanwhile angles under the threshold will be smooth.
## Shade Flat
Sets the shading for the object to flat. Flat means that every face of the object shows faceted, with a sharp edge.

## Adjust Extrusion
Extrudes a surface out of a curve or text object.

In the header you can see the height of the extrusion. In the Transform panel in the sidebar you can adjust this height also afterwards. The Z value.
## Adjust Offset
Adjust Offset is just of interest when you have an extruded surface at the curve. It scales the surface size in x and z direction.

## Convert to
### Curve
Converts a selected Mesh or Text Object to a Curve Object.
### Mesh
Converts a selected object to a Mesh Object.
### Grease Pencil
Converts a selected curve to a grease pencil stroke.
### Point Cloud
Converts a selected object to a point cloud object.
### Last Operator Convert to
#### Target
Target is a drop-down box that allows you to choose the convert method again.
#### Keep Original
With this option ticked the original object gets kept. And a new object gets created.

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.
Surface object

## Shade Smooth
Sets the shading for the object to smooth. Smooth means that the sharp edges are no longer seen.

## Shade Auto Smooth
Sets the shading for the object to smooth with Autosmooth activated. Autosmooth means that sharp edges above an angle threshold will have sharp faceted faces, meanwhile angles under the threshold will be smooth.
## Shade Flat
Sets the shading for the object to flat. Flat means that every face of the object shows faceted, with a sharp edge.

## Convert to
### Curve
Converts a selected Mesh or Text Object to a Curve Object.
### Mesh
Converts a selected object to a Mesh Object.
### Grease Pencil
Converts a selected curve to a grease pencil stroke.
### Point Cloud
Converts a selected object to a point cloud object.
### Last Operator Convert to
#### Target
Target is a drop-down box that allows you to choose the convert method again.
#### Keep Original
With this option ticked the original object gets kept. And a new object gets created.

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Metaball object

## Convert to
### Curve
Converts a selected Mesh or Text Object to a Curve Object.
### Mesh
Converts a selected object to a Mesh Object.
### Grease Pencil
Converts a selected curve to a grease pencil stroke.
### Point Cloud
Converts a selected object to a point cloud object.
### Last Operator Convert to
#### Target
Target is a drop-down box that allows you to choose the convert method again.
#### Keep Original
With this option ticked the original object gets kept. And a new object gets created.

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Text object

## Adjust Extrusion
Extrudes a surface out of a curve or text object.
In the header you can see the height of the extrusion. In the Transform panel in the sidebar you can adjust this height also afterwards. The Z value.
## Adjust Offset
Width size is just of interest when you have an extruded surface at the curve. It scales the surface size in x and z direction.

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Volume object

Just default settings.

Grease Pencil object

## Convert to
### Path
Converts a grease pencil stroke to a path.
### Bezier Curve
Converts a grease pencil stroke to a bezier curve.
### Polygon Curve
Converts a grease pencil stroke to a polygon curve.

### Last Operator Convert Grease Pencil

#### Type
Type is a drop-down box that allows you to choose the convert method again.
#### Bevel Depth
A curve can have a extruded geometry with bevel. Adjust the bevel depth.
#### Bevel Resolution
A curve can have a extruded geometry with bevel. Adjust the bevel resolution.
#### Normalize Weight
Normalize the weight, set from stroke width.
#### Radius Factor
Multiplier for the points radii, set from stroke width.
#### Link Stroke
Link strokes with zero radius sections of curves.

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Armature

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Lattice

## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.
### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.

Empty + Image object

The Image object types is a special kind of an empty. So they have the same entry in the context menu.

## Adjust Empty Display Size
Scale the size of the empty in the viewport.
Note, this value does not show elsewhere. And there is no way to reset it to the default size except to scale it again with Empty Draw Size. The value in the header will help you.

Speaker object

Just default settings.

Camera object

## Adjust Focal Length
Changes the focal length of the camera. You can adjust it afterwards in the properties editor.

## Adjust Focus Distance
Changes the focus distance for depth of field. You can adjust it afterwards in the properties editor. The values in the depth of field are not as exact as the dof distance values though.

Object specific - Light object

There are four different light types. Each light type has its own settings. Power is the same in all. When you adjust the values then you will see a string with the values in the header.

## Point light

### Adjust Light Power
Adjust the power of the light. The light power setting is in the properties editor in the light panel in the object data properties tab.

### Adjust Light Radius
Adjust the radius of the point light.

## Sun light

### Adjust Light Power
Adjust the power of the light. The light power setting is in the properties editor in the light panel in the object data properties tab.

### Adjust Sun Light Angle
Adjust the angle of the sun light.

## Spot light

### Adjust Light Power
Adjust the power of the light. The light power setting is in the properties editor in the light panel in the object data properties tab.

### Adjust Light Radius
Adjust the radius of the light.

### Adjust Spot Light Size
Adjust the angle of the spotlight beam. Note that the value in the header is in radians, while the value in the panel is in degrees.

### Adjust Spot Light Blend
Adjust softness of the spotlight edge.

## Area light

### Adjust Light Power
Adjust the power of the light. The light power setting is in the properties editor in the light panel in the object data properties tab.

### Adjust Area Light Size
Area light only.
Scale the size of the area light. Size Y appears with Shape Rectangle.

Light Probe object

Just default settings.

Force Field

The force field is displayed as an empty.

## Adjust Empty Display Size
Scale the size of the empty in the viewport.
Note, this value does not show elsewhere. And there is no way to reset it to the default size except to scale it again with Empty Draw Size. The value in the header will help you.

Collection Instance

## Adjust Empty Display Size
Scale the size of the empty in the viewport.
Note, this value does not show elsewhere. And there is no way to reset it to the default size except to scale it again with Empty Draw Size. The value in the header will help you.
## Set Origin
### Geometry to Origin
Sets the geometry to origin.
### Origin to Geometry
Sets the origin to geometry.
### Origin to 3D cursor
Sets the origin to the 3D cursor.
### Origin to Center of Mass(Surface)
Sets the origin to the center of mass, calculating it from the center of the surface area.
### Origin to Center of Mass(Volume)
Sets the origin to the center of mass, calculating from the center of the Volume. It must be manifold geometry with consistent normal's.

### Last Operator Set Origin
The last operator is the same for all set origin methods.
#### Type
Choose the method again.
#### Center
Use the median center or the bounds center for calculation.