12.1.23 Editors - Geometry Nodes Editor - Header - Add Menu - Mesh - Read

Detailed table of content

Add menu - Mesh - Read

Nodes to modify the mesh geometry.

## Edge Angle
Calculates the angle in radians between two faces that meet at an edge. Without two faces on the edge, the angle will be 0.
### Outputs
#### Unsigned Angle
The unsigned output angle. The shortest angle will be picked.
#### Signed Angle
The signed angle between the two faces, where Convex angles are positive and Concave angles are negative. This calculation is slower than the unsigned angle.

## Edge Neighbours
Outputs the number of faces connected to each edge.
### Outputs
#### Face Count
The number of faces.

## Edge Vertices
Outputs the index and position of the two vertices that defines an edge. Index outputs an integer. Position a vector.
### Outputs
#### Vertex Index 1
The index of the first vertice.
#### Vertex Index 2
The index of the second vertice.
#### Position 1
The position of the first vertice.
#### Position 2
The position of the second vertice.

## Edges to Face Group
Group Faces into regions, surrounded by the selected boundary edges.
### Inuputs
#### Boundary Edges
The input edges.
### Outputs
#### Face Group ID
The output face group.

## Face Area
Gives each face area a unique id. Which can be used in a capture attribute for example, to create instances of other geometry to this now unique face areas.
### Outputs
#### Area
The face area output.

## Face Group Boundaries
Find edges on the boundaries between face sets
### Inputs
### Face Set
The input face sets to calculate the boundaries from.
### Outputs
#### Boundary Edges
The edges that lies on the boundaries between the different face sets
#### Face Count
The face count for the face neighbors.

## Face Neighbours
Outputs the number of vertices or faces connected to each face.
### Outputs
#### Vertex Count
The vertex count for the face neighbors.
#### Face Count
The face count for the face neighbors.

## Face Sets – Tool Mode
Get each face’s sculpt face set value to use in the geometry node tree.
This node is only available in the Tool Mode for Node Group Tools assets.
### Outputs
#### Face Set
A face set ID output as integer fields.
#### Exists
A boolean field output that shows where a face set exists or not.

## Is Face Planar
Returns true if all of the points of the evaluated face are on the same plane.
### Inputs
#### Threshold
The threshold to consinder the points to be at the same plane.
### Outputs
#### Planar
True if the face is planar.

## Is Face Smooth
Retreives if the face is shaded smooth.
### Outputs
#### Smooth
Smooth output.

## Is Edge Smooth
Retreives if the edge is shaded smooth.
### Outputs
#### Smooth
Smooth output.

## Mesh Island
Outputs a separate index for each mesh island. The indices are based on the order of the lowest-numbered vertex in each island.
### Outputs
#### Index
The index output.

## Shortest Edge Path
Calculates the shortest path from multiple start points.
### Input
#### End Vertex
The last point of the path.
#### Edge Cost
The amount of calculation to find the shortest path.
### Outputs
#### Next Vertex Index
The vertices index of the shortest path.
#### Total Cost
The calculation amount.

## Vertex Neighbors
Outputs the number of vertices or faces connected to each vertex.
### Outputs
#### Vertex Count
The vertex count for the vertex neighbors.
#### Face Count
The face count for the vertex neighbors.