13.1.16 Editors - Compositor Editor - Header - Node menu

Node menu

This menu contains further node functionality.
## Move
Moves the selected nodes.
## Rotate
You can't rotate single nodes, obviously. But when you have more than one selected then you can rotate them around their center point.
## Resize
You can't resize single nodes, obviously. But when you have more than one selected then you can scale them around their center point.

## Copy
Copies the selected node(s).
## Paste
Pastes the selected node(s).

## Duplicate Keep Input
This works at nodes that have a connected input. Duplicating will keep the input connections established in the duplicated node. The output connections will be removed.
## Duplicate
Duplicates the selected node(s). All connections will be removed in the duplicated node.
## Duplicate Linked
Duplicates the selected node(s), but not their node trees.
## Delete
Deletes the selected node(s).
## Delete with Reconnect
Deletes the selected node(s). When this node is in the middle of a connection, then the connections will be reconnected.

## Join new Frame
Frame node functionality. Adds the selected node to a frame.
## Remove from Frame
Frame node functionality. Removes the selected node from a frame.
## Frame Make Parent
Frame node functionality. Adds the selected node to a frame.

## Links
### Make Links
Tries to connect nodes where it makes sense. For example, the BSDF output of a Principled shader with the Surface input of the Material Output node.
### Make and Replace Links
Same as Make Links. But it will replace existing links.
### Detach Links
Removes all connections from the selected node, but tries to reconnect the remaining nodes.
### Detach Links Move
Removes all connections from the selected node by dragging.
### Mute Links
Mute links with the mouse.

## Separate
Node group functionality. You need to be in edit group mode.
### Copy
Copies the selected node, and pastes a copy of it outside of the node group. The node group remains unchanged.
### Move
Moves the selected to outside of the node group, and removes it from the node group.

## Hide / Toggle
Here you find hide options to make the display of nodes more compact.

Demonstration happens at an image node.

### Hide
Hides everything but input and output dots. To view the full node again perform the operator again. It's a toggle. Or click at the triangle left besides the node name.
### Toggle Node Mute
Deactivates the node.
### Toggle Node Preview
This is a compositor feature for the preview image. It does not belong here, but shares the same menu. It shows or hides the preview image.
### Toggle hidden node sockets
Toggles away the unused node sockets. In this case the vector input node socket and the alpha output node socket will be hidden.

### Toggle Node Options
Hides away the properties.
### Collapse and Hide Unused Sockets
Like Hide. Hides everything but the node sockets. But it also hides the unused node sockets.