F-Curve Tab - Active F-Curve Panel

This panel displays the properties for the active F-Curve.

Note that you need to have a channel selected to reveal the tabs.

## Channel Name
The name of the currently active F-Curve channel.
## RNA Path
RNA Path to property. This is a read only information.
## RNA Array Index
The RNA Array Index to the specific property affected by the F-Curve if applicable. This is a read only information.
## Display Color
With what colors to display the curves. User defined allows you to choose a custom color for the curve. A color field appears. The other methods works random.
## Handle Smoothing
Select the method to compute automatic Bezier Handles.
### None
Only directly adjacent key values are used when computing the handles. Vector handles points directly at the adjacent keyframes.
### Continuous Acceleration
Also keyframes behind the next or previous keyframe gets used for calculation. Which results in a smoother curve.

F-Curve Tab - Active Keyframe Panel

## Interpolation
Set the interpolation type for this keyframe.
## Key Frame
The current position of this keyframe.
## Value
The Y value of this keyframe.
### Left Handle Type / Right Handle Type
Set the handle type. The handles of a keyframe can be independent. Some constellations just works with some other constellations.
#### Free
Move and adjust the handles independently.
#### Aligned
With the left handler the right handler moves too.
#### Vector
Creates a curve with straight lines.
#### Automatic
Creates a smooth curve.
#### Auto Clamped
Creates a smooth curve that only changes the direction at other curve points. It is clamped to prevent overshoots in the curve shape.
### Frame
The current frame of this handle.
### Value
The current Y position of this handle.