12.1.8 Editors - Geometry Nodes Editor - Header - Add Menu - Input - Scene

Detailed table of content

Add menu - Input - Scene

Here you find input nodes.

## Cursor
The Cursor Geometry node gets the 3D Cursor location and rotation, for tool execution. Useful for creating tools with the 3D Cursor input from user.
Note that this node just shows with geometry nodes type Tool.
### Outputs
#### Location
The location of the scene’s 3D cursor, in the local space of the modified object.
#### Rotation
The rotation of the scene’s 3D cursor, in the local space of the modified object.

## Active Camera
The node outputs the the scene's current active camera.
Typical usage would be to connect this node to an Object Info node to
obtain its transform.
### Outputs
#### Active Camera
The active camera.

## Collection Info
The Collection Info node retreives information from collections. This can be useful to use an external collection to control parameters in the geometry node tree.
### Inputs
#### Collection
Collection to get the properties from.
### Properties
#### Transform Space
The transformation of the geometry outputs.
#### Original
Output the geometry relative to the collection offset.
#### Relative
Bring the input collection geometry into the modified object, maintaining the relative position between the objects in the scene.
### Outputs
#### Geometry
Geometry of the collection in world space with all its modifiers applied.

## Image Info
Retreive infos from an image.
### Input
#### Image
Load or connect a image.
##### New
Create a new image.
Opens a new image dialog where you can adjust the color, size and further settings.
##### Open
Open a existing image.

##### Image prop
###### Image browser
A list of available images
###### Image name
The name of the image
###### Fake user
Add a fake user to this asset.

###### New
Create a new image.
Opens a new image dialog where you can adjust the color, size and further settings.
###### Open Image
Open a existing image.
###### Remove
Removes the image as the active image.
#### Frame
For videos. Which frame to use.
### Outputs
#### Width
The width of the image.
#### Height
The height of the image
#### Has Alpha
Returns true if the image has an alpha channel
#### Frame Count
For movies. How many frames.
#### FPS
For movies, what FPS rate.

## Is Viewport
The Is Viewport node outputs true when geometry nodes is evaluated for the viewport. For the final render the node outputs false.
### Outputs
#### Is Viewport
A booleran that indicates if the geometry nodes is evaluated for preview.

## Named Layer Selection
Output a selection of a grease pencil layer by attribute name
### Inputs
#### Name
The layer name attribute.
### Outputs
#### Selection
The selected layer

## Object Info
The Object Info node retreives information from objects. And outputs it then.
### Inputs
#### Object
Object to get the properties from.
### Outputs
#### Transform
Transform matrix output.
#### Location
Location of the object in world space.
#### Rotation
Rotation of the object in world space.
#### Scale
Scale of the object in world space.
#### Geometry
Geometry of the object in world space with all its modifiers applied.

## Scene time
Outputs the current scene time in seconds or in frames.
The Frame output is a float value to make subframe rendering for motion
blur possible.
### Outputs
#### Seconds
Output in seconds.
#### Frame
Output in Frames.

## Self Object
Retreives the parent object of the geometry nodegroup.

## Viewport Transform
Gets and retreives the view direction and location from the 3D Viewport.
### Outputs
#### Projection
Outputs the 3D Viewport’s perspective or orthographic projection matrix as a matrix transform value.
#### View
Outputs the view direction and location of the 3D Viewport as a matrix transform value.
#### Is Orthographic
Outputs a boolean to show if the camera is orthographic with a true or false value.