12.1.40 Editors - Geometry Nodes Editor - Header - Add Menu - Utilities

Detailed table of content

Add menu - Utilities

Utility nodes are mainly for mathematical operations.

## Random Value
Generates a random value.
### Input
##### Min
The minimum value of the range. This input is only available for Float, Integer, and Vector types.
##### Max
The maximum value of the range. This input is only available for Float, Integer, and Vector types.
##### ID
An ID to drive the random number generator seed. By default, this input uses the same value as if the ID Node, which is the id attribute of the context geometry if it exists, and otherwise the index.
##### Seed
The random seed for the random number generation.
### Properties
#### Data Type
What kind of random value to create. The items should be self explaining.
### Output
#### Value
The output value.

## Switch
Switch between two inputs values based on a boolean.
### Inputs
#### Switch
The boolean switch.
#### A
The input value A. Used when the switch is off.
#### B
The input value B. Used when the switch is on.

### Properties
#### Input Type
What input type the values are, which defines what type to output then.

### Outputs
#### Output
Numerical value output.