12.1.24 Editors - Geometry Nodes Editor - Header - Add Menu - Mesh - Sample

Detailed table of content

Add menu - Mesh - Sample

Nodes to modify the mesh geometry.

## Sample Nearest Surface
Calculate the interpolated value of a mesh attribute on the closest point of its surface.
### Inputs
#### Mesh
Input mesh.
#### Value
The value to calculate.
#### Group ID
Is evaluated on the face domain, and splits the input mesh into multiple parts, each with its own id.
#### Sample Position
The sample position to calculate.
#### Sample Group ID
Determines in which group the closest nearest surface is detected.
#### Properties
##### Data Type
Which data to calculate.

### Outputs
#### Value
The output value.
#### Is Valid
Wether the sampling was successful. It is false when the sampled group is empty.

## Sample UV Surface
Calculate the interpolated value of a mesh attribute at a UV coordinate.
### Inputs
#### Mesh
Input mesh.
#### Value
The value to calculate.
#### Source UV Map
The input UV map.
#### Sample UV
The sample position to calculate.
#### Properties
##### Data Type
Which data to calculate.

### Outputs
#### Value
The output value.
#### Is Valid
Wether the node could find a single face to sample at the uv coordinate.