Detailed Table of content

Introduction

The 3D View is made of several areas.

Yellow is the Tool Shelf.
Blue is the Header or Menu bar. It can be at the top or the bottom.

Green is the Viewport. Here you will see and work with your 3D data.

Red is the Properties Sidebar.

The content of the Tool Shelf , the Header and the Properties Sidebar can vary. It depends of the type of the objects and the modes that you are in.

This chapter here is about the Header.

Header Tool - Mode Drop-down Box

The Mode drop-down box allows you to switch between the different modes.

Modes are object states that allows you to edit and manipulate objects at different levels with different tool sets and goals. The sculpt mode for example allows you to sculpt a mesh object. Edit Mode allows to manipulate the mesh of the object, and so on.

The available modes can differ from object to object. A armature for example has an additional pose mode. And when you work with the grease pencil, then the Edit Strokes mode becomes available.

## Object Mode
This mode allows to manipulate objects at Object level. Like move it around, rotate it, etc. This mode is available for all object types.
## Edit Mode
The edit mode allows to edit the object. With a mesh object this means that you are able to modify and to change the geometry. With an armature you build your skeleton. And with a text object you can type in text, and choose the font etc.
Not all objects has an edit mode.
## Sculpt Mode
Sculpt mode is a mesh object only mode. In this mode you can sculpt the mesh.
## Vertex Paint
Vertex Paint is a mesh object only mode. In this mode you can paint vertices with colors.
## Weight Paint
Weight Paint is a mesh object only mode. In this mode you can adjust weight painting for an armature for example. But Weight Painted mesh objects can also be used in conjunction with particles.
## Texture Paint
Weight Paint is a mesh object only mode. In this mode you can paint at the texture of a mesh directly. This mode requires to have a working UV mapping and a texture at the mesh object.
## Edit Strokes
Edit Strokes is a Grease Pencil only mode. It allows to manipulate the curves at a mesh level.
## Particle Edit
Particle edit is a Particle System mode only. When you apply a particle system to a mesh object then this mode becomes available. It allows you to manipulate the particle system at a mesh level. You can comb hair particles for example.

Header Tool - 3D Manipulator Widget

The 3D Manipulator widget tool allows you to enable and to disable a 3D Manipulator widget in the viewport. It is made of several sub elements.
This element exists in most modes. But in Sculpting mode for example the 3D Manipulator is not available.
### 3D Manipulator
This button activates or deactivates the widget. Have a look at the shortcut here.
### Transformation manipulator Translate, Rotate and Scale
Here you can activate or deactivate three different types of widgets. One for Translate, one for Rotate, one for Scale.
You can also activate more than one widget at a time. Hold down shift while clicking at one of the buttons adds to the selection.
When you use the translate and scale widget, then you can transform in two directions by holding down shift. For example when you use translate widget and pull at the blue handler for upwards in Z direction, then you don't pull upwards, but sidewards in X and Y direction. The green and red line indicates the movement freedom.

When you use the Translate widget and hold down Ctrl, then you move the object with a snapping of one unit.
#### Last Operator Translate, Rotate and Resize
For the last Operator Translate, Rotate and Resize please have a look in the chapter Navigation Menu. They are identical.
### Transform Orientation
Transform Orientation is a drop-down box where you can choose between different orientation methods for the transform operation. The widget points into this direction then.
#### View
The transform orientation aligns to the current view.
#### Gimbal
Aligns each axis to the Euler rotation axis as used for input.
#### Normal
This is of interest for bones for example. Aligns the transformation axis to average normal of the selected elements. Bone Y axis for Pose mode.
#### Local
Uses the local orientation of the selected elements.
#### Global
Uses the global orientation for the selected elements.
Header Tool - Proportional Editing

Proportional editing is a way to transform selected elements with some kind of a falloff. So when you for example pull a vertice upwards in Edit mode, the neighbour vertices will also pull upwards, but not so strong. The neighbours gets influenced proportional.
Proportional Editing is not available in all modes.

Proportional editing in Object mode is made of two elements. The on off switch. And a drop-down box where you can choose the falloff method.

In Edit Mode with a mesh object you just have the on off switch. But here you can choose between three different falloff modes.
Both settings can be found in the Last Operator panel, when you for example move or scale an object or selection.

## Changing the Proportional influence radius
You can change the influence radius for proportional editing with the mouse wheel or the Page up Page down arrows while keeping the mouse button pressed down for translate, rotate or scale. Or at the widget.
## Usage:
Create for example two cubes. Now move one of it around. Enable proportional editing. Choose your favourite falloff method if you want.
When you click at the widget you will see a white circle around the Pivot point. That's the influence radius for the proportional editing.
Now increase the radius for falloff. So that the second cube is in the influence radius. You will see it moving at one point.
In the last operator Translate there is also a Proportional Size edit box that shows you the size of the radius. Here you can adjust the value too. But note that it will not update the visible influence radius in the 3D view. And when you change the radius in the viewport with the scroll wheel, then it will use the old value, and not the value that you have typed in here. So you better adjust the radius in the viewport. And use this edit box as a visual feedback.

Header Tool - Transform Snapping

## Transform Snapping
This element is for snapping while transformation. Not to mix with the snapping tools in the Tools tab in the Tool Shelf. The Transform Snapping tool includes for example grid snapping.
Transform Snapping is not available in all modes.
The Transform Snapping tool is made of three elements.
### Transform Snapping
Here you enable or disable snapping.

### Snap Element
Snap Element is a drop-down box where you can choose between different snapping methods.
#### Volume
Snapping happens to the volume of another object.
#### Snapping
Snapping happens to the face of another object.
#### Edge
Snapping happens to the Edge of another object.
#### Vertex
Snapping happens to the Edge of another object.
#### Increment
Snapping happens relative to the ground grid.
### Absolute Grid alignment while translating
With this feature on the selection snaps to the grid points. Without this feature it snaps increasing by unit size. When you have a grid snapping of 1, and an element at 0.56, then without absolute grid alignment it will snap at 1.56, 2.56 etc. With absolute grid snapping it will snap at 0, 1, 2 etc.

Header Tool - Viewport Shading

The Viewport shading drop-down box contains the different shading modes for the viewport. It exists in all modes.

## Rendered
Displays the content in the viewport like you would have rendered it. This mode is dependant of what render engine you have currently active. And is available for Blender Render and Cycles.
## Material
Displays the content in the viewport with all material settings and with OpenGL rendering.
## Texture
Displays the content in the viewport textured. You need of course a working UV mapping and a texture at the mesh to see it.
## Solid
Displays the content in the viewport with a solid white color.
## Wireframe
Displays the content in the viewport as Wireframe.
## Bounding Box
Displays the content in the viewport as Bounding box. The mesh content is not displayed.

Header Tool - Pivot Point

The Pivot Point is the point around which the object manipulation happens. Rotation, mirroring, and so on. Normally this happens around the pivot of the active object. In this menu you can set the pivot point to other locations. Like the position of the 3D cursor.

It exists in all modes.

## Active Element
With this setting the manipulation happens relative to the center of the selected active elements. With more than one element is involved, then in Object mode this center gets calculated from the elements pivots. In edit mode the pivot is also the median point.

## Median Point
With this setting the manipulation happens relative to the median point of the selected elements. This can be another point than calculating the center of the pivots. The median gets calculated from the geometry, not from the pivot point of the geometry.

## Individual Origins
With this setting the manipulation happens relative to the origins of the selected elements. The origin is the little orange dot in every element.

## 3D Cursor
With this setting the manipulation happens relative to the 3D cursor.

## Bounding Box Center
With this setting the manipulation happens relative to the Bounding Box Center.

Header Tool - Manipulate Center Points

This option is of interest when you have more than one object selected. With this option enabled a transformation will change the positions of the object’s origins, but will not affect the object itself.
For example, when you want to scale a group of selected cubes. Without the option enabled the cubes will scale also down when you scale the selection. With this option enabled, the cubes will keep their size. But they will scale closer together. The Pivot points gets scaled.

Header Tool - Mesh Object - Edit Mode - Mesh Select Mode

The mesh select mode in Edit Mode with a Mesh object allows you to switch between the three available selection modes Vertice select, Edge Select and Face Select.

You can have more than one mode active by shift clicking at the other mesh select modes.

Header Tool - Mesh Object - Edit Mode - Limit Selection to Visible

Limit selection to visible limits the view to what you can see from the front. By default the back geometry shines a bit through.

Header Tool - Mesh Object - Face selection masking for Painting

Painting at a Mesh object has two header tools that just belongs to the painting operations. One of it is Face selection masking for Painting. It is visible in Vertex Paint Weight Paint and Texture Paint.

## Face selection masking for Painting
When you activate this tool then you reveal a Select menu in the header. And you can select the mesh parts that you want to manipulate.
Note that you may first want to deselect all. By default everything is selected ...

The select menu is explained in the chapter Vertex Painting - Select Menu.

Header Tool - Mesh Object - Vertex selection masking for Painting

Painting at a Mesh object has two header tools that just belongs to the painting operations. One of it is Face selection masking for Painting. It is visible in Vertex Paint and Weight Paint.
## Vertex selection masking for Painting
When you activate this tool then you reveal a Select menu in the header. And you can select the mesh parts that you want to manipulate.
This tool is meant for Weight Painting. And so the mesh displays the vertices too.
Note that you may first want to deselect all. By default everything is selected ...

The select menu is explained in the chapter Vertex Painting - Select Menu.

Header Tool - Particle Edit - Select modes

The Select modes allows you to change the display and the editability of the particle vertices.
## Path
No keypoints are visible. You can only select or deselect all keypoints at once.
## Point
You see all keypoints. And all keypoints are editable
## Tip
You can only see and edit the tip keypoints.

Header Tool - Reset 3D View

Reset 3D View is a navigation element. It resets the 3D view to a predefined setting.

It exists in all modes.

Reset 3D View is an add-on, and can be uninstalled when wanted. But note that the functionality is missing then.

Header Tool - Align View Buttons

The Align View buttons contains some quick navigation elements to navigate in the viewport. You can switch between the different views, switch between orthographic and perspectivic view, switch to camera view and back to viewport view, and set the active camera.
It exists in all modes.
Align View Buttons is an add-on, and can be uninstalled when wanted. But note that the functionality is missing then.

## Top, Bottom, etc.
Switches to Top view, Bottom View, etc.

## View Persp/Ortho
Toggles between perspectivic and orthographic view. Perspectivic view acts like a real camera with the perspectivic distortions. Orthographic view acts like a mathematical display of an object, without distortions.

## Align View to active Camera
Switches to Camera view and back to Viewport Camera.

## Set Active Camera
Sets the currently selected camera as the active camera. The active camera is the camera that gets used for rendering.
You need to have a camera object selected to activate the tool. Unlike the tool in the View menu, this tool here just works for camera objects.

Header - Options panels