7.0.18 Editors - 3D Viewport - Armature - Pose Mode - Pose context menu

Pose Mode - Pose Context Menu

Call this menu with double right click in the 3D viewport. You need to be in Edit mode with an armature object.

## Insert Key frame
Opens a menu where you can insert a key frame with a defined keying set.

## Copy Pose
Copies the current pose. You copy what you have selected.
## Paste Pose
Pastes a previous copied pose.
## Paste X Flipped Pose
Pastes a previous copied pose, but flipped along X axis.
### Last Operator Paste Pose
#### Flipped on X Axis
Paste the pose flipped along X Axis.
#### On Selected Only
Paste just on the selected bones. Not on the unselected.
## Rename active Bone
Calls a dialog where you can rename the active bone.

## Push Pose from Breakdown
Exaggerates the current pose. Pushes the current pose further away from the previous pose.
### Last Operator Push Pose
#### Percentage
The percentage of exaggeration.
#### Previous Key frame
The key frame position before the current frame.
#### Next Key frame
The key frame position after the current frame.
#### Channels
Limit the push effect to specific channels.

#### Axis Lock
Limit the push effect to specific axis.

## Relax Pose to Breakdown
Relaxes the current pose.
### Last Operator Relax Pose to Breakdown
#### Percentage
The percentage of relaxing.
#### Previous Key frame
The key frame position before the current frame.
#### Next Key frame
The key frame position after the current frame.
#### Channels
Limit the relax effect to specific channels.

#### Axis Lock
Limit the relax effect to specific axis.

#### Pose Breakdowner
Creates a suitable breakdowner pose on the current frame.
When you perform the tool then you will see a per cent slider in the header where you can read the percentual influence of the blending. Move the mouse to position the blend pose where you need it.
##### Last Operator Pose Breakdowner
###### Percentage
The percentage of exaggeration.
###### Previous Key frame
The key frame position before the current frame.
###### Next Key frame
The key frame position after the current frame.
#### Channels
Limit the breakdowner pose to specific channels.

#### Axis Lock
Limit the breakdowner pose to specific axis.

## Blend to Neighbout
Blends the current pose with the neighbouring poses.
When you perform the tool then you will see a per cent slider in the header where you can read the percentual influence of the blending. Move the mouse to position the blend pose where you need it.
### Last Operator Blend to Neighbour

#### Factor
The blend factor.
#### Previous Keyframe
The keyframe to calculate from before the current position.
#### Next Keyframe
The keyframe to calculate from after the current position.
#### Channels

#### Axis Lock
Lock the transformation along an axis.

## Calculate Motion Paths
Objects can be animated. Let's say you send them from a to b to c. The object will move to b, then to c. Some kind of a path. This path is not visible by default.
With motion paths you can calculate this path, and make it visible.

#### Last Operator Calculate Object Path
##### Start
Defines the start frame of the calculation.
##### End
Defines the end frame of the calculation.
##### Bake Location
Where to draw the curve. At the head or at the tail of the bone(s)

## Clear Motion Paths
Clear remove the motion path from the object.

## Update Armature Motion Paths
Updates the motion paths for the armature object.
## Update All Motion Paths
Updates the motion paths for all objects.

## Hide Selected
Hides the selected geometry.

## Show Hidden
Makes all hidden geometry visible again.

### Clear User Transforms
Resets Pose of selected bones back to key frame state.