26.3 Editors - Properties Editor - Output Properties Tab

Detailed table of content

Output Properties Tab

The Output properties contains all the settings to render the final image or movie. Most o fthe settings are the same for all three available render engines.

## Render Engine
Shows the active render engine. Specific renderer does have other settings. And you can also switch to another renderer. But note that this is more a visual guide. It misses the Cycles render settings.

Dimensions Panel

This panel contains the dimension settings.

## Presets
A list of dimension presets with the most common settings.
To add a new preset type in a new preset name into the edit box at the end of the list, and click at the + sign.
To remove a preset click at the - sign behind the name.

## Resolution X / Y
The dimensions of the image in pixels.
%
Render the image in per cent of the original image. You can for example render in 200% of the resolution values. Or in 50%.
## Aspect X / Y
The image aspect ratio. For anamorphic or non square pixel output.
## Render Region
Activate render region for the output image.
There is a render region feature in the 3D view and in the Image editor where you can render a portion of the screen for preview purposes. Normally the output will always render the full image then, regardless of the render region. When you activate Render Region then the output will also render the render region only, and not the full image.
### Crop to Render Region
Crop the output image to the size of the render region.
## Frame Rate
The output frame rate. When you choose custom then two more properties appears.

Frame Range Panel

## Frame Start / End
The start and end frame for an animation.
## Frame Step
Number of frames to skip forward while playing the animation. With a value of 2 every second frame gets skipped.
### FPS
The custom frame per seconds value.
### Base
Frame rate base. A multiplier that makes it for example possible to set up 29,97 Frames instead of 30 for NTSC.
## Time Stretching
Remap the length of an animation.
### Old
The old length.
### New
The new length.
Stereoscopy Panel

Allows you to render out stereoscopic images from the active camera. For the anaglyph images you need special stereoscopy glasses to see the 3D effect. And in case of the interlace method a 3d ready monitor and shutter glasses.

The anaglyph method is to create stereo images. The interlace method is mostly used in movies.

## Workflow
Turn on Stereoscopy.

Select the Camera in the Outliner. In the Properties Editor choose the Object Data Properties tab (which should show a camera icon at this point), and open the Stereoscopy panel.
Change the Convergence Plane Distance to your needs. This can also be done in the 3D view with the handlers when you are in Camera view.
Interocular distance is the distance between the left and the right camera.

Outside of the camera view you will see this plane in front of the camera.
Adjust the plane to your needs. The plane is the reference point. Everything behind appears behind the focus. Everything before the plane appears before the focus.

In the sidebar in the 3D view you will find further settings.
Turn on volume to see if the objects are inside of the volume.

Do a preview rendering, and adjust the settings if required.
Go back to the Output tab to the Output panel. By activating stereoscopy here is a new section called Views. Here you can find further export settings.

## Stereo 3D / Multiview
The stereoscopy method. Stereo 3D uses two predefined virtual cameras. The camera settings gets inherited from the main camera.
Multiview allows you to set up several cameras manually. You need to create every camera by hand. And you need to follow name conventions to get this to work. In the outliner give the cameras the suffix that you want to use in the list. Here three cameras with a suffix.

Now do the same in the list of cameras. Give every camera the same suffix than in the outliner. The camera name is not important. Important is the suffix. This is the identifier.

And in the render window you have now the render result of your three cameras.
Note that for stereoscopy just two cameras gets used for rendering the anaglyph or interlaced result. Usually the ones with suffix _L and _R. So our third camera does not influence the stereoscopic image here.

## List of Cameras
The list of cameras. Note that with method Stereo 3D these cameras does not exist in the outliner. They are virtually created as child objects to the main camera that you use for rendering.
In this list you can choose the cameras to change the suffix.
The checkbox allows you to disable the cameras. Both options are just of interest for the multi-view setup. Normal stereoscopy setup does not require any further setup.
### Resize handler
The resize handler allows you to resize the list.
### Search field
The triangle button down left allows you to open a search field.

## Add / Remove / Rename
Add adds a custom camera. Remove removes a custom camera. And custom cameras can be renamed by clicking at the name.
The camera names left and right can‘ t be renamed, and you can‘ t remove them from the list. Individual cameras can be renamed and removed.
## Suffix
The camera identifier. The suffix gets appended at the end of the single images of the camera. The left camera has the suffix _L, and the right camera has the suffix _R

## Output Views Subpanel
This subpanel just shows with Stereoscopy enabled!
Adjust the stereoscopy export settings. Note that this settings does not adjust what you view in the image editor. This settings influences what you save from the image editor then.
### Individual
Save out single images from each camera when you save the result from the image editor. So for a stereoscopic image two images for the two cameras.
### Stereo 3D
Save out the stereoscopic image as a single image when you save the result from the image editor.
#### Stereo Mode
How to export the stereoscopic image with save as in the image editor. There are four methods available.
### Stereo Mode Type Anaglyph
Render Views for left and right eyes as two differently filtered colors in a single image. You need anaglyph glasses to see the 3d effect.

#### Anaglyph Type
The color model to display the graphics.

### Stereo Mode Type Interlace
Render Views from left and right eyes interlaced into a single image. You need a 3D Ready monitor to see the stereo effect.

#### Interlace Type
The interlace type that you can choose.
#### Swap Left/Right
Swaps left and right camera view.
### Stereo Mode Type Side by Side
Renders images of the two cameras side by side.
#### Cross Eyed
Swaps left and right camera view.
#### Squeezed Frame
Combine both views in a squeezed image.

### Stereo Mode Type Top Bottom
Renders images of the two cameras side by side.
#### Squeezed Frame
Combine both views in a squeezed image.

Output Panel

The file output settings.
## File Path
The location to save rendered frames. Here you will find rendered animation sequences. For single images you can save out the result in the image editor.
When rendering an animation, the frame number is appended at the end of the file name with four padded zeros (e.g. image0001.png). You can set a custom padding size by adding the appropriate number of # anywhere in the file name (e.g. image_##_test.png translates to image_01_test.png).
This setting expands relative paths where a // prefix represents the directory of the current blend-file.
## Load File
Here you can load an existing file to overwrite it. Or you can use it to load a file in a directory and rename it then to your destination file name.
## File Format
The output file format.
Each file format has some own settings.

### Image file formats
#### BMP
##### Color
The output color format. Black and white or rgb.
#### Iris
##### Color
The output color format. Black and white, rgb or rgba.
#### PNG
##### Color
The output color format. Black and white, rgb or rgba.
##### Color Depth
8 or 16 colors per channel.
##### Compression
The compression level.
#### JPEG
##### Color
The output color format. Black and white, or rgb.
##### Quality
The jpeg quality.
#### JPEG 2000
##### Color
The output color format. Black and white, rgb or rgba.
##### Color Depth
8, 12 or 16 colors per channel.
##### Quality
The jpeg quality.
##### Codec
Which jpeg 2000 codec to use.
##### Cinema
Use OpenJpeg Cinema preset.
##### Cinema (48)
Use OpenJpeg Cinema (48) preset.
##### YCC
Save luminance / chrominance / chrominance channels instead of rgb channels.
#### Targa
##### Color
The output color format. Black and white, rgb or rgba.
#### Targa Raw
##### Color
The output color format. Black and white or rgb.
#### Cineon
##### Color
The output color format. Black and white, or rgb.
Gamma of 1.7 and Non-Linear is hard coded.
#### DPX
##### Color
The output color format. Black and white, rgb, or RGBA.
##### Color Depth
8, 10, 12 or 16 colors per channel.
##### Log
Convert to logarithmic color space.
#### Open EXR Multilayer
##### Color Depth
Float half values or Float full values per channel.
##### Codec
What codec to use.

##### Preview
When rendering animations, save Jpeg preview images into the same directory.
#### Open EXR
##### Color
The output color format. Black and white, rgb, or RGBA.
##### Color Depth
Float half values or Float full values per channel.
##### Codec
What codec to use.

##### Preview
When rendering animations, save Jpeg preview images into the same directory.
#### Radiance HDR
##### Color
The output color format. Black and white, or rgb.
#### TIFF
##### Color
The output color format. Black and white, rgb, or RGBA.
##### Color Depth
8 or 16 bit per channel.
##### Compression
The compression method.

#### WebP
##### Color
The output color format. Black and white, rgb, or RGBA.
#### FFmpeg video
##### Color
The output color format. Black and white, or rgb.
##### Video
Video Codec
Color Depth
Output Quality
Encoding Speed

## Transparent
Eevee, Eevee (Legacy), and Workbench renderer. Render and export the result with transparent background.

## Encoding subpanel
Only available with Ffmpeg video format. These options are unavailable for other file formats.
### Container
Video container or file type, including MPEG-4, Matroska, etc
### Autosplit Output
Autosplit the exported video file at 2GB boundaries.
Note: Useful for longer videos renders
### Video
#### Presets (Header)
These are presets for different groups of settings.
#### Video Codec
Chooses the method of compression and encoding.

#### Color Depth
Select between 8 and 10 or 12 bit color depths. The Color Depth property in the Encoding block allows to select higher color depths for video output when using suitable codecs in ffmpeg.
For H.264, H.265, and AV1, a 10-bit option is available. Additionally, for H.265 and AV1, a 12-bit option can be chosen.
Note: When 'lossless' encoding is selected, the color format switches from YUV 4:2:0 to YUV 4:4:4, supporting 10-bit or 12-bit variants.
#### Output Quality
1. Constant Bitrate (CBR): This setting maintains a steady bitrate throughout the video, ensuring consistent quality but potentially leading to larger file sizes. Ideal for streaming and situations where bandwidth is limited.
2. Lossless: Ensures no data is lost during compression, preserving the original video quality perfectly. This results in larger file sizes but is excellent for archival or high-quality needs.
3. Perceptually Lossless: Uses advanced algorithms to compress the video in a way that is visually indistinguishable from the original, while reducing file size significantly.
##### Compression Levels:
- High: Produces high-quality video with minimal compression, resulting in larger files.
- Medium: Balances quality and file size, suitable for most uses.
- Low: More compression applied, reducing file size but still maintaining decent quality.
- Very Low: High compression, significantly reducing file size but with noticeable quality loss.
- Lowest: Maximum compression, smallest file size with the most quality reduction.

#### Encoding Speed
Presets to change between a fast encode (bigger file size) and more compression (smaller file size).
#### Keyframe Interval
The number of frames in each Group of Pictures (GOP). Set this to 0 for 'intra_only', which means each frame is independent (no inter-frame compression). A higher GOP number typically results in a smaller file size, but it requires a more powerful device to play back smoothly.
#### Max B-frames
Enables the use of B-frames (bi-directional frames), which are used in video compression to improve efficiency and quality. B-frames can reference both previous and subsequent frames to store motion data more effectively. This generally results in better video quality at a smaller file size, but it may require more processing power to encode and decode the video.
##### Interval
The 'Interval (of B-frames)' setting determines the maximum number of B-frames (bi-directional frames) that can appear between non-B-frames (I-frames and P-frames) in a video. B-frames help compress video by referencing both previous and future frames, improving overall compression efficiency and quality. Adjusting this interval affects the video's file size and playback performance.
#### Constant Bitrate Settings
#### Bitrate
Sets the average quality of the video by determining the number of bits per frame.
#### Minimum / Maximum
Controls the variable bit rate (VBR). This allows certain parts of the video to use more data for better quality and less for simpler parts, managed by setting the minimum and maximum values.
#### Buffer
The size of the decoder's data buffer.
#### Mux Rate
The maximum bit rate of the combined video and audio stream. Multiplexing merges separate video and audio streams into a single file, like zipping a video and an audio file together.
##### Mux Packet Size
Reduces data fragmentation or overhead depending on the source.

### Audio
These settings control how sound is exported when rendering.
#### Audio Codec
Choose the format for audio output. For a complete list, refer to video formats. You can also export with No Audio.
#### Audio Channels
The number of audio outputs:
##### Mono:
One audio channel.
##### Stereo:
Two audio channels (left and right).
##### 4 Channels:
Four audio channels.
##### 5.1 Surround:
Six audio channels, including one low-frequency effect (LFE) channel.
##### 7.1 Surround:
Eight audio channels, including one LFE channel.
#### Sample Rate
Sets how frequently the audio is sampled, affecting quality.
#### Bitrate
Controls the sound quality. Higher bit rates give better sound but result in larger files.
#### Volume
Adjusts the audio output volume.

## Options subpanel
Not all options are available for all file formats.
### Saving
#### File Extensions
Adds the correct file extensions per file type to the output files.
#### Cache Result
Saves the rendered image and passes to a Multilayer EXR-file in temporary location on your hard drive. This allows the compositor to read these to improve performance, especially for heavy compositing.
### Image Sequence
#### Overwrite
Overwrite existing files when rendering.
#### Placeholders
Create empty placeholder frames while rendering.

## Color management subpanel

### Color management settings
#### Follow scene
Uses the color management from the scene.
#### Override
Uses the color management settings that is defined below instead of the color management from the scene.
This settings is in most parts equal to the color management settings in the render properties. But has no settings for the Sequencer.
### Display Device
The device that the image is being viewed on. Your monitor.
Most computer monitors are configured for the sRGB color space.
Color management can also be disabled by setting the device to None.

### View Transform
Choose between different ways to view the image on the same monitor.
#### Standard
Does no extra conversion besides the conversion for the display device.
#### Filmic
For more photo realistic results and better handling of high dynamic range. The contrast can be adjusted by changing the Look option for the Filmic view transform.
#### Filmic Log
Converts to Filmic log color space. This can be used for export to color grading applications, or to inspect the image by flattening out very dark and light areas.
#### Raw
Intended for inspecting the image but not for final export. Raw gives the image without any color space conversion.
#### False Color
Shows a heat map of image intensities, to visualize the dynamic range.

### Look
Adjust the contrast.
### Exposure
Used to control the image brightness (in stops) applied before color space conversion. The calculation is: output_value=render_value×2(exposure)
### Gamma
Extra gamma correction applied after color space conversion. Note that the default sRGB or Rec709 color space conversions already include a gamma correction of approximately 2.2 (except the Raw and Log views), so this would be applied in addition to that.
### Use Curves
Adjust RGB Curves to control image colors before color space conversion.

#### Navigation elements
The navigation elements at the top are described from left to right.
##### Zoom in and out
The two buttons with the magnifying glass at it zooms in and out in the curve window.

##### Tools
Tools is a menu that contains some cuve related tools.
###### Reset View
Resets the curve windows zoom.
###### Vector Handle
Set handle type to Vector.
###### Auto Handle
Set handle type to Auto.
###### Auto Clamped Handle
Set handle type to Auto Clamped.
###### Extend Horizontal
Causes the curve to stay horizontal before the first point and after the last point.
###### Extend Extrapolated
Causes the curve to extrapolate before the first point and after the last point, based on the shape of the curve.
###### Reset Curve
Resets the curve to the initial shape.

##### Use Clipping
Clipping options. Set up clipping for the stroke.
##### Delete Points
Deletes selected curve points.

#### Black Level
The color that Black is mapped to.
#### White Level
The color that White is mapped to.
##### Hotkeys for Black and White Level
You may want to sample the black and white level colors directly in the image by clicking at an area. There are hotkeys for that.
Ctrl + Left Mouse click in the image sets the Black level value from that position.
Shift + Left Mouse click in the image sets the White Level value from that position.
To see the result you need to tick the View as Render button.

#### Reset
Resets the Curve and the Black and White Level values to the default values.

## Transparent subpanel
Cycles only. Enable the rendering of transparent background.
### Transparent Glass
Render glass with transparent background.
### Roughness Threshold
For transparent transmission. Keep surfaces with roughness above the threshold opaque.

Metadata Panel

What metadata to include into the image or movie.

## Metadata Input
Where to get the Metadata from.
## Include
What Metadata to include.
## Note
Include a custom comment.
## Burn into Image
Render the stamp info text into the image. The information is cluttered across the rendered image. Parts of it appears up left in the rendering. Parts down left, and parts down right.

The props have decorators. This means this information can be keyframed. The font itself is the system font, and cannot be changed.
### Font Size
The font size.
### Text Color
The text color.
### Background
The background color of the text.
### Include Labels
Display stamp labels like "Camera" in front of camera name, etc.

Post Processing Panel

Enable Post Processing.

## Pipeline
### Compositing
Process the pipeline through the compositing in case compositing nodes are enabled.
### Sequencer
Process the pipeline (and composited result) through the video sequence pipeline in case Sequencer strips exists.
## Dither
Amount of dithering noise added to the rendered image to break up banding.
This prop has a decorator, and can be keyframe animated.