Detailed Table of content

Edit Mode - Curve Menu

The curve menu just exists for curve objects.

Transform

## To Sphere
Shapes a selection of objects into the shape of a sphere. The calculation happens with the object origins.
In Object mode this tools requires to have more than one object selected.
### Usage
Select the vertices, activate the tool, then drag the mouse in the 3D viewport. In the header you will read the current factor then. Which tells you how close you are towards the sphere shape. This also works with curves in the same way.

### Last Operator Add Ico Sphere Panel
#### Factor
The factor to transform the selection into a shape form.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
#### Proportional Falloff
Here you can adjust the falloff methods.
#### Proportional Size
Here you can see and adjust the falloff radius.

#### Connected
The proportional falloff gets calculated for connected parts only.
#### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Shear
Shear shears the selection.
### Last Operator Shear
#### Offset
Here you can adjust an offset.
#### Shear Axis
The shear tool works along a imaginary 2d plane. The shear axis controls if the itemas are sheared along the x or the y axes of this plane. This is the plane along which the transformation happens. You can shear along the x or the y axis of this plane.
To make things even more complicated, the orientation of this imaginary plane is defined by the Axis and Axis Ortho items below.
#### Axis
Defines one axis of the imaginary shear axis plane.
#### Axis Ortho
Defines the other axis of the imaginary shear axis plane.
#### Orientation
Here you can choose the orientation for the shear action.

#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Bend
Bends the selection.

## Push/Pull
It pushes or pulls the object positions relative to the center of the selection.
In Object mode this tool requires to have more than one object selected.
### Last Operator Push/Pull
#### Factor
Here you can adjust the strength of influence of the tool.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Warp
Warps a mesh selection between two defined points. This also works with curves.
### Last operator Warp
#### Warp Angle
The strength of the warp effect.
#### Offset Angle
A offset angle to bend sidewards.
#### Min
The start point.
#### Max
The end point.

## Randomize Transform
This tool allows randomizes the positions of the selected vertices.
### Last Operator Randomize Transform
#### Amount
Here you can adjust the amount.
#### Uniform
The uniform offset distance.
#### Normal
Align the offset direction to the normals.
#### Random Seed
The seed value for randomization.

## Skin Resize
This tool is for mesh objects. And has no functionality with a curve object.

## Shrink/Fatten
Shrink/Fatten scales the selected geometry along its normals. Transform orientation and Pivot point gets ignored.
A positive value pushes the vertices outwards. A negative value pushes the vertices inwards.
### Last Operator Shrink/Fatten
The Last Operator Shrink/Fatten panel gives you tools to adjust the Shrink/Fatten operation. Here you have numeric input for the strength and a few more options.
#### Offset
Offset is the strength of the offset for Shrink/Fatten.
#### Offset Even
Offset Even scales the selection to give more thickness in even areas.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Move Texture Space
Move Texture space is meant for mesh objects, but has also functionality with a curve object.
This tool relies at the move tool. With the difference that it moves the texture space instead of the object. It has also a very special use case, and just works with a material with a Texture Coordinate / Generated node. And requires to have the shading at Material or Rendered to see a result in the viewport.
In the viewport you will see the UV cage in black color. In the header you will see the values for the current position of the UV cage.
Note that once done and applied, there is no way to reset the UV cage back to zero. When you repeat the operation, then the values will start at 0 again. Even when the UV cage is already offset.

### Last Operator Translate
#### Move X, Y Z
Here you can limit the position relative to the source object.

#### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the mirroring action.

#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Scale Texture Space
Scale Texture space is meant for mesh objects, but has also functionality with a curve object.
This tool relies at the scale tool. With the difference that it scales the texture space instead of the object. It has also a very special use case, and just works with a material with a Texture Coordinate / Generated node. And requires to have the shading at Material or Rendered to see a result in the viewport.
In the viewport you will see the UV cage in black color. In the header you will see the values for the current position of the UV cage.
Note that once done and applied, there is no way to reset the UV cage back to zero. When you repeat the operation, then the values will start at 0 again. Even when the UV cage is already offset.

### Last Operator Resize Texture
##### Move X, Y Z
Here you can limit the position relative to the source object.

#### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the mirroring action.

#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Set Dimensions
Edit Mode Only!
Normally all scale operations in Bforartists are relative to the current selection and dimensions. And you always start with a relative value of 1.
Set dimensions allows to scale mesh selections in absolute world values. No matter how the initial values are. The new values gets set in the Last Operator.
Set dimensions is an add-on. You can turn it off in the add-ons section of the user preferences when you want.
### Last Operator Set Dimensions
##### New Dimensions
When you activate the tool then you will see the world coordinates of the selection. Here you can change the values to other world coordinates.

Mirror

Mirror mirrors the selected geometry along the defined axis.
## Interactive Mirror
Mirror by hotkeys. You activate the tool, type in x for x global for example, or x x for x local. And the selection gets mirrored
## X Global, Y Global etc.
Mirrors the selection around the chosen axis.
### Last Operator Mirror
The Last Operator Mirror panel gives you tools to adjust the mirror action.

#### Orientation
Orientation is a drop-down box where you can choose the type of orientation for the mirroring action.
#### Constraint Axis
Constraint Axis gives you again the possibility to define the mirror axis. You can choose more than one axis here.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

Snap

Here you can choose several methods to snap one element to another. The menu items should be self explaining.
## Last Operator Snap
Some snap operations shows a last operation panel, some not.
### Offset
If the selection should snap as a whole, or if each individual element of the selection should snap.

Operators

## Duplicate
Duplicates the current selection. This can be a single control point or a whole curve.
The copy sticks to the mouse until you release it. A Right click while moving will reset the position of the duplicate. The duplicated part will be part of the same object.
When you drag the duplicate around you will see the position values in the header.
### Last Operator Duplicate
#### Move X , Y , Z

#### Orientation
Here you can choose the orientation.

#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Split
Splits the curve at the selected control point(s). You need to select two control points to select the segment between it.

## Separate
Separates the selected control points, and creates a new curve object out of it. You need to select two control points to select the segment between it.

## Toggle Cyclic
Toggle Cyclic closes or opens the curve.
### Last Operator Toggle Cyclic
#### Direction
Direction is a drop-down box where you can choose the direction in which the curve gets closed.

## Decimate Curve
Decimates the currently selected geometry. It starts with a Ratio of 1. Which means no decimation. The lower the ratio the more decimation you will get.
### Last Operator Decimate Curve
#### Ratio
Here you can adjust the strength of decimation.

## Set Spline Type
With set Spline Type you can set the type of the curve.
Poly is a straight line between the control points. Bezier has curve handlers. A nurbs curve has a control cage.

### Last Operator Set Spline Type
#### Type
Type is a drop-down box where you can choose the spline type
#### Handles
Use Handles when converting Bezier curves into polygons.

## Tilt
Modifies the Mean Tilt.
Activate the tool, and drag the mouse. You will see a value in the header now. The selected curve path will rotate by dragging the mouse.
The Tilt angle always starts at zero. It is relative. To modify the Mean Tilt use the edit box in the Transform panel.
### Last Operator Tilt
#### Angle
The Tilt angle.
#### Proportional editing
Enables proportional editing. Activating proportional editing reveals further settings.
##### Proportional Falloff
Here you can adjust the falloff methods.
##### Proportional Size
Here you can see and adjust the falloff radius.

##### Connected
The proportional falloff gets calculated for connected parts only.
##### Projected(2D)
The proportional falloff gets calculated in the screen space. Depth doesn't play a role. When it's in the radius, then it gets calculated.

## Clear Tilt
Sets the Mean Tilt to zero.

## Set Handle Type
Handles defines the type of handle for the knots of the curve. You have the choice between Auto, Vector, Align and Free. And the Last Operator gives you a fifth possibility to toggle between Free and Align.
### Auto
Auto aligns the handles automatically.
### Vector
Set Handle type to Vector.
### Align
Set Handle type to Align.
### Free
Set Handle type to Free.
### Toggle Free/Aligned
Toggle Free/Aligned.
#### Last Operator Set Handle Type
##### Type
Type is a drop-down box where you can set the handle type. You have the choice between Auto, Vector, Align, Free. And the fifth possibility toggles between Free and Align.

## Recalc Normals
Recalculates the normals of the selected curve.
### Last Operator Recalc Normals
#### Length
Recalculates the handle length too.

## Show / Hide
### Show Hidden
Makes all curve geometry in the scene visible again.
### Hide Selected
Hides the selected curve geometry.
#### Last Operator Hide Selected
##### Unselected
Hides the not selected curve geometry.
### Hide Unselected
Hides the not selected curve geometry. The selected geometry stays visible.

## Delete
### Vertices
Dissolves the selected vertices. When removing vertices in between then the curve stays intact and connected.
### Segment
Removes the segment between the selected vertices.

## Dissolve Vertices
Dissolves the selected vertices. When removing vertices in between then the curve stays intact and connected.